## Slide 1
CMSC 417: Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
Spring 2026
Topic: Internetworking
(Textbook chapter 3)
Feb 25th, 2026

## Slide 2: Classful IP addressing

## Slide 3
Picture courtesy: https://www.geeksforgeeks.org/introduction-of-classful-ip-addressing/
How can you tell network class from the IP address?

## Slide 4
Picture courtesy: https://www.ictshore.com/free-ccna-course/network-layer-ipv4-addressing/attachment/1013-05-classful_addressing/
What percentage of addresses and allocated to each class?

## Slide 5: Global Addresses
Properties
  globally unique
  hierarchical: network + host
  4 Billion IP address, half are A type, ¼ is B type, and 1/8 is C type
Format
Dot notation
  10.3.2.4
  128.96.33.81
  192.12.69.77

## Slide 6
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Let’s assume we have 4-bit address (instead of 32 bit)
Class A (Half of all possible addresses)
Class B (1/4 of all possible addresses)
Class C (1/8 of all possible addresses)

## Slide 7
0000
0001
0010
0011
0100
0101
0110
0111
Let’s assume we have 4-bit address (instead of 32 bit)
Class A (Half of all possible addresses)
Say, 1 bit for network part = 2 different networks
Say, 2 bits for host part = 4 hosts per network

## Slide 8: Global Addresses
Properties
  globally unique
  hierarchical: network + host
  4 Billion IP address, half are A type, ¼ is B type, and 1/8 is C type
Format
Dot notation
  10.3.2.4
  128.96.33.81
  192.12.69.77

## Slide 9
The “/X” notation
128.8.12.34/X means
the first X bits are the “Network part” or “Network prefix”

## Slide 10: Classful Addressing
In the olden days, only fixed allocation sizes
  Class A: 0*
    Very large /8 blocks (e.g., MIT has 18.0.0.0/8)
    There can be 126 different class A networks (0 and 127 values are reserved) and (224-2) different hosts (2 values are reserved)
  Class B: 10*
    Large /16 blocks (e.g,. Princeton has 128.112.0.0/16)
  Class C: 110*
    Small /24 blocks (e.g., AT&T Labs has 192.20.225.0/24)
    221 different networks possible, 254 hosts (255 is reserved for broadcast and 0 is reserved)
  Class D: 1110* for multicast groups
  Class E: 11110* reserved for future use
This is why folks use dotted-quad notation!

## Slide 11: IP Datagram Forwarding
Strategy
  every datagram contains destination's address
  if directly connected to destination network, then forward to host
  if not directly connected to destination network, then forward to some router
  forwarding table maps network number into next hop
  each host has a default router
  each router maintains a forwarding table
Example (router R2)

## Slide 12: IP Datagram Forwarding
R1
R2
R3
I-0
I-1
Forwarding table at R2

## Slide 13: IP Datagram Forwarding
R1
R2
R3
I-0
I-1
Forwarding table at R2
IP data packet (datagram)

## Slide 14: IP Datagram Forwarding
Algorithm
if (NetworkNum of destination = NetworkNum of one of my interfaces) then
deliver packet to destination over that interface
else
if (NetworkNum of destination is in my forwarding table) then
deliver packet to NextHop router
else
deliver packet to default router
First: find the NetworkNum. How?
R1
R2
R3
I-0
I-1
Forwarding table at R2

## Slide 15: Obtaining a Block of Addresses
Internet Corporation for Assigned Names and Numbers (ICANN)
  Allocates large blocks to Regional Internet Registries
Regional Internet Registries (RIRs)
  E.g., ARIN (American Registry for Internet Numbers)
  Allocates to ISPs and large institutions
Internet Service Providers (ISPs)
  Allocate address blocks to their customers
  Who may, in turn, allocate to their customers…

## Slide 16
Obtaining a Block of Addresses
Your organization: XYZ
Maximum # of hosts is estimated to be 10 millions.
What class of IP address will you request for?
Maximum # of hosts is estimated to be 64K ?
Maximum # of hosts is estimated to be 250?
Maximum # of hosts is estimated to be 100?
Maximum # of hosts is estimated to be 20?
Maximum # of hosts is estimated to be 300?
Maximum # of hosts is estimated to be 66K?
2^24 ~= 16 million
2^16 ~= 65K
2^8 = 256
Notes: Class A can have 16 millions (16777214 = 2^24-2)
Class B can have 65K (65534 = 2^16 - 2)
Class C can have 254 (2^8-2)

## Slide 17
Problems with the classes of addresses
Wastage of addresses
Bigger tables to look up at routers

## Slide 18: Subnetting: Splitting the network-prefix for smaller sub-networks

## Slide 19
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
ISP
The ISP provided the network address space: 223.1.1.X/24

## Slide 20
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
ISP
The ISP provided the network address space: 223.1.1.X/24
223.1.2.X
223.1.3.X

## Slide 21
Router
The ISP provided the network address space: 223.1.1.X/24
Two separate networks are needed. How can we assign addresses to these “sub” networks?

## Slide 22
Router
The ISP provided the network address space: 223.1.1.X/24

## Slide 23
Router
The ISP provided the network address space: 223.1.1.X/24
Use subnetting

## Slide 24
Router
The ISP provided the network address space: 223.1.1.X/24
11011111.00000001.00000001.XXXXXXX
Use part of the host bits to identify separate subnets.

## Slide 25
Router
The ISP provided the network address space: 223.1.1.X/24
11011111.00000001.00000001.XXXXXXX
Use part of the host bits to identify separate subnets.
11011111.00000001.00000001.0XXXXXX
11011111.00000001.00000001.1XXXXXX
How will the router know the “subnet prefix” for a packet?

## Slide 26
Router
The ISP provided the network address space: 223.1.1.X/24
11011111.00000001.00000001.XXXXXXX
Use part of the host bits to identify separate subnets.
11011111.00000001.00000001.0XXXXXX
11011111.00000001.00000001.1XXXXXX
Subnet mask = 11111111. 11111111. 11111111.10000000

## Slide 27: Subnetting
Add another level to address/routing hierarchy: subnet
Subnet masks define variable partition of host part of class A and B addresses
Subnets visible only within site
“Bitwise and”

## Slide 28: Subnetting
Forwarding Table at Router R1

## Slide 29: Subnetting
Forwarding Table at Router R1
Forwarding Algorithm
D = destination IP address
for each entry < SubnetNum, SubnetMask, NextHop>
  D1 = SubnetMask & D
  if D1 = SubnetNum
    if NextHop is an interface
    deliver datagram directly to destination
    else
    deliver datagram to NextHop (a router)

## Slide 30: Subnetting
Notes
Would use a default router if nothing matches
Not necessary for all ones in subnet mask to be contiguous
Can put multiple subnets on one physical network
Subnets not visible from the rest of the Internet

## Slide 31
Subnets “toy” example

## Slide 32
Address space assigned to you:

## Slide 33
30 hosts max.
22 hosts max.
18 hosts max.

## Slide 36
Classful address is dead.
Long live subnetting & prefix.
Notes: Classful addressing is operationally dead
No routing protocol in active Internet use assumes class boundaries.
BGP is fully classless.
OSPF and RIP v2 carry explicit prefix lengths.
CIDR (RFC 4632) removed fixed /8, /16, /24 semantics.
Subnetting did not die — it evolved
Under CIDR, all addressing is subnetting.
Prefix allocation is hierarchical subdivision.
Route aggregation is simply reverse-subnetting (supernetting).

## Slide 37: Class-less Interdomain Routing (CIDR)
Generalizes the ideas of subnetting
Notes: OSPF includes the subnet mask in LSAs.
BGP advertises NLRI as prefix/length.
RIP v2 carries subnet mask fields (v1 did not).

## Slide 38
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0

## Slide 39
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
223.1.1.128
223.1.1.192
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0

## Slide 40
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
223.1.1.128
223.1.1.192
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Lesson 1:
Address classes are not needed. Mask can define the number of bits for the network part.
Lesson 2:
Network hierarchies can be hidden from the outside world.
Network addresses can be aggregated/summarized/combined

## Slide 41: CIDR: Classless address

## Slide 42
CIDR: Classless InterDomain Routing
  Network portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
200.23.16.0–200.23.17.255
IP addressing: CIDR
This X bit network part is often called Prefix or Network-prefix

## Slide 43
IP addressing: CIDR
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
forwarding table
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address

## Slide 44: CIDR: Super-netting/ Route aggregation

## Slide 45
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.0.0/16

## Slide 46
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Forwarding tab.
223.1.0.0/16
223.1.0.0/16

## Slide 47
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24

## Slide 48
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24

## Slide 49
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24
Route aggregation

## Slide 50
Route aggregation with CIDR

## Slide 51: Classless Inter-Domain Routing (CIDR)
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network.
Network number = IP address + Mask
Written as 12.4.0.0/15

## Slide 52: Hierarchical Address Allocation
Hierarchy is key to scalability
  Address allocated in contiguous chunks (prefixes)
  Today, the Internet has about 1,132,452 prefixes
12.0.0.0/8
12.0.0.0/16
12.254.0.0/16
12.1.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
:
12.3.0.0/24
12.3.1.0/24
:
:
12.3.254.0/24
12.253.0.0/19
12.253.32.0/19
12.253.160.0/19
:
:
:
:
:
  (March 4, 2025. Source: https://ipv4.bgp.he.net/report/netstats)

## Slide 53: Separate Forwarding Entry Per Prefix
Prefix-based forwarding
  Map the destination address to matching prefix
  Forward to the outgoing interface
host
host
host
LAN 1
...
host
host
host
LAN
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 54
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1

## Slide 55
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing

## Slide 56
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing
Forwarding tab.

## Slide 57
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing
Forwarding tab.
201.10.0.0/21
201.10.6.0/23

## Slide 58
11001001.00001010.00000000.00000000/21
11001001.00001010.00000110.00000000/23
11001001.00001010.00000110.00010001
A packet with dest. Addr.: 201.10.6.17
201.10.0.0/21
201.10.6.0/23
CIDR Makes Packet Forwarding Harder
Forwarding table

## Slide 59: CIDR Makes Packet Forwarding Harder
Forwarding table may have many matches
  E.g., entries for 201.10.0.0/21 and 201.10.6.0/23
  The IP address 201.10.6.17 would match both!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 60: Longest Prefix Match Forwarding
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
  Cute algorithmic problem: very fast lookups
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
201.10.6.17
destination
forwarding table
outgoing link

## Slide 61: Getting an IP address: DHCP Protocol

## Slide 62: IP addresses: how to get one?
Q: How does a host get its IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/…
DHCP: Dynamic Host Configuration Protocol: dynamically get address from a server
  “plug-and-play”

## Slide 63: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network

## Slide 64: DHCP: Dynamic Host Configuration Protocol
DHCP overview:
  host broadcasts “DHCP discover” msg
  DHCP server responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 65: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 66
<Discover>
Broadcast: is there a DHCP server out there?

## Slide 67
A note on the “broadcast address”

## Slide 68
inet 10.104.216.101  00001010.01101000.11011000.01100101
netmask ff:ff:f0:00  11111111.11111111.11110000.00000000
broadcast 10.104.223.255 
00001010.01101000.11011111.11111111

## Slide 69
Which protocol would you use to exchange these DHCP protocol messages?
<Discover>
Broadcast: is there a DHCP server out there?
Notes: It operates on UDP (User Datagram Protocol) and typically uses port 67 for DHCP servers and port 68 for DHCP clients.

## Slide 70
<Discover>
Broadcast: is there a DHCP server out there?

## Slide 71
<Discover>
Broadcast: is there a DHCP server out there?

## Slide 72
<Discover>
Broadcast: is there a DHCP server out there?

## Slide 73
<Discover>
Broadcast: is there a DHCP server out there?

## Slide 74
<Discover>
Broadcast: is there a DHCP server out there?
yiaddr (“your” IP address)
Used by the server.

## Slide 75
<Discover>
Broadcast: is there a DHCP server out there?
XId (transaction ID)
A random ID set by the client to keep track of the “question-answer” pair.

## Slide 76
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use

## Slide 77
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use

## Slide 78
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use

## Slide 79
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use

## Slide 80
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use

## Slide 81
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use
<Request>
Broadcast: OK. I’ll take that IP address! Can I ?

## Slide 82
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use
<Request>
Broadcast: OK. I’ll take that IP address! Can I ?
Notes: It is broadcast so that other DHCP servers can get a notification. The behavior is different for first time aquiring address vs renewing the lease of the address.

## Slide 83
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use
<Request> Broadcast: OK. I’ll take that IP address! Can I ?

## Slide 84
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use
<Request> Broadcast: OK. I’ll take that IP address! Can I ?
<Ack>
Broadcast: OK. You’ve got that IP address!

## Slide 85
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use
<Request> Broadcast: OK. I’ll take that IP address! Can I ?
<Ack>
Broadcast: OK. You’ve got that IP address!
Discussion Point 1: The transaction ID (xid). RFC 2131
Discussion Point 2: Broadcast address. (Limited/Directed broadcast)
Notes: RFC 2131, Page [39]: The DHCP client broadcasts DHCPDISCOVER, DHCPREQUEST and DHCPINFORM messages, unless the client knows the address of a DHCP server. The client unicasts DHCPRELEASE messages to the server.
DHCP is not intended for use in configuring routers.

## Slide 86
Broadcast traffic is sent to all stations on a LAN.
There are two types of IPv4 broadcast addresses:
Limited broadcast: The limited broadcast address is
255.255.255.255. It is “limited” because it is never forwarded across a router.
(b) Directed broadcast: The directed (also called net-directed) broadcast address of the 192.0.2.0/24 network is 192.0.2.255 (the host portion of the address is all “1”s in binary, or 255). It is called “directed” broadcast, because traffic to these addresses may be sent from remote networks (it may be “directed”).
Broadcast addresses: Limited and Directed broadcast

## Slide 87: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 88: Dynamic Host Configuration Protocol (DHCP)
DHCP server is responsible for providing configuration information to hosts
DHCP server maintains a pool of available addresses
There is at least one DHCP server for an administrative domain (a server or a relay agent per subnet)

## Slide 89: DHCP relay
Newly booted or attached host sends DHCPDISCOVER message to a special IP address (255.255.255.255)
DHCP relay agent unicasts the message to DHCP server and waits for the response

## Slide 90
Check your IP addresses
ifconfig (linux/mac) / ipconfig (windows)

## Slide 91
Check your IP addresses
(ifconfig/ipconfig)

## Slide 92
Thank you