## Slide 1: EECS 252 Graduate Computer Architecture Lec 1 - Introduction
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://www-inst.eecs.berkeley.edu/~cs252

## Slide 2: Outline
Computer Science at a Crossroads
Computer Architecture v. Instruction Set Arch.
How would you like your CS252?
What Computer Architecture brings to table

## Slide 3: Crossroads: Conventional Wisdom in Comp. Arch
Old Conventional Wisdom: Power is free, Transistors expensive
New Conventional Wisdom: “Power wall” Power expensive, Xtors free (Can put more on chip than can afford to turn on)
Old CW: Sufficiently increasing Instruction Level Parallelism via compilers, innovation (Out-of-order, speculation, VLIW, …)
New CW: “ILP wall” law of diminishing returns on more HW for ILP
Old CW: Multiplies are slow, Memory access is fast
New CW: “Memory wall” Memory slow, multiplies fast (200 clock cycles to DRAM memory, 4 clocks for multiply)
Old CW: Uniprocessor performance 2X / 1.5 yrs
New CW: Power Wall + ILP Wall + Memory Wall = Brick Wall
  Uniprocessor performance now 2X / 5(?) yrs
 Sea change in chip design: multiple “cores” (2X processors per chip / ~ 2 years)
    More simpler processors are more power efficient

## Slide 4: Crossroads: Uniprocessor Performance
VAX : 25%/year 1978 to 1986
RISC + x86: 52%/year 1986 to 2002
RISC + x86: ??%/year 2002 to present
From Hennessy and Patterson, Computer Architecture: A Quantitative Approach, 4th edition, October, 2006

## Slide 5: Sea Change in Chip Design
Intel 4004 (1971): 4-bit processor, 2312 transistors, 0.4 MHz, 10 micron PMOS, 11 mm2 chip
Processor is the new transistor?
RISC II (1983): 32-bit, 5 stage pipeline, 40,760 transistors, 3 MHz, 3 micron NMOS, 60 mm2 chip
125 mm2 chip, 0.065 micron CMOS = 2312 RISC II+FPU+Icache+Dcache
  RISC II shrinks to ~ 0.02 mm2 at 65 nm
  Caches via DRAM or 1 transistor SRAM (www.t-ram.com) ?
  Proximity Communication via capacitive coupling at > 1 TB/s ? (Ivan Sutherland @ Sun / Berkeley)

## Slide 6: Déjà vu all over again?
Multiprocessors imminent in 1970s, ‘80s, ‘90s, …
“… today’s processors … are nearing an impasse as technologies approach the speed of light..”
David Mitchell, The Transputer: The Time Is Now (1989)
Transputer was premature  Custom multiprocessors strove to lead uniprocessors  Procrastination rewarded: 2X seq. perf. / 1.5 years
“We are dedicating all of our future product development to multicore designs. … This is a sea change in computing”
Paul Otellini, President, Intel (2004)
Difference is all microprocessor companies switch to multiprocessors (AMD, Intel, IBM, Sun; all new Apples 2 CPUs)  Procrastination penalized: 2X sequential perf. / 5 yrs  Biggest programming challenge: 1 to 2 CPUs

## Slide 7: Problems with Sea Change
Algorithms, Programming Languages, Compilers, Operating Systems, Architectures, Libraries, … not ready to supply Thread Level Parallelism or Data Level Parallelism for 1000 CPUs / chip,
Architectures not ready for 1000 CPUs / chip
  Unlike Instruction Level Parallelism, cannot be solved by just by computer architects and compiler writers alone, but also cannot be solved without participation of computer architects
This edition of CS 252 (and 4th Edition of textbook Computer Architecture: A Quantitative Approach) explores shift from Instruction Level Parallelism to Thread Level Parallelism / Data Level Parallelism
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Outline
Computer Science at a Crossroads
Computer Architecture v. Instruction Set Arch.
How would you like your CS252?
What Computer Architecture brings to table

## Slide 9: Instruction Set Architecture: Critical Interface
instruction set
software
hardware
Properties of a good abstraction
  Lasts through many generations (portability)
  Used in many different ways (generality)
  Provides convenient functionality to higher levels
  Permits an efficient implementation at lower levels
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Example: MIPS
0
r0
r1
°
°
°
r31
PC
lo
hi
Programmable storage
2^32 x bytes
31 x 32-bit GPRs (R0=0)
32 x 32-bit FP regs (paired DP)
HI, LO, PC
Data types ?
Format ?
Addressing Modes?
  Arithmetic logical
  Add, AddU, Sub, SubU, And, Or, Xor, Nor, SLT, SLTU,
  AddI, AddIU, SLTI, SLTIU, AndI, OrI, XorI, LUI
  SLL, SRL, SRA, SLLV, SRLV, SRAV
  Memory Access
  LB, LBU, LH, LHU, LW, LWL,LWR
  SB, SH, SW, SWL, SWR
  Control
  J, JAL, JR, JALR
  BEq, BNE, BLEZ,BGTZ,BLTZ,BGEZ,BLTZAL,BGEZAL
32-bit instructions on word boundary

## Slide 11: Instruction Set Architecture
“... the attributes of a [computing] system as seen by the programmer, i.e. the conceptual structure and functional behavior, as distinct from the organization of the data flows and controls the logic design, and the physical implementation.” – Amdahl, Blaauw, and Brooks, 1964
SOFTWARE
-- Organization of Programmable
Storage
-- Data Types & Data Structures:
Encodings & Representations
-- Instruction Formats
-- Instruction (or Operation Code) Set
-- Modes of Addressing and Accessing Data Items and Instructions
-- Exceptional Conditions
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: ISA vs. Computer Architecture
Old definition of computer architecture = instruction set design
  Other aspects of computer design called implementation
  Insinuates implementation is uninteresting or less challenging
Our view is computer architecture >> ISA
Architect’s job much more than instruction set design; technical hurdles today more challenging than those in instruction set design
Since instruction set design not where action is, some conclude computer architecture (using old definition) is not where action is
  We disagree on conclusion
  Agree that ISA not where action is (ISA in CA:AQA 4/e appendix)

## Slide 13: Comp. Arch. is an Integrated Approach
What really matters is the functioning of the complete system
  hardware, runtime system, compiler, operating system, and application
  In networking, this is called the “End to End argument”
Computer architecture is not just about transistors, individual instructions, or particular implementations
  E.g., Original RISC projects replaced complex instructions with a compiler + simple instructions

## Slide 14: Computer Architecture is Design and Analysis
Architecture is an iterative process:
Searching the space of possible designs
At all levels of computer systems
Creativity
Good Ideas
Mediocre Ideas
Bad Ideas
Cost /
Performance
Analysis

## Slide 15: Outline
Computer Science at a Crossroads
Computer Architecture v. Instruction Set Arch.
How would you like your CS252?
What Computer Architecture brings to table
Technology Trends

## Slide 16: CS252: Administrivia
Instructor: Prof David Patterson
Office: 635 Soda Hall, pattrsn@cs
Office Hours: Tue 11 - noon or by appt.
(Contact Cecilia Pracher; cpracher@eecs)
T. A: Archana Ganapathi, archanag@eecs
Class: M/W, 11:00 - 12:30pm 203 McLaughlin (and online)
Text: Computer Architecture: A Quantitative Approach, 4th Edition (Oct, 2006), Beta, distributed for free provided report errors
Web page: http://www.cs/~pattrsn/courses/cs252-S06/
Lectures available online <9:00 AM day of lecture
Wiki page: ??
First reading assignment: Chapter 1 (handout) for today, Monday
Appendix A (handout) A for Wed 1/24
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 17: Typical Class format (after week 2)
Bring questions to class
1-Minute Review
20-Minute Lecture
5- Minute Administrative Matters
25-Minute Lecture/Discussion
5-Minute Break (water, stretch)
25-Minute Discussion based on your questions
I will come to class early to answer questions, can stay after on Wednesdays
Time
Attention
20 min
“And in conclusion”

## Slide 18: Quizzes
Preparation causes you to systematize your understanding
Reduce the pressure of taking exam
  2 Graded quizzes: dates TBA
  goal: test knowledge vs. speed writing
    3 hrs to take 1.5-hr quiz (5:30-8:30 PM, TBA location)
  Both quizzes can bring summary sheet
    Transfer ideas from book to paper
Students/Faculty meet over free pizza/drinks at La Val’s after exam
Notes: This is the 1st slide of the “Course Structure and Course Philosophy” section of the lecture.
Need to emphasis that for exams, our goal is the test your knowledge. It is not our goal to test how well your perform under time pressure.

## Slide 19: CS 252 Course Focus
Understanding the design techniques, machine structures, technology factors, evaluation methods that will determine the form of computers in 21st Century
Technology
Programming
Languages
Operating
Systems
History
Applications
Interface Design
(ISA)
Measurement & Evaluation
Parallelism
Computer Architecture:
• Organization
• Hardware/Software Boundary
Compilers

## Slide 20: Your CS252
Computer architecture is at a crossroads
  Institutionalization and renaissance
  Power, dependability, multi CPU vs. 1 CPU performance
Mix of lecture vs. discussion
  Depends on how well reading is done before class
Goal is to learn how to do good systems research
  Learn a lot from looking at good work in the past
  At commit point, you may chose to pursue your own new idea instead.

## Slide 21: Research Paper Reading
As graduate students, you are now researchers
Most information of importance to you will be in research papers
Ability to rapidly scan and understand research papers is key to your success
So: you will read a few papers in this course
  Quick 1 paragraph summaries and question will be due in class
  Important supplement to book.
  Will discuss papers in class
Papers will be scanned and on web page

## Slide 22: Related Courses
CS 152
CS 252
CS 258
CS 250
How to build it
Implementation details
Why, Analysis,
Evaluation
Parallel Architectures,
Languages, Systems
Integrated Circuit Technology
from a computer-organization viewpoint
Strong
Prerequisite
Basic knowledge of the
organization of a computer
is assumed!

## Slide 23: Coping with CS 252
Undergrads must have taken CS152
Grad Students with too varied background?
  In past, CS grad students took written prelim exams on undergraduate material in hardware, software, and theory
  1st 5 weeks reviewed background, helped 252, 262, 270
  Prelims were dropped => some unprepared for CS 252?
Grads without CS152 equivalent may have to work hard; Review: Appendix A, B, C; CS 152 home page, maybe Computer Organization and Design (COD) 3/e
  Chapters 1 to 8 of COD if never took prerequisite
  If took a class, be sure COD Chapters 2, 6, 7 are familiar
  I can loan you a copy
Will spend 2 lectures on review of Pipelining and Memory Hierarchy, and in class quiz to be sure everyone is up to speed

## Slide 24: Grading
15% Homeworks (work in pairs) and reading writeups
35% Examinations (2 Quizzes)
35% Research Project (work in pairs)
  Transition from undergrad to grad student
  Berkeley wants you to succeed, but you need to show initiative
  pick topic (more on this later)
  meet 3 times with faculty to see progress
  give oral presentation or poster session
  written report like conference paper
  3 weeks work full time for 2 people
  Opportunity to do “research in the small” to help make transition from good student to research colleague
15% Class Participation

## Slide 25: New Project opportunity this semester
FPGAs as New Research Platform
As ~ 25 CPUs can fit in Field Programmable Gate Array (FPGA), 1000-CPU system from ~ 40 FPGAs?
  64-bit simple “soft core” RISC at 100MHz in 2004 (Virtex-II)
  FPGA generations every 1.5 yrs; 2X CPUs, 2X clock rate
HW research community does logic design (“gate shareware”) to create out-of-the-box, Massively Parallel Processor runs standard binaries of OS, apps
  Gateware: Processors, Caches, Coherency, Ethernet Interfaces, Switches, Routers, … (IBM, Sun have donated processors)
  E.g., 1000 processor, IBM Power binary-compatible, cache-coherent supercomputer @ 200 MHz; fast enough for research
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: RAMP
Since goal is to ramp up research in multiprocessing, called Research Accelerator for Multiple Processors
  To learn more, read “RAMP: Research Accelerator for Multiple Processors - A Community Vision for a Shared Experimental Parallel HW/SW Platform,” Technical Report UCB//CSD-05-1412, Sept 2005
  Web page ramp.eecs.berkeley.edu

## Slide 27: Why RAMP Good for Research?
 | SMP | Cluster | Simulate | RAMP
Cost (1000 CPUs) | F ($40M) | C ($2M) | A+ ($0M) | A ($0.1M)
Cost of ownership | A | D | A | A
Scalability | C | A | A | A
Power/Space (kilowatts, racks) | D (120 kw, 12 racks) | D (120 kw, 12 racks) | A+ (.1 kw, 0.1 racks) | A (1.5 kw, 0.3 racks)
Community | D | A | A | A
Observability | D | C | A+ | A+
Reproducibility | B | D | A+ | A+
Flexibility | D | C | A+ | A+
Credibility | A+ | A+ | F | A
Perform. (clock) | A (2 GHz) | A (3 GHz) | F (0 GHz) | C (0.2 GHz)
GPA | C | B- | B | A-
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: RAMP 1 Hardware
Completed Dec. 2004 (14x17 inch 22-layer PCB)
Module:
  FPGAs, memory, 10GigE conn.
  Compact Flash
  Administration/ maintenance ports:
    10/100 Enet
    HDMI/DVI
    USB
  ~4K/module w/o FPGAs or DRAM
  Called “BEE2” for Berkeley Emulation Engine 2
Notes: <number>
<footer>
<header>
<date/time>

## Slide 29
Multiple Module RAMP 1 Systems
8 compute modules (plus power supplies) in 8U rack mount chassis
  500-1000 emulated processors
Many topologies possible
2U single module tray for developers
Disk storage: disk emulator + Network Attached Storage
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30: Vision: Multiprocessing Watering Hole
RAMP attracts many communities to shared artifact  Cross-disciplinary interactions  Accelerate innovation in multiprocessing
RAMP as next Standard Research Platform? (e.g., VAX/BSD Unix in 1980s, x86/Linux in 1990s)
RAMP
Parallel file system
Thread scheduling
Multiprocessor switch design
Fault insertion to check dependability
Data center in a box
Internet in a box
Dataflow language/computer
Security enhancements
Router design
Compile to FPGA
Parallel languages

## Slide 31: Supporters (wrote letters to NSF) & Participants
Gordon Bell (Microsoft)
Ivo Bolsens (Xilinx CTO)
Norm Jouppi (HP Labs)
Bill Kramer (NERSC/LBL)
Craig Mundie (MS CTO)
G. Papadopoulos (Sun CTO)
Justin Rattner (Intel CTO)
Ivan Sutherland (Sun Fellow)
Chuck Thacker (Microsoft)
Kees Vissers (Xilinx)
Doug Burger (Texas)
Bill Dally (Stanford)
Carl Ebeling (Washington)
Susan Eggers (Washington)
Steve Keckler (Texas)
Greg Morrisett (Harvard)
Scott Shenker (Berkeley)
Ion Stoica (Berkeley)
Kathy Yelick (Berkeley)
RAMP Participants: Arvind (MIT), Krste Asanovíc (MIT), Derek Chiou (Texas), James Hoe (CMU), Christos Kozyrakis (Stanford), Shih-Lien Lu (Intel), Mark Oskin (Washington), David Patterson (Berkeley), Jan Rabaey (Berkeley), and John Wawrzynek (Berkeley)

## Slide 32: RAMP Summary
RAMP as system-level time machine: preview computers of future to accelerate HW/SW generations
  Trace anything, Reproduce everything, Tape out every day
  FTP new supercomputer overnight and boot in morning
  Clone to check results (as fast in Berkeley as in Boston?)
  Emulate Massive Multiprocessor, Data Center, or Distributed Computer
Carpe Diem
  Systems researchers (HW & SW) need the capability
  FPGA technology is ready today, and getting better every year
  Stand on shoulders vs. toes: standardize on multi-year Berkeley effort on FPGA platform Berkeley Emulation Engine 2 (BEE2)
  Architecture researchers get opportunity to immediately aid colleagues via gateware (as SW researchers have done in past)
  See ramp.eecs.berkeley.edu
Vision “Multiprocessor Research Watering Hole” accelerate research in multiprocessing via standard research platform  hasten sea change from sequential to parallel computing
Notes: <number>
<footer>
<header>
<date/time>

## Slide 33: RAMP projects for CS 252
Design a of guest timing accounting strategy
  Want to be able specify performance parameters (clock rate, memory latency, network latency, …)
  Host must accurately account for guest clock cycles
  Don’t want to slow down host execution time very much
Build a disk emulator for use in RAMP
  Imitates disk, accesses network attached storage for data
  Modeled after guest VM/driver VM from Xen VM?
Build a cluster using components from opencores.org on BEE2
  Open source hardware consortium
Build an emulator of an “Internet in a Box”
  (Emulab/Planetlab in a box is closer to reality)

## Slide 34: Other projects
Recreate results from research paper to see
  If they are reproducible
  If they still hold
Performance evaluation of Niagara, new 8 core, 4 threads per core chip from Sun
Propose your own research project that is related to computer architecture

## Slide 35: Outline
Computer Science at a Crossroads
Computer Architecture v. Instruction Set Arch.
How would you like your CS252?
What Computer Architecture brings to table

## Slide 36: What Computer Architecture brings to Table
Other fields often borrow ideas from architecture
Quantitative Principles of Design
  Take Advantage of Parallelism
  Principle of Locality
  Focus on the Common Case
  Amdahl’s Law
  The Processor Performance Equation
Careful, quantitative comparisons
  Define, quantity, and summarize relative performance
  Define and quantity relative cost
  Define and quantity dependability
  Define and quantity power
Culture of anticipating and exploiting advances in technology
Culture of well-defined interfaces that are carefully implemented and thoroughly checked

## Slide 37: 1) Taking Advantage of Parallelism
Increasing throughput of server computer via multiple processors or multiple disks
Detailed HW design
  Carry lookahead adders uses parallelism to speed up computing sums from linear to logarithmic in number of bits per operand
  Multiple memory banks searched in parallel in set-associative caches
Pipelining: overlap instruction execution to reduce the total time to complete an instruction sequence.
  Not every instruction depends on immediate predecessor  executing instructions completely/partially in parallel possible
  Classic 5-stage pipeline: 1) Instruction Fetch (Ifetch), 2) Register Read (Reg), 3) Execute (ALU), 4) Data Memory Access (Dmem), 5) Register Write (Reg)

## Slide 38: Pipelined Instruction Execution
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5

## Slide 39: Limits to pipelining
Hazards prevent next instruction from executing during its designated clock cycle
  Structural hazards: attempt to use the same hardware to do two different things at once
  Data hazards: Instruction depends on result of prior instruction still in the pipeline
  Control hazards: Caused by delay between the fetching of instructions and decisions about changes in control flow (branches and jumps).
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 40: 2) The Principle of Locality
The Principle of Locality:
  Program access a relatively small portion of the address space at any instant of time.
Two Different Types of Locality:
  Temporal Locality (Locality in Time): If an item is referenced, it will tend to be referenced again soon (e.g., loops, reuse)
  Spatial Locality (Locality in Space): If an item is referenced, items whose addresses are close by tend to be referenced soon (e.g., straight-line code, array access)
Last 30 years, HW relied on locality for memory perf.
P
MEM
$
Notes: The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
This is kind of like in real life, we all have a lot of friends. But at any given time most of us can only keep in touch with a small group of them.
There are two different types of locality: Temporal and Spatial. Temporal locality is the locality in time which says if an item is referenced, it will tend to be referenced again soon.
This is like saying if you just talk to one of your friends, it is likely that you will talk to him or her again soon.
This makes sense. For example, if you just have lunch with a friend, you may say, let’s go to the ball game this Sunday. So you will talk to him again soon.
Spatial locality is the locality in space. It says if an item is referenced, items whose addresses are close by tend to be referenced soon.
Once again, using our analogy. We can usually divide our friends into groups. Like friends from high school, friends from work, friends from home.
Let’s say you just talk to one of your friends from high school and she may say something like: “So did you hear so and so just won the lottery.”
You probably will say NO, I better give him a call and find out more.
So this is an example of spatial locality. You just talked to a friend from your high school days. As a result, you end up talking to another high school friend. Or at least in this case, you hope he still remember you are his friend.
+3 = 10 min. (X:50)

## Slide 41: Levels of the Memory Hierarchy
CPU Registers
100s Bytes
300 – 500 ps (0.3-0.5 ns)
L1 and L2 Cache
10s-100s K Bytes
~1 ns - ~10 ns
$1000s/ GByte
Main Memory
G Bytes
80ns- 200ns
~ $100/ GByte
Disk
10s T Bytes, 10 ms (10,000,000 ns)
~ $1 / GByte
Capacity
Access Time
Cost
Tape
infinite
sec-min
~$1 / GByte
Registers
L1 Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Xfer Unit
prog./compiler
1-8 bytes
cache cntl
32-64 bytes
OS
4K-8K bytes
user/operator
Mbytes
Upper Level
Lower Level
faster
Larger
L2 Cache
cache cntl
64-128 bytes
Blocks

## Slide 42: 3) Focus on the Common Case
Common sense guides computer design
  Since its engineering, common sense is valuable
In making a design trade-off, favor the frequent case over the infrequent case
  E.g., Instruction fetch and decode unit used more frequently than multiplier, so optimize it 1st
  E.g., If database server has 50 disks / processor, storage dependability dominates system dependability, so optimize it 1st
Frequent case is often simpler and can be done faster than the infrequent case
  E.g., overflow is rare when adding 2 numbers, so improve performance by optimizing more common case of no overflow
  May slow down overflow, but overall performance improved by optimizing for the normal case
What is frequent case and how much performance improved by making case faster => Amdahl’s Law

## Slide 43: 4) Amdahl’s Law
Best you could ever hope to do:

## Slide 44: Amdahl’s Law example
New CPU 10X faster
I/O bound server, so 60% time waiting for I/O
Apparently, its human nature to be attracted by 10X faster, vs. keeping in perspective its just 1.6X faster

## Slide 45: 5) Processor performance equation
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle
Inst Count CPI Clock Rate
Program X
Compiler X (X)
Inst. Set. X X
Organization X X
Technology X
inst count
CPI
Cycle time

## Slide 46: What’s a Clock Cycle?
Old days: 10 levels of gates
Today: determined by numerous time-of-flight issues + gate delays
  clock propagation, wire lengths, drivers
Latch
or
register
combinational
logic

## Slide 47: And in conclusion …
Computer Architecture >> instruction sets
Computer Architecture skill sets are different
  5 Quantitative principles of design
  Quantitative approach to design
  Solid interfaces that really work
  Technology tracking and anticipation
CS 252 to learn new skills, transition to research
Computer Science at the crossroads from sequential to parallel computing
  Salvation requires innovation in many fields, including computer architecture
RAMP is interesting and timely CS 252 project opportunity given CS is at the crossroads
Read Chapter 1, then Appendix A, record bugs!