## Slide 1: EECS 252 Graduate Computer Architecture Lec 2 - Introduction
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://www-inst.eecs.berkeley.edu/~cs252

## Slide 2: Review from last lecture
Computer Architecture >> instruction sets
Computer Architecture skill sets are different
  5 Quantitative principles of design
  Quantitative approach to design
  Solid interfaces that really work
  Technology tracking and anticipation
CS 252 to learn new skills, transition to research
Computer Science at the crossroads from sequential to parallel computing
  Salvation requires innovation in many fields, including computer architecture
RAMP is interesting and timely CS 252 project opportunity given CS is at the crossroads

## Slide 3: Review: Computer Architecture brings
Other fields often borrow ideas from architecture
Quantitative Principles of Design
  Take Advantage of Parallelism
  Principle of Locality
  Focus on the Common Case
  Amdahl’s Law
  The Processor Performance Equation
Careful, quantitative comparisons
  Define, quantity, and summarize relative performance
  Define and quantity relative cost
  Define and quantity dependability
  Define and quantity power
Culture of anticipating and exploiting advances in technology
Culture of well-defined interfaces that are carefully implemented and thoroughly checked

## Slide 4: Outline
Review
Technology Trends: Culture of tracking, anticipating and exploiting advances in technology
Careful, quantitative comparisons:
Define, quantity, and summarize relative performance
Define and quantity relative cost
Define and quantity dependability
Define and quantity power

## Slide 5: Moore’s Law: 2X transistors / “year”
“Cramming More Components onto Integrated Circuits”
  Gordon Moore, Electronics, 1965
# on transistors / cost-effective integrated circuit double every N months (12 ≤ N ≤ 24)

## Slide 6: Tracking Technology Performance Trends
Drill down into 4 technologies:
  Disks,
  Memory,
  Network,
  Processors
Compare ~1980 Archaic (Nostalgic) vs. ~2000 Modern (Newfangled)
  Performance Milestones in each technology
Compare for Bandwidth vs. Latency improvements in performance over time
Bandwidth: number of events per unit time
  E.g., M bits / second over network, M bytes / second from disk
Latency: elapsed time for a single event
  E.g., one-way network delay in microseconds, average disk access time in milliseconds

## Slide 7: Disks: Archaic(Nostalgic) v. Modern(Newfangled)
Seagate 373453, 2003
15000 RPM (4X)
73.4 GBytes (2500X)
Tracks/Inch: 64000 (80X)
Bits/Inch: 533,000 (60X)
Four 2.5” platters (in 3.5” form factor)
Bandwidth: 86 MBytes/sec (140X)
Latency: 5.7 ms (8X)
Cache: 8 MBytes
CDC Wren I, 1983
3600 RPM
0.03 GBytes capacity
Tracks/Inch: 800
Bits/Inch: 9550
Three 5.25” platters
Bandwidth: 0.6 MBytes/sec
Latency: 48.3 ms
Cache: none

## Slide 8: Latency Lags Bandwidth (for last ~20 years)
Performance Milestones
Disk: 3600, 5400, 7200, 10000, 15000 RPM (8x, 143x)
(latency = simple operation w/o contention
BW = best-case)
Notes: <number>
<footer>
<header>
<date/time>
Disk: 33X BW, 6X latency

## Slide 9: Memory: Archaic (Nostalgic) v. Modern (Newfangled)
1980 DRAM (asynchronous)
0.06 Mbits/chip
64,000 xtors, 35 mm2
16-bit data bus per module, 16 pins/chip
13 Mbytes/sec
Latency: 225 ns
(no block transfer)
2000 Double Data Rate Synchr. (clocked) DRAM
256.00 Mbits/chip (4000X)
256,000,000 xtors, 204 mm2
64-bit data bus per DIMM, 66 pins/chip (4X)
1600 Mbytes/sec (120X)
Latency: 52 ns (4X)
Block transfers (page mode)

## Slide 10: Latency Lags Bandwidth (last ~20 years)
Performance Milestones
Memory Module: 16bit plain DRAM, Page Mode DRAM, 32b, 64b, SDRAM, DDR SDRAM (4x,120x)
Disk: 3600, 5400, 7200, 10000, 15000 RPM (8x, 143x)
(latency = simple operation w/o contention
BW = best-case)
Notes: <number>
<footer>
<header>
<date/time>
DRAM: 120X BW, 4X latency
Jog between 3rd and 4th point is because a lot of time between 32b Fast page mode and 64b

## Slide 11: LANs: Archaic (Nostalgic)v. Modern (Newfangled)
Ethernet 802.3
Year of Standard: 1978
10 Mbits/s link speed
Latency: 3000 sec
Shared media
Coaxial cable
Ethernet 802.3ae
Year of Standard: 2003
10,000 Mbits/s (1000X) link speed
Latency: 190 sec (15X)
Switched media
Category 5 copper wire
Coaxial Cable:
Copper core
Insulator
Braided outer conductor
Plastic Covering
Copper, 1mm thick, twisted to avoid antenna effect
Twisted Pair:
"Cat 5" is 4 twisted pairs in bundle

## Slide 12: Latency Lags Bandwidth (last ~20 years)
Performance Milestones
Ethernet: 10Mb, 100Mb, 1000Mb, 10000 Mb/s (16x,1000x)
Memory Module: 16bit plain DRAM, Page Mode DRAM, 32b, 64b, SDRAM, DDR SDRAM (4x,120x)
Disk: 3600, 5400, 7200, 10000, 15000 RPM (8x, 143x)
(latency = simple operation w/o contention
BW = best-case)
Notes: <number>
<footer>
<header>
<date/time>
Network: 1000X BW, 13X Latency

## Slide 13: CPUs: Archaic (Nostalgic) v. Modern (Newfangled)
1982 Intel 80286
12.5 MHz
2 MIPS (peak)
Latency 320 ns
134,000 xtors, 47 mm2
16-bit data bus, 68 pins
Microcode interpreter, separate FPU chip
(no caches)
2001 Intel Pentium 4
1500 MHz (120X)
4500 MIPS (peak) (2250X)
Latency 15 ns (20X)
42,000,000 xtors, 217 mm2
64-bit data bus, 423 pins
3-way superscalar, Dynamic translate to RISC, Superpipelined (22 stage), Out-of-Order execution
On-chip 8KB Data caches, 96KB Instr. Trace cache, 256KB L2 cache

## Slide 14: Latency Lags Bandwidth (last ~20 years)
Performance Milestones
Processor: ‘286, ‘386, ‘486, Pentium, Pentium Pro, Pentium 4 (21x,2250x)
Ethernet: 10Mb, 100Mb, 1000Mb, 10000 Mb/s (16x,1000x)
Memory Module: 16bit plain DRAM, Page Mode DRAM, 32b, 64b, SDRAM, DDR SDRAM (4x,120x)
Disk : 3600, 5400, 7200, 10000, 15000 RPM (8x, 143x)
CPU high,
Memory low (“Memory Wall”)
Notes: <number>
<footer>
<header>
<date/time>
Processor: 2250X, 22X Latency

## Slide 15: Rule of Thumb for Latency Lagging BW
In the time that bandwidth doubles, latency improves by no more than a factor of 1.2 to 1.4
  (and capacity improves faster than bandwidth)
Stated alternatively: Bandwidth improves by more than the square of the improvement in Latency

## Slide 16: CS252: Administrivia
Instructor: Prof David Patterson
Office: 635 Soda Hall, pattrsn@cs
Office Hours: Tue 11 - noon or by appt.
(Contact Cecilia Pracher; cpracher@eecs)
T. A: Archana Ganapathi, archanag@eecs
Class: M/W, 11:00 - 12:30pm 203 McLaughlin (and online)
Text: Computer Architecture: A Quantitative Approach, 4th Edition (Oct, 2006), Beta, distributed for free provided report errors
Web page: http://www.cs/~pattrsn/courses/cs252-S06/
Lectures available online <9:00 AM day of lecture
Wiki page: ??
Reading assignment: Pipeline baiscs Appendix A (handout) A for Wed 1/24
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 17: Computers in the News
“Intel loses market share in own backyard,” By Tom Krazit, CNET News.com, 1/18/2006
“Intel's share of the U.S. retail PC market fell by 11 percentage points, from 64.4 percent in the fourth quarter of 2004 to 53.3 percent. … Current Analysis' market share numbers measure U.S. retail sales only, and therefore exclude figures from Dell, which uses its Web site to sell directly to consumers. … AMD chips were found in 52.5 percent of desktop PCs sold in U.S. retail stores during that period.”
Technical advantages of AMD Opteron/Athlon vs. Intel Pentium 4 as we’ll see in this course.

## Slide 18: 6 Reasons Latency Lags Bandwidth
1. Moore’s Law helps BW more than latency
  Faster transistors, more transistors, more pins help Bandwidth
    MPU Transistors: 0.130 vs. 42 M xtors (300X)
    DRAM Transistors: 0.064 vs. 256 M xtors (4000X)
    MPU Pins: 68 vs. 423 pins (6X)
    DRAM Pins: 16 vs. 66 pins (4X)
  Smaller, faster transistors but communicate over (relatively) longer lines: limits latency
    Feature size: 1.5 to 3 vs. 0.18 micron (8X,17X)
    MPU Die Size: 35 vs. 204 mm2 (ratio sqrt  2X)
    DRAM Die Size: 47 vs. 217 mm2 (ratio sqrt  2X)

## Slide 19: 6 Reasons Latency Lags Bandwidth (cont’d)
2. Distance limits latency
  Size of DRAM block  long bit and word lines  most of DRAM access time
  Speed of light and computers on network
  1. & 2. explains linear latency vs. square BW?
3. Bandwidth easier to sell (“bigger=better”)
  E.g., 10 Gbits/s Ethernet (“10 Gig”) vs. 10 sec latency Ethernet
  4400 MB/s DIMM (“PC4400”) vs. 50 ns latency
  Even if just marketing, customers now trained
  Since bandwidth sells, more resources thrown at bandwidth, which further tips the balance

## Slide 20: 6 Reasons Latency Lags Bandwidth (cont’d)
4. Latency helps BW, but not vice versa
  Spinning disk faster improves both bandwidth and rotational latency
    3600 RPM  15000 RPM = 4.2X
    Average rotational latency: 8.3 ms 2.0 ms
    Things being equal, also helps BW by 4.2X
  Lower DRAM latency  More access/second (higher bandwidth)
  Higher linear density helps disk BW (and capacity), but not disk Latency
    9,550 BPI  533,000 BPI  60X in BW

## Slide 21: 6 Reasons Latency Lags Bandwidth (cont’d)
5. Bandwidth hurts latency
  Queues help Bandwidth, hurt Latency (Queuing Theory)
  Adding chips to widen a memory module increases Bandwidth but higher fan-out on address lines may increase Latency
6. Operating System overhead hurts Latency more than Bandwidth
  Long messages amortize overhead; overhead bigger part of short messages

## Slide 22: Summary of Technology Trends
For disk, LAN, memory, and microprocessor, bandwidth improves by square of latency improvement
  In the time that bandwidth doubles, latency improves by no more than 1.2X to 1.4X
Lag probably even larger in real systems, as bandwidth gains multiplied by replicated components
  Multiple processors in a cluster or even in a chip
  Multiple disks in a disk array
  Multiple memory modules in a large memory
  Simultaneous communication in switched LAN
HW and SW developers should innovate assuming Latency Lags Bandwidth
  If everything improves at the same rate, then nothing really changes
  When rates vary, require real innovation

## Slide 23: Outline
Review
Technology Trends: Culture of tracking, anticipating and exploiting advances in technology
Careful, quantitative comparisons:
Define and quantity power
Define and quantity dependability
Define, quantity, and summarize relative performance
Define and quantity relative cost

## Slide 24: Define and quantity power ( 1 / 2)
For CMOS chips, traditional dominant energy consumption has been in switching transistors, called dynamic power
For mobile devices, energy better metric
For a fixed task, slowing clock rate (frequency switched) reduces power, but not energy
Capacitive load a function of number of transistors connected to output and technology, which determines capacitance of wires and transistors
Dropping voltage helps both, so went from 5V to 1V
To save energy & dynamic power, most CPUs now turn off clock of inactive modules (e.g. Fl. Pt. Unit)

## Slide 25: Example of quantifying power
Suppose 15% reduction in voltage results in a 15% reduction in frequency. What is impact on dynamic power?

## Slide 26: Define and quantity power (2 / 2)
Because leakage current flows even when a transistor is off, now static power important too
Leakage current increases in processors with smaller transistor sizes
Increasing the number of transistors increases power even if they are turned off
In 2006, goal for leakage is 25% of total power consumption; high performance designs at 40%
Very low power systems even gate voltage to inactive modules to control loss due to leakage

## Slide 27: Outline
Review
Technology Trends: Culture of tracking, anticipating and exploiting advances in technology
Careful, quantitative comparisons:
Define and quantity power
Define and quantity dependability
Define, quantity, and summarize relative performance
Define and quantity relative cost

## Slide 28: Define and quantity dependability (1/3)
How decide when a system is operating properly?
Infrastructure providers now offer Service Level Agreements (SLA) to guarantee that their networking or power service would be dependable
Systems alternate between 2 states of service with respect to an SLA:
Service accomplishment, where the service is delivered as specified in SLA
Service interruption, where the delivered service is different from the SLA
Failure = transition from state 1 to state 2
Restoration = transition from state 2 to state 1

## Slide 29: Define and quantity dependability (2/3)
Module reliability = measure of continuous service accomplishment (or time to failure). 2 metrics
Mean Time To Failure (MTTF) measures Reliability
Failures In Time (FIT) = 1/MTTF, the rate of failures
  Traditionally reported as failures per billion hours of operation
Mean Time To Repair (MTTR) measures Service Interruption
  Mean Time Between Failures (MTBF) = MTTF+MTTR
Module availability measures service as alternate between the 2 states of accomplishment and interruption (number between 0 and 1, e.g. 0.9)
Module availability = MTTF / ( MTTF + MTTR)

## Slide 30: Example calculating reliability
If modules have exponentially distributed lifetimes (age of module does not affect probability of failure), overall failure rate is the sum of failure rates of the modules
Calculate FIT and MTTF for 10 disks (1M hour MTTF per disk), 1 disk controller (0.5M hour MTTF), and 1 power supply (0.2M hour MTTF):

## Slide 31: Example calculating reliability
If modules have exponentially distributed lifetimes (age of module does not affect probability of failure), overall failure rate is the sum of failure rates of the modules
Calculate FIT and MTTF for 10 disks (1M hour MTTF per disk), 1 disk controller (0.5M hour MTTF), and 1 power supply (0.2M hour MTTF):

## Slide 32: Outline
Review
Technology Trends: Culture of tracking, anticipating and exploiting advances in technology
Careful, quantitative comparisons:
Define and quantity power
Define and quantity dependability
Define, quantity, and summarize relative performance
Define and quantity relative cost

## Slide 33: Definition: Performance
Performance(X) Execution_time(Y)
n = =
Performance(Y) Execution_time(X)
Performance is in units of things per sec
  bigger is better
If we are primarily concerned with response time
  performance(x) = 1 execution_time(x)
  " X is n times faster than Y" means

## Slide 34: Performance: What to measure
Usually rely on benchmarks vs. real workloads
To increase predictability, collections of benchmark applications, called benchmark suites, are popular
SPECCPU: popular desktop benchmark suite
  CPU only, split between integer and floating point programs
  SPECint2000 has 12 integer, SPECfp2000 has 14 integer pgms
  SPECCPU2006 to be announced Spring 2006
  SPECSFS (NFS file server) and SPECWeb (WebServer) added as server benchmarks
Transaction Processing Council measures server performance and cost-performance for databases
  TPC-C Complex query for Online Transaction Processing
  TPC-H models ad hoc decision support
  TPC-W a transactional web benchmark
  TPC-App application server and web services benchmark

## Slide 35: How Summarize Suite Performance (1/5)
Arithmetic average of execution time of all pgms?
  But they vary by 4X in speed, so some would be more important than others in arithmetic average
Could add a weights per program, but how pick weight?
  Different companies want different weights for their products
SPECRatio: Normalize execution times to reference computer, yielding a ratio proportional to performance =
time on reference computer
time on computer being rated

## Slide 36: How Summarize Suite Performance (2/5)
If program SPECRatio on Computer A is 1.25 times bigger than Computer B, then
Note that when comparing 2 computers as a ratio, execution times on the reference computer drop out, so choice of reference computer is irrelevant

## Slide 37: How Summarize Suite Performance (3/5)
Since ratios, proper mean is geometric mean (SPECRatio unitless, so arithmetic mean meaningless)
Geometric mean of the ratios is the same as the ratio of the geometric means
Ratio of geometric means = Geometric mean of performance ratios  choice of reference computer is irrelevant!
These two points make geometric mean of ratios attractive to summarize performance

## Slide 38: How Summarize Suite Performance (4/5)
Does a single mean well summarize performance of programs in benchmark suite?
Can decide if mean a good predictor by characterizing variability of distribution using standard deviation
Like geometric mean, geometric standard deviation is multiplicative rather than arithmetic
Can simply take the logarithm of SPECRatios, compute the standard mean and standard deviation, and then take the exponent to convert back:

## Slide 39: How Summarize Suite Performance (5/5)
Standard deviation is more informative if know distribution has a standard form
  bell-shaped normal distribution, whose data are symmetric around mean
  lognormal distribution, where logarithms of data--not data itself--are normally distributed (symmetric) on a logarithmic scale
For a lognormal distribution, we expect that
68% of samples fall in range
95% of samples fall in range
Note: Excel provides functions EXP(), LN(), and STDEV() that make calculating geometric mean and multiplicative standard deviation easy

## Slide 40: Example Standard Deviation (1/2)
GM and multiplicative StDev of SPECfp2000 for Itanium 2

## Slide 41: Example Standard Deviation (2/2)
GM and multiplicative StDev of SPECfp2000 for AMD Athlon

## Slide 42: Comments on Itanium 2 and Athlon
Standard deviation of 1.98 for Itanium 2 is much higher-- vs. 1.40--so results will differ more widely from the mean, and therefore are likely less predictable
Falling within one standard deviation:
  10 of 14 benchmarks (71%) for Itanium 2
  11 of 14 benchmarks (78%) for Athlon
Thus, the results are quite compatible with a lognormal distribution (expect 68%)

## Slide 43: And in conclusion …
Tracking and extrapolating technology part of architect’s responsibility
Expect Bandwidth in disks, DRAM, network, and processors to improve by at least as much as the square of the improvement in Latency
Quantify dynamic and static power
  Capacitance x Voltage2 x frequency, Energy vs. power
Quantify dependability
  Reliability (MTTF, FIT), Availability (99.9…)
Quantify and summarize performance
  Ratios, Geometric Mean, Multiplicative Standard Deviation
Read Appendix A, record bugs online!