## Slide 1: EECS 252 Graduate Computer Architecture Lec 3 – Performance + Pipeline Review
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://www-inst.eecs.berkeley.edu/~cs252

## Slide 2: Review from last lecture
Tracking and extrapolating technology part of architect’s responsibility
Expect Bandwidth in disks, DRAM, network, and processors to improve by at least as much as the square of the improvement in Latency
Quantify Cost (vs. Price)
  IC  f(Area2) + Learning curve, volume, commodity, margins
Quantify dynamic and static power
  Capacitance x Voltage2 x frequency, Energy vs. power
Quantify dependability
  Reliability (MTTF vs. FIT), Availability (MTTF/(MTTF+MTTR)

## Slide 3: Outline
Review
Quantify and summarize performance
  Ratios, Geometric Mean, Multiplicative Standard Deviation
F&P: Benchmarks age, disks fail,1 point fail danger
252 Administrivia
MIPS – An ISA for Pipelining
5 stage pipelining
Structural and Data Hazards
Forwarding
Branch Schemes
Exceptions and Interrupts
Conclusion

## Slide 4: Definition: Performance
Performance(X) Execution_time(Y)
n = =
Performance(Y) Execution_time(X)
Performance is in units of things per sec
  bigger is better
If we are primarily concerned with response time
  performance(x) = 1 execution_time(x)
  " X is n times faster than Y" means

## Slide 5: Performance: What to measure
Usually rely on benchmarks vs. real workloads
To increase predictability, collections of benchmark applications-- benchmark suites -- are popular
SPECCPU: popular desktop benchmark suite
  CPU only, split between integer and floating point programs
  SPECint2000 has 12 integer, SPECfp2000 has 14 integer pgms
  SPECCPU2006 to be announced Spring 2006
  SPECSFS (NFS file server) and SPECWeb (WebServer) added as server benchmarks
Transaction Processing Council measures server performance and cost-performance for databases
  TPC-C Complex query for Online Transaction Processing
  TPC-H models ad hoc decision support
  TPC-W a transactional web benchmark
  TPC-App application server and web services benchmark

## Slide 6: How Summarize Suite Performance (1/5)
Arithmetic average of execution time of all pgms?
  But they vary by 4X in speed, so some would be more important than others in arithmetic average
Could add a weights per program, but how pick weight?
  Different companies want different weights for their products
SPECRatio: Normalize execution times to reference computer, yielding a ratio proportional to performance =
time on reference computer
time on computer being rated

## Slide 7: How Summarize Suite Performance (2/5)
If program SPECRatio on Computer A is 1.25 times bigger than Computer B, then
Note that when comparing 2 computers as a ratio, execution times on the reference computer drop out, so choice of reference computer is irrelevant

## Slide 8: How Summarize Suite Performance (3/5)
Since ratios, proper mean is geometric mean (SPECRatio unitless, so arithmetic mean meaningless)
2 points make geometric mean of ratios attractive to summarize performance:
Geometric mean of the ratios is the same as the ratio of the geometric means
Ratio of geometric means = Geometric mean of performance ratios  choice of reference computer is irrelevant!

## Slide 9: How Summarize Suite Performance (4/5)
Does a single mean well summarize performance of programs in benchmark suite?
Can decide if mean a good predictor by characterizing variability of distribution using standard deviation
Like geometric mean, geometric standard deviation is multiplicative rather than arithmetic
Can simply take the logarithm of SPECRatios, compute the standard mean and standard deviation, and then take the exponent to convert back:

## Slide 10: How Summarize Suite Performance (5/5)
Standard deviation is more informative if know distribution has a standard form
  bell-shaped normal distribution, whose data are symmetric around mean
  lognormal distribution, where logarithms of data--not data itself--are normally distributed (symmetric) on a logarithmic scale
For a lognormal distribution, we expect that
68% of samples fall in range
95% of samples fall in range
Note: Excel provides functions EXP(), LN(), and STDEV() that make calculating geometric mean and multiplicative standard deviation easy

## Slide 11: Example Standard Deviation (1/2)
GM and multiplicative StDev of SPECfp2000 for Itanium 2
Outside 1 StDev

## Slide 12: Example Standard Deviation (2/2)
GM and multiplicative StDev of SPECfp2000 for AMD Athlon
Outside 1 StDev

## Slide 13: Comments on Itanium 2 and Athlon
Standard deviation of 1.98 for Itanium 2 is much higher-- vs. 1.40--so results will differ more widely from the mean, and therefore are likely less predictable
SPECRatios falling within one standard deviation:
  10 of 14 benchmarks (71%) for Itanium 2
  11 of 14 benchmarks (78%) for Athlon
Thus, results are quite compatible with a lognormal distribution (expect 68% for 1 StDev)

## Slide 14: Fallacies and Pitfalls (1/2)
Fallacies - commonly held misconceptions
  When discussing a fallacy, we try to give a counterexample.
Pitfalls - easily made mistakes.
  Often generalizations of principles true in limited context
  Show Fallacies and Pitfalls to help you avoid these errors
Fallacy: Benchmarks remain valid indefinitely
  Once a benchmark becomes popular, tremendous pressure to improve performance by targeted optimizations or by aggressive interpretation of the rules for running the benchmark: “benchmarksmanship.”
  70 benchmarks from the 5 SPEC releases. 70% were dropped from the next release since no longer useful
Pitfall: A single point of failure
  Rule of thumb for fault tolerant systems: make sure that every component was redundant so that no single component failure could bring down the whole system (e.g, power supply)

## Slide 15: Fallacies and Pitfalls (2/2)
Fallacy - Rated MTTF of disks is 1,200,000 hours or  140 years, so disks practically never fail
But disk lifetime is 5 years  replace a disk every 5 years; on average, 28 replacements wouldn't fail
A better unit: % that fail (1.2M MTTF = 833 FIT)
Fail over lifetime: if had 1000 disks for 5 years = 1000*(5*365*24)*833 /109 = 36,485,000 / 106 = 37 = 3.7% (37/1000) fail over 5 yr lifetime (1.2M hr MTTF)
But this is under pristine conditions
  little vibration, narrow temperature range  no power failures
Real world: 3% to 6% of SCSI drives fail per year
  3400 - 6800 FIT or 150,000 - 300,000 hour MTTF [Gray & van Ingen 05]
3% to 7% of ATA drives fail per year
  3400 - 8000 FIT or 125,000 - 300,000 hour MTTF [Gray & van Ingen 05]

## Slide 16: CS252: Administrivia
Instructor: Prof David Patterson
Office: 635 Soda Hall, pattrsn@cs
Office Hours: Tue 11 - noon or by appt.
(Contact Cecilia Pracher; cpracher@eecs)
T. A: Archana Ganapathi, archanag@eecs
Class: M/W, 11:00 - 12:30pm 203 McLaughlin (and online)
Text: Computer Architecture: A Quantitative Approach, 4th Edition (Oct, 2006), Beta, distributed for free provided report errors
Web page: http://www.cs/~pattrsn/courses/cs252-S06/
Lectures available online <9:00 AM day of lecture
Wiki page: ??
Reading assignment: Memory Hierarchy Basics Appendix C (handout) for Mon 1/30
Wed 2/1: Great ISA debate (3 papers) + Prerequisite Quiz
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 17: Outline
Review
Quantify and summarize performance
  Ratios, Geometric Mean, Multiplicative Standard Deviation
F&P: Benchmarks age, disks fail,1 point fail danger
252 Administrivia
MIPS – An ISA for Pipelining
5 stage pipelining
Structural and Data Hazards
Forwarding
Branch Schemes
Exceptions and Interrupts
Conclusion

## Slide 18: A "Typical" RISC ISA
32-bit fixed format instruction (3 formats)
32 32-bit GPR (R0 contains zero, DP take pair)
3-address, reg-reg arithmetic instruction
Single address mode for load/store: base + displacement
  no indirection
Simple branch conditions
Delayed branch
see: SPARC, MIPS, HP PA-Risc, DEC Alpha, IBM PowerPC,
CDC 6600, CDC 7600, Cray-1, Cray-2, Cray-3

## Slide 19: Example: MIPS (­ MIPS)
Op
31
26
0
15
16
20
21
25
Rs1
Rd
immediate
Op
31
26
0
25
Op
31
26
0
15
16
20
21
25
Rs1
Rs2
target
Rd
Opx
Register-Register
5
6
10
11
Register-Immediate
Op
31
26
0
15
16
20
21
25
Rs1
Rs2/Opx
immediate
Branch
Jump / Call

## Slide 20: Datapath vs Control
Datapath: Storage, FU, interconnect sufficient to perform the desired functions
  Inputs are Control Points
  Outputs are signals
Controller: State machine to orchestrate operation on the data path
  Based on desired function and signals
Datapath
Controller
Control Points
signals

## Slide 21: Approaching an ISA
Instruction Set Architecture
  Defines set of operations, instruction format, hardware supported data types, named storage, addressing modes, sequencing
Meaning of each instruction is described by RTL on architected registers and memory
Given technology constraints assemble adequate datapath
  Architected storage mapped to actual storage
  Function units to do all the required operations
  Possible additional storage (eg. MAR, MBR, …)
  Interconnect to move information among regs and FUs
Map each instruction to sequence of RTLs
Collate sequences into symbolic controller state transition diagram (STD)
Lower symbolic STD to control points
Implement controller

## Slide 22: 5 Steps of MIPS Datapath Figure A.2, Page A-8
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
L
M
D
ALU
MUX
Memory
Reg File
MUX
MUX
Data
Memory
MUX
Sign
Extend
4
Adder
Zero?
Next SEQ PC
Address
Next PC
WB Data
Inst
RD
RS1
RS2
Imm
IR <= mem[PC];
PC <= PC + 4
Reg[IRrd] <= Reg[IRrs] opIRop Reg[IRrt]

## Slide 23: 5 Steps of MIPS Datapath Figure A.3, Page A-9
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
MUX
Data
Memory
MUX
Sign
Extend
Zero?
IF/ID
ID/EX
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
Next SEQ PC
RD
RD
RD
WB Data
Next PC
Address
RS1
RS2
Imm
MUX
IR <= mem[PC];
PC <= PC + 4
A <= Reg[IRrs];
B <= Reg[IRrt]
rslt <= A opIRop B
Reg[IRrd] <= WB
WB <= rslt

## Slide 24: Inst. Set Processor Controller
IR <= mem[PC];
PC <= PC + 4
A <= Reg[IRrs];
B <= Reg[IRrt]
r <= A opIRop B
Reg[IRrd] <= WB
WB <= r
Ifetch
opFetch-DCD
PC <= IRjaddr
if bop(A,b)
PC <= PC+IRim
br
jmp
RR
r <= A opIRop IRim
Reg[IRrd] <= WB
WB <= r
RI
r <= A + IRim
WB <= Mem[r]
Reg[IRrd] <= WB
LD
ST
JSR
JR

## Slide 25: 5 Steps of MIPS Datapath Figure A.3, Page A-9
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
MUX
Data
Memory
MUX
Sign
Extend
Zero?
IF/ID
ID/EX
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
Next SEQ PC
RD
RD
RD
WB Data
Data stationary control
  local decode for each instruction phase / pipeline stage
Next PC
Address
RS1
RS2
Imm
MUX

## Slide 26: Visualizing Pipelining Figure A.2, Page A-8
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5

## Slide 27: Pipelining is not quite that easy!
Limits to pipelining: Hazards prevent next instruction from executing during its designated clock cycle
  Structural hazards: HW cannot support this combination of instructions (single person to fold and put clothes away)
  Data hazards: Instruction depends on result of prior instruction still in the pipeline (missing sock)
  Control hazards: Caused by delay between the fetching of instructions and decisions about changes in control flow (branches and jumps).

## Slide 28: One Memory Port/Structural Hazards Figure A.4, Page A-14
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg

## Slide 29: One Memory Port/Structural Hazards (Similar to Figure A.5, Page A-15)
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble
How do you “bubble” the pipe?

## Slide 30: Speed Up Equation for Pipelining
For simple RISC pipeline, CPI = 1:

## Slide 31: Example: Dual-port vs. Single-port
Machine A: Dual ported memory (“Harvard Architecture”)
Machine B: Single ported memory, but its pipelined implementation has a 1.05 times faster clock rate
Ideal CPI = 1 for both
Loads are 40% of instructions executed
SpeedUpA = Pipeline Depth/(1 + 0) x (clockunpipe/clockpipe)
= Pipeline Depth
SpeedUpB = Pipeline Depth/(1 + 0.4 x 1) x (clockunpipe/(clockunpipe / 1.05)
= (Pipeline Depth/1.4) x 1.05
= 0.75 x Pipeline Depth
SpeedUpA / SpeedUpB = Pipeline Depth/(0.75 x Pipeline Depth) = 1.33
Machine A is 1.33 times faster

## Slide 32: Data Hazard on R1 Figure A.6, Page A-17
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB

## Slide 33: Three Generic Data Hazards
Read After Write (RAW) InstrJ tries to read operand before InstrI writes it
Caused by a “Dependence” (in compiler nomenclature). This hazard results from an actual need for communication.
I: add r1,r2,r3
J: sub r4,r1,r3

## Slide 34: Three Generic Data Hazards
Write After Read (WAR) InstrJ writes operand before InstrI reads it
Called an “anti-dependence” by compiler writers. This results from reuse of the name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Reads are always in stage 2, and
  Writes are always in stage 5
I: sub r4,r1,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 35: Three Generic Data Hazards
Write After Write (WAW) InstrJ writes operand before InstrI writes it.
Called an “output dependence” by compiler writers This also results from the reuse of name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Writes are always in stage 5
Will see WAR and WAW in more complicated pipes
I: sub r1,r4,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 36: Forwarding to Avoid Data Hazard Figure A.7, Page A-19
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 37: HW Change for Forwarding Figure A.23, Page A-37
MEM/WR
ID/EX
EX/MEM
Data
Memory
ALU
mux
mux
Registers
NextPC
Immediate
mux
What circuit detects and resolves this hazard?

## Slide 38: Forwarding to Avoid LW-SW Data Hazard Figure A.8, Page A-20
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
lw r4, 0(r1)
sw r4,12(r1)
or r8,r6,r9
xor r10,r9,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 39: Data Hazard Even with Forwarding Figure A.9, Page A-21
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Notes: MIPS actutally didn’t interlecok: MPU without Interlocked Pipelined Stages

## Slide 40: Data Hazard Even with Forwarding (Similar to Figure A.10, Page A-21)
Time (clock cycles)
or r8,r1,r9
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
Reg
ALU
DMem
Ifetch
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Ifetch
ALU
DMem
Reg
Bubble
Reg
Ifetch
ALU
DMem
Bubble
Reg
How is this detected?

## Slide 41: Software Scheduling to Avoid Load Hazards
Try producing fast code for
a = b + c;
d = e – f;
assuming a, b, c, d ,e, and f in memory.
Slow code:
LW Rb,b
LW Rc,c
ADD Ra,Rb,Rc
SW a,Ra
LW Re,e
LW Rf,f
SUB Rd,Re,Rf
SW d,Rd
Fast code:
LW Rb,b
LW Rc,c
LW Re,e
ADD Ra,Rb,Rc
LW Rf,f
SW a,Ra
SUB Rd,Re,Rf
SW d,Rd
Compiler optimizes for performance. Hardware checks for safety.

## Slide 42: Outline
Review
Quantify and summarize performance
  Ratios, Geometric Mean, Multiplicative Standard Deviation
F&P: Benchmarks age, disks fail,1 point fail danger
252 Administrivia
MIPS – An ISA for Pipelining
5 stage pipelining
Structural and Data Hazards
Forwarding
Branch Schemes
Exceptions and Interrupts
Conclusion

## Slide 43: Control Hazard on Branches Three Stage Stall
10: beq r1,r3,36
14: and r2,r3,r5
18: or r6,r1,r7
22: add r8,r1,r9
36: xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
What do you do with the 3 instructions in between?
How do you do it?
Where is the “commit”?

## Slide 44: Branch Stall Impact
If CPI = 1, 30% branch, Stall 3 cycles => new CPI = 1.9!
Two part solution:
  Determine branch taken or not sooner, AND
  Compute taken branch address earlier
MIPS branch tests if register = 0 or  0
MIPS Solution:
  Move Zero test to ID/RF stage
  Adder to calculate new PC in ID/RF stage
  1 clock cycle penalty for branch versus 3

## Slide 45: Pipelined MIPS Datapath Figure A.24, page A-38
Adder
IF/ID
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
Data
Memory
MUX
Sign
Extend
Zero?
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
RD
RD
RD
WB Data
Interplay of instruction set design and cycle time.
Next PC
Address
RS1
RS2
Imm
MUX
ID/EX

## Slide 46: Four Branch Hazard Alternatives
#1: Stall until branch direction is clear
#2: Predict Branch Not Taken
  Execute successor instructions in sequence
  “Squash” instructions in pipeline if branch actually taken
  Advantage of late pipeline state update
  47% MIPS branches not taken on average
  PC+4 already calculated, so use it to get next instruction
#3: Predict Branch Taken
  53% MIPS branches taken on average
  But haven’t calculated branch target address in MIPS
    MIPS still incurs 1 cycle branch penalty
    Other machines: branch target known before outcome

## Slide 47: Four Branch Hazard Alternatives
#4: Delayed Branch
  Define branch to take place AFTER a following instruction
  branch instruction sequential successor1 sequential successor2 ........ sequential successorn
  branch target if taken
  1 slot delay allows proper decision and branch target address in 5 stage pipeline
  MIPS uses this
Branch delay of length n

## Slide 48: Scheduling Branch Delay Slots (Fig A.14)
A is the best choice, fills delay slot & reduces instruction count (IC)
In B, the sub instruction may need to be copied, increasing IC
In B and C, must be okay to execute sub when branch fails
add $1,$2,$3
if $2=0 then
delay slot
A. From before branch
B. From branch target
C. From fall through
add $1,$2,$3
if $1=0 then
delay slot
add $1,$2,$3
if $1=0 then
delay slot
sub $4,$5,$6
sub $4,$5,$6
becomes
becomes
becomes
if $2=0 then
add $1,$2,$3
add $1,$2,$3
if $1=0 then
sub $4,$5,$6
add $1,$2,$3
if $1=0 then
sub $4,$5,$6
Notes: <number>
<footer>
<header>
<date/time>
Limitations on delayed-branch scheduling come from 1) restrictions on the instructions that can be moved/copied into the delay slot and 2) limited ability to predict at compile time whether a branch is likely to be taken or not.
In B and C, the use of $1 prevents the add instruction from being moved to the delay slot
In B the sub may need to be copied because it could be reached by another path. B is preferred when the branch is taken with high probability (such as loop branches

## Slide 49: Delayed Branch
Compiler effectiveness for single branch delay slot:
  Fills about 60% of branch delay slots
  About 80% of instructions executed in branch delay slots useful in computation
  About 50% (60% x 80%) of slots usefully filled
Delayed Branch downside: As processor go to deeper pipelines and multiple issue, the branch delay grows and need more than one delay slot
  Delayed branching has lost popularity compared to more expensive but more flexible dynamic approaches
  Growth in available transistors has made dynamic approaches relatively cheaper

## Slide 50: Evaluating Branch Alternatives
Assume 4% unconditional branch, 6% conditional branch- untaken, 10% conditional branch-taken
Scheduling Branch CPI speedup v. speedup v. scheme penalty unpipelined stall
Stall pipeline 3 1.60 3.1 1.0
Predict taken 1 1.20 4.2 1.33
Predict not taken 1 1.14 4.4 1.40
Delayed branch 0.5 1.10 4.5 1.45

## Slide 51: Problems with Pipelining
Exception: An unusual event happens to an instruction during its execution
  Examples: divide by zero, undefined opcode
Interrupt: Hardware signal to switch the processor to a new instruction stream
  Example: a sound card interrupts when it needs more audio output samples (an audio “click” happens if it is left waiting)
Problem: It must appear that the exception or interrupt must appear between 2 instructions (Ii and Ii+1)
  The effect of all instructions up to and including Ii is totalling complete
  No effect of any instruction after Ii can take place
The interrupt (exception) handler either aborts program or restarts at instruction Ii+1

## Slide 52: Precise Exceptions in Static Pipelines
Key observation: architected state only change in memory and register write stages.

## Slide 53: And In Conclusion: Control and Pipelining
Quantify and summarize performance
  Ratios, Geometric Mean, Multiplicative Standard Deviation
F&P: Benchmarks age, disks fail,1 point fail danger
Next time: Read Appendix A, record bugs online!
Control VIA State Machines and Microprogramming
Just overlap tasks; easy if tasks are independent
Speed Up  Pipeline Depth; if ideal CPI is 1, then:
Hazards limit performance on computers:
  Structural: need more HW resources
  Data (RAW,WAR,WAW): need forwarding, compiler scheduling
  Control: delayed branch, prediction
Exceptions, Interrupts add complexity
Next time: Read Appendix C, record bugs online!