## Slide 1: EECS 252 Graduate Computer Architecture Lec 4 – Memory Hierarchy Review
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://www-inst.eecs.berkeley.edu/~cs252

## Slide 2: Review from last lecture
Quantify and summarize performance
  Ratios, Geometric Mean, Multiplicative Standard Deviation
F&P: Benchmarks age, disks fail,1 point fail danger
Control VIA State Machines and Microprogramming
Just overlap tasks; easy if tasks are independent
Speed Up  Pipeline Depth; if ideal CPI is 1, then:
Hazards limit performance on computers:
  Structural: need more HW resources
  Data (RAW,WAR,WAW): need forwarding, compiler scheduling
  Control: delayed branch, prediction
Exceptions, Interrupts add complexity

## Slide 3: Outline
Review
Redo Geomtric Mean, Standard Deviation
252 Administrivia
Memory hierarchy
Locality
Cache design
Virtual address spaces
Page table layout
TLB design options
Conclusion

## Slide 4: Example Standard Deviation: Last time
GM and multiplicative StDev of SPECfp2000 for Itanium 2
Outside 1 StDev
Itanium 2 is 2712/100 times as fast as Sun Ultra 5 (GM), & range within 1 Std. Deviation is [13.72, 53.62]

## Slide 5: Example Standard Deviation : Last time
GM and multiplicative StDev of SPECfp2000 for AMD Athlon
Outside 1 StDev
Athon is 2086/100 times as fast as Sun Ultra 5 (GM), & range within 1 Std. Deviation is [14.94, 29.11]

## Slide 6: Example Standard Deviation (3/3)
GM and StDev Itanium 2 v Athlon
Outside 1 StDev
Ratio execution times (At/It) = Ratio of SPECratios (It/At) Itanium 2 1.30X Athlon (GM), 1 St.Dev. Range [0.75,2.27]

## Slide 7: Comments on Itanium 2 and Athlon
Standard deviation for SPECRatio of 1.98 for Itanium 2 is much higher-- vs. 1.40--so results will differ more widely from the mean, and therefore are likely less predictable
SPECRatios falling within one standard deviation:
  10 of 14 benchmarks (71%) for Itanium 2
  11 of 14 benchmarks (78%) for Athlon
Thus, results are quite compatible with a lognormal distribution (expect 68% for 1 StDev)
Itanium 2 vs. Athlon St.Dev is 1.74, which is high, so less confidence in claim that Itanium 1.30 times as fast as Athlon
  Indeed, Athlon faster on 6 of 14 programs
Range is [0.75,2.27] with 11/14 inside 1 StDev (78%)

## Slide 8
Memory Hierarchy Review

## Slide 9: Since 1980, CPU has outpaced DRAM ...
CPU
60% per yr
2X in 1.5 yrs
DRAM
9% per yr
2X in 10 yrs
10
DRAM
CPU
Performance
(1/latency)
100
1000
1980
2000
1990
Year
Gap grew 50% per year
Q. How do architects address this gap?
A. Put smaller, faster “cache” memories between CPU and DRAM.
Create a “memory hierarchy”.

## Slide 10: 1977: DRAM faster than microprocessors
Apple ][ (1977)
Steve
Wozniak
Steve Jobs
CPU: 1000 ns
DRAM: 400 ns

## Slide 11: Levels of the Memory Hierarchy
CPU Registers
100s Bytes
<10s ns
Cache
K Bytes
10-100 ns
1-0.1 cents/bit
Main Memory
M Bytes
200ns- 500ns
$.0001-.00001 cents /bit
Disk
G Bytes, 10 ms (10,000,000 ns)
10 - 10 cents/bit
-5
-6
Capacity
Access Time
Cost
Tape
infinite
sec-min
10
-8
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Xfer Unit
prog./compiler
1-8 bytes
cache cntl
8-128 bytes
OS
512-4K bytes
user/operator
Mbytes
Upper Level
Lower Level
faster
Larger

## Slide 12: Memory Hierarchy: Apple iMac G5
iMac G5
1.6 GHz
07 | Reg | L1 Inst | L1 Data | L2 | DRAM | Disk
Size | 1K | 64K | 32K | 512K | 256M | 80G
Latency Cycles, Time | 1, 0.6 ns | 3, 1.9 ns | 3, 1.9 ns | 11, 6.9 ns | 88, 55 ns | 107, 12 ms
Let programs address a memory space that scales to the disk size, at a speed that is usually as fast as register access
Managed
by compiler
Managed
by hardware
Managed by OS,
hardware,
application
Goal: Illusion of large, fast, cheap memory

## Slide 13: iMac’s PowerPC 970: All caches on-chip
(1K)
Registers
512K
L2
L1 (64K Instruction)
L1 (32K Data)

## Slide 14: The Principle of Locality
The Principle of Locality:
  Program access a relatively small portion of the address space at any instant of time.
Two Different Types of Locality:
  Temporal Locality (Locality in Time): If an item is referenced, it will tend to be referenced again soon (e.g., loops, reuse)
  Spatial Locality (Locality in Space): If an item is referenced, items whose addresses are close by tend to be referenced soon (e.g., straightline code, array access)
Last 15 years, HW relied on locality for speed
It is a property of programs which is exploited in machine design.
Notes: The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
This is kind of like in real life, we all have a lot of friends. But at any given time most of us can only keep in touch with a small group of them.
There are two different types of locality: Temporal and Spatial. Temporal locality is the locality in time which says if an item is referenced, it will tend to be referenced again soon.
This is like saying if you just talk to one of your friends, it is likely that you will talk to him or her again soon.
This makes sense. For example, if you just have lunch with a friend, you may say, let’s go to the ball game this Sunday. So you will talk to him again soon.
Spatial locality is the locality in space. It says if an item is referenced, items whose addresses are close by tend to be referenced soon.
Once again, using our analogy. We can usually divide our friends into groups. Like friends from high school, friends from work, friends from home.
Let’s say you just talk to one of your friends from high school and she may say something like: “So did you hear so and so just won the lottery.”
You probably will say NO, I better give him a call and find out more.
So this is an example of spatial locality. You just talked to a friend from your high school days. As a result, you end up talking to another high school friend. Or at least in this case, you hope he still remember you are his friend.
+3 = 10 min. (X:50)

## Slide 15: Programs with locality cache well ...
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)
Spatial
Locality
Temporal
Locality
Bad locality behavior

## Slide 16: Memory Hierarchy: Terminology
Hit: data appears in some block in the upper level (example: Block X)
  Hit Rate: the fraction of memory access found in the upper level
  Hit Time: Time to access the upper level which consists of
    RAM access time + Time to determine hit/miss
Miss: data needs to be retrieve from a block in the lower level (Block Y)
  Miss Rate = 1 - (Hit Rate)
  Miss Penalty: Time to replace a block in the upper level +
    Time to deliver the block the processor
Hit Time << Miss Penalty (500 instructions on 21264!)
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Blk X
Blk Y
Notes: A HIT is when the data the processor wants to access is found in the upper level (Blk X).
The fraction of the memory access that are HIT is defined as HIT rate.
HIT Time is the time to access the Upper Level where the data is found (X). It consists of:
(a) Time to access this level.
(b) AND the time to determine if this is a Hit or Miss.
If the data the processor wants cannot be found in the Upper level. Then we have a miss and we need to retrieve the data (Blk Y) from the lower level.
By definition (definition of Hit: Fraction), the miss rate is just 1 minus the hit rate.
This miss penalty also consists of two parts:
(a) The time it takes to replace a block (Blk Y to BlkX) in the upper level.
(b) And then the time it takes to deliver this new block to the processor.
It is very important that your Hit Time to be much much smaller than your miss penalty. Otherwise, there will be no reason to build a memory hierarchy.
+2 = 14 min. (X:54)

## Slide 17: CS252: Administrivia
Instructor: Prof. David Patterson
Office: 635 Soda Hall, pattrsn@eecs, Office Hours: Tue 4-5
(or by appt. Contact Cecilia Pracher; cpracher@eecs)
T. A: Archana Ganapathi, archanag@eecs
Class: M/W, 11:00 - 12:30pm 203 McLaughlin (and online)
Text: Computer Architecture: A Quantitative Approach, 4th Edition (Oct, 2006), Beta, distributed free provided report errors
Wiki page : vlsi.cs.berkeley.edu/cs252-s06
Wednesday 2/1: Finish review + Review project topics + Prerequisite Quiz
  Example: Prerequisite Quiz is online
Computers in the News: State of the Union
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 18: 4 Papers
Mon 2/6: Great ISA debate (4 papers)
1. Amdahl, Blaauw, and Brooks, “Architecture of the IBM System/360.” IBM Journal of Research and Development, 8(2):87-101, April 1964.
2. Lonergan and King, “Design of the B 5000 system.” Datamation, vol. 7, no. 5, pp. 28-32, May, 1961.
3. Patterson and Ditzel, “The case for the reduced instruction set computer.” Computer Architecture News, October 1980.
4. Clark and Strecker, “Comments on ‘the case for the reduced instruction set computer’," Computer Architecture News, October 1980.
Papers and issues to address per paper on wiki
Read and Send your comments ( 1-2 pages)
  Email comments to archanag@cs AND pattrsn@cs by Friday 10PM
  We’ll publish all comments anonymously on wiki by Saturday
  Read, reflect, and comment before class on Monday
  Live debate in class

## Slide 19: Cache Measures
Hit rate: fraction found in that level
  So high that usually talk about Miss rate
  Miss rate fallacy: as MIPS to CPU performance, miss rate to average memory access time in memory
Average memory-access time = Hit time + Miss rate x Miss penalty (ns or clocks)
Miss penalty: time to replace a block from lower level, including time to replace in CPU
  access time: time to lower level
  = f(latency to lower level)
  transfer time: time to transfer block
  =f(BW between upper & lower levels)

## Slide 20: 4 Questions for Memory Hierarchy
Q1: Where can a block be placed in the upper level? (Block placement)
Q2: How is a block found if it is in the upper level? (Block identification)
Q3: Which block should be replaced on a miss? (Block replacement)
Q4: What happens on a write? (Write strategy)

## Slide 21: Q1: Where can a block be placed in the upper level?
Block 12 placed in 8 block cache:
  Fully associative, direct mapped, 2-way set associative
  S.A. Mapping = Block Number Modulo Number Sets
Cache
01234567
01234567
01234567
Memory
1111111111222222222233
01234567890123456789012345678901
Full Mapped
Direct Mapped
(12 mod 8) = 4
2-Way Assoc
(12 mod 4) = 0

## Slide 22: Q2: How is a block found if it is in the upper level?
Tag on each block
  No need to check index or block offset
Increasing associativity shrinks index, expands tag
Block
Offset
Block Address
Index
Tag

## Slide 23: Q3: Which block should be replaced on a miss?
Easy for Direct Mapped
Set Associative or Fully Associative:
  Random
  LRU (Least Recently Used)
Assoc: 2-way 4-way 8-way
Size LRU Ran LRU Ran LRU Ran
16 KB 5.2% 5.7% 4.7% 5.3% 4.4% 5.0%
64 KB 1.9% 2.0% 1.5% 1.7% 1.4% 1.5%
256 KB 1.15% 1.17% 1.13% 1.13% 1.12% 1.12%

## Slide 24: Q3: After a cache read miss, if there are no empty cache blocks, which block should be removed from the cache?
A randomly chosen block?
Easy to implement, how
well does it work?
The Least Recently Used (LRU) block? Appealing,
but hard to implement for high associativity
Miss Rate for 2-way Set Associative Cache |  |  | 
 | Size | Random | LRU
 | 16 KB | 5.7% | 5.2%
 | 64 KB | 2.0% | 1.9%
 | 256 KB | 1.17% | 1.15%
Also,
try
other
LRU
approx.

## Slide 25: Q4: What happens on a write?
 | Write-Through | Write-Back
Policy | Data written to cache block also written to lower-level memory | Write data only to the cache Update lower level when a block falls out of the cache
Debug | Easy | Hard
Do read misses produce writes? | No | Yes
Do repeated writes make it to lower level? | Yes | No
Additional option -- let writes to an un-cached address allocate a new cache line (“write-allocate”).

## Slide 26: Write Buffers for Write-Through Caches
Q. Why a write buffer ?
Processor
Cache
Write Buffer
Lower Level Memory
Holds data awaiting write-through to
lower level memory
A. So CPU doesn’t stall
Q. Why a buffer, why not just one register ?
A. Bursts of writes are
common.
Q. Are Read After Write (RAW) hazards an issue for write buffer?
A. Yes! Drain buffer before next read, or send read 1st after check write buffers.

## Slide 27: 5 Basic Cache Optimizations
Reducing Miss Rate
Larger Block size (compulsory misses)
Larger Cache size (capacity misses)
Higher Associativity (conflict misses)
Reducing Miss Penalty
Multilevel Caches
Reducing hit time
Giving Reads Priority over Writes
  E.g., Read complete before earlier writes in write buffer

## Slide 28: Outline
Review
Redo Geomtric Mean, Standard Deviation
252 Administrivia
Memory hierarchy
Locality
Cache design
Virtual address spaces
Page table layout
TLB design options
Conclusion

## Slide 29: The Limits of Physical Addressing
CPU
Memory
A0-A31
A0-A31
D0-D31
D0-D31
“Physical addresses” of memory locations
Data
All programs share one address space:
The physical address space
No way to prevent a program from accessing any machine resource
Machine language programs must be
aware of the machine organization

## Slide 30: Solution: Add a Layer of Indirection
CPU
Memory
A0-A31
A0-A31
D0-D31
D0-D31
Data
User programs run in an standardized
virtual address space
Address Translation hardware
managed by the operating system (OS)
maps virtual address to physical memory
“Physical Addresses”
Address
Translation
Virtual
Physical
“Virtual Addresses”
Hardware supports “modern” OS features:
Protection, Translation, Sharing

## Slide 31: Three Advantages of Virtual Memory
Translation:
  Program can be given consistent view of memory, even though physical memory is scrambled
  Makes multithreading reasonable (now used a lot!)
  Only the most important part of program (“Working Set”) must be in physical memory.
  Contiguous structures (like stacks) use only as much physical memory as necessary yet still grow later.
Protection:
  Different threads (or processes) protected from each other.
  Different pages can be given special behavior
    (Read Only, Invisible to user programs, etc).
  Kernel data protected from User programs
  Very important for protection from malicious programs
Sharing:
  Can map same physical page to multiple users (“Shared memory”)

## Slide 32: Page tables encode virtual address spaces
A machine usually supports
pages of a few sizes
(MIPS R4000):
A valid page table entry codes physical memory “frame” address for the page
A virtual address space
is divided into blocks
of memory called pages
Physical
Address Space
Virtual
Address Space
frame
frame
frame
frame

## Slide 33: Page tables encode virtual address spaces
A machine usually supports
pages of a few sizes
(MIPS R4000):
Physical
Memory Space
A valid page table entry codes physical memory “frame” address for the page
A virtual address space
is divided into blocks
of memory called pages
frame
frame
frame
frame
A page table is indexed by a
virtual address
virtual address
Page Table
OS manages the page table for each ASID

## Slide 34: Details of Page Table
Physical
Memory Space
Page table maps virtual page numbers to physical frames (“PTE” = Page Table Entry)
Virtual memory => treat memory  cache for disk
Virtual Address
Page Table
index
into
page
table
Page Table
Base Reg
V
Access
Rights
PA
V page no.
offset
12
table located
in physical
memory
P page no.
offset
12
Physical Address
frame
frame
frame
frame
virtual address
Page Table

## Slide 35: Page tables may not fit in memory!
A table for 4KB pages for a 32-bit address space has 1M entries
Each process needs its own address space!
P1 index
P2 index
Page Offset
31
12
11
0
21
22
32 bit virtual address
Top-level table wired in main memory
Subset of 1024 second-level tables in main memory; rest are on disk or unallocated
Two-level Page Tables

## Slide 36: VM and Disk: Page replacement policy
...
Page Table
1 0
used
dirty
1 0
0 1
1 1
0 0
Set of all pages
in Memory
Tail pointer:
Clear the used
bit in the
page table
Head pointer
Place pages on free list if used bit
is still clear.
Schedule pages with dirty bit set to
be written to disk.
Freelist
Free Pages
Dirty bit: page written.
Used bit: set to
1 on any reference
Architect’s role: support setting dirty and used bits

## Slide 37
TLB Design Concepts

## Slide 38: MIPS Address Translation: How does it work?
“Physical Addresses”
CPU
Memory
A0-A31
A0-A31
D0-D31
D0-D31
Data
TLB also contains
protection bits for virtual address
Virtual
Physical
“Virtual Addresses”
Translation
Look-Aside
Buffer
(TLB)
Translation Look-Aside Buffer (TLB)
A small fully-associative cache of
mappings from virtual to physical addresses
Fast common case: Virtual address is in TLB,
process has permission to read/write it.
What is the table of
mappings that it caches?

## Slide 39
V=0 pages either reside on disk or have not yet been allocated.
OS handles V=0
“Page fault”
Physical and virtual pages must be the same size!
The TLB caches page table entries
TLB
Page Table
2
0
1
3
virtual address
page
off
2
frame
page
2
5
0
physical address
page
off
TLB caches page table entries.
MIPS handles TLB misses in software (random replacement). Other machines use hardware.
for ASID
Physical
frame
address

## Slide 40: Can TLB and caching be overlapped?
 |  |  | Index |  | Byte Select |  |  | 
 | Cache Tags |  |  |  |  |  | Cache Data | 
 |  |  |  |  |  |  |  | Cache Block
 |  |  |  |  |  |  |  | Cache Block
Data out
Virtual Page Number | Page Offset
Translation
Look-Aside
Buffer
(TLB)
Virtual
Physical
=
Hit
Cache Tag
This works, but ...
Q. What is the downside?
A. Inflexibility. Size of cache limited by page size.

## Slide 41: Problems With Overlapped TLB Access
Overlapped access only works as long as the address bits used to
index into the cache do not change as the result of VA translation
This usually limits things to small caches, large page sizes, or high
n-way set associative caches if you want a large cache
Example: suppose everything the same except that the cache is
increased to 8 K bytes instead of 4 K:
11
2
00
virt page #
disp
20
12
cache
index
This bit is changed
by VA translation, but
is needed for cache
lookup
Solutions:
go to 8K byte page sizes;
go to 2 way set associative cache; or
SW guarantee VA[13]=PA[13]
1K
4
4
10
2 way set assoc cache

## Slide 42: Use virtual addresses for cache?
“Physical Addresses”
CPU
Main Memory
A0-A31
A0-A31
D0-D31
D0-D31
Only use TLB on a cache miss !
Translation
Look-Aside
Buffer
(TLB)
Virtual
Physical
“Virtual Addresses”
A. Synonym problem. If two address spaces share a physical frame, data may be in cache twice. Maintaining consistency is a nightmare.
Cache
Virtual
D0-D31
Downside: a subtle, fatal problem. What is it?

## Slide 43: Summary #1/3: The Cache Design Space
Several interacting dimensions
  cache size
  block size
  associativity
  replacement policy
  write-through vs write-back
  write allocation
The optimal choice is a compromise
  depends on access characteristics
    workload
    use (I-cache, D-cache, TLB)
  depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 44: Summary #2/3: Caches
The Principle of Locality:
  Program access a relatively small portion of the address space at any instant of time.
    Temporal Locality: Locality in Time
    Spatial Locality: Locality in Space
Three Major Categories of Cache Misses:
  Compulsory Misses: sad facts of life. Example: cold start misses.
  Capacity Misses: increase cache size
  Conflict Misses: increase cache size and/or associativity. Nightmare Scenario: ping pong effect!
Write Policy: Write Through vs. Write Back
Today CPU time is a function of (ops, cache misses) vs. just f(ops): affects Compilers, Data structures, and Algorithms

## Slide 45: Summary #3/3: TLB, Virtual Memory
Page tables map virtual address to physical address
TLBs are important for fast translation
TLB misses are significant in processor performance
  funny times, as most systems can’t access all of 2nd level cache without TLB misses!
Caches, TLBs, Virtual Memory all understood by examining how they deal with 4 questions: 1) Where can block be placed? 2) How is block found? 3) What block is replaced on miss? 4) How are writes handled?
Today VM allows many processes to share single memory without having to swap all processes to disk; today VM protection is more important than memory hierarchy benefits, but computers insecure
Prepare for debate + quiz on Wednesday
Notes: Let’s do a short review of what you learned last time.
Virtual memory was originally invented as another level of memory hierarchy such that programers, faced with main memory much smaller than their programs, do not have to manage the loading and unloading portions of their program in and out of memory.
It was a controversial proposal at that time because very few programers believed software can manage the limited amount of memory resource as well as human.
This all changed as DRAM size grows exponentially in the last few decades.
Nowadays, the main function of virtual memory is to allow multiple processes to share the same main memory so we don’t have to swap all the non-active processes to disk.
Consequently, the most important function of virtual memory these days is to provide memory protection.
The most common technique, but we like to emphasis not the only technique, to translate virtual memory address to physical memory address is to use a page table.
TLB, or translation lookaside buffer, is one of the most popular hardware techniques to reduce address translation time.
Since TLB is so effective in reducing the address translation time, what this means is that TLB misses will have a significant negative impact on processor performance.
+3 = 3 min. (X:43)