## Slide 1: EECS 252 Graduate Computer Architecture Lec 5 – Projects + Prerequisite Quiz
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://www-inst.eecs.berkeley.edu/~cs252

## Slide 2: Review from last lecture #1/3: The Cache Design Space
Several interacting dimensions
  cache size
  block size
  associativity
  replacement policy
  write-through vs write-back
  write allocation
The optimal choice is a compromise
  depends on access characteristics
    workload
    use (I-cache, D-cache, TLB)
  depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 3: Review from last lecture #2/3: Caches
The Principle of Locality:
  Program access a relatively small portion of the address space at any instant of time.
    Temporal Locality: Locality in Time
    Spatial Locality: Locality in Space
Three Major Categories of Cache Misses:
  Compulsory Misses: sad facts of life. Example: cold start misses.
  Capacity Misses: increase cache size
  Conflict Misses: increase cache size and/or associativity. Nightmare Scenario: ping pong effect!
Write Policy: Write Through vs. Write Back
Today CPU time is a function of (ops, cache misses) vs. just f(ops): affects Compilers, Data structures, and Algorithms

## Slide 4: Review from last lecture #3/3: TLB, Virtual Memory
Page tables map virtual address to physical address
TLBs are important for fast translation
TLB misses are significant in processor performance
  funny times, as most systems can’t access all of 2nd level cache without TLB misses!
Caches, TLBs, Virtual Memory all understood by examining how they deal with 4 questions: 1) Where can block be placed? 2) How is block found? 3) What block is replaced on miss? 4) How are writes handled?
Today VM allows many processes to share single memory without having to swap all processes to disk; today VM protection is more important than memory hierarchy benefits, but computers insecure
Notes: Let’s do a short review of what you learned last time.
Virtual memory was originally invented as another level of memory hierarchy such that programers, faced with main memory much smaller than their programs, do not have to manage the loading and unloading portions of their program in and out of memory.
It was a controversial proposal at that time because very few programers believed software can manage the limited amount of memory resource as well as human.
This all changed as DRAM size grows exponentially in the last few decades.
Nowadays, the main function of virtual memory is to allow multiple processes to share the same main memory so we don’t have to swap all the non-active processes to disk.
Consequently, the most important function of virtual memory these days is to provide memory protection.
The most common technique, but we like to emphasis not the only technique, to translate virtual memory address to physical memory address is to use a page table.
TLB, or translation lookaside buffer, is one of the most popular hardware techniques to reduce address translation time.
Since TLB is so effective in reducing the address translation time, what this means is that TLB misses will have a significant negative impact on processor performance.
+3 = 3 min. (X:43)

## Slide 5: Problems with Sea Change
Algorithms, Programming Languages, Compilers, Operating Systems, Architectures, Libraries, … not ready for 1000 CPUs / chip
Software people don’t start working hard until hardware arrives
  3 months after HW arrives, SW people list everything that must be fixed, then we all wait 4 years for next iteration of HW/SW
How get 1000 CPU systems in hands of researchers to innovate in timely fashion on in algorithms, compilers, languages, OS, architectures, … ?
Skip the waiting years between HW/SW iterations?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Build Academic MPP from FPGAs
As ~ 25 CPUs fit in Field Programmable Gate Array, 1000-CPU system from ~ 40 FPGAs?
  16 32-bit simple “soft core” RISC at 150MHz in 2004 (Virtex-II)
  FPGA generations every 1.5 yrs; ~2X CPUs, ~1.2X clock rate
HW research community does logic design (“gate shareware”) to create out-of-the-box, MPP
  E.g., 1000 processor, standard ISA binary-compatible, 64-bit, cache-coherent supercomputer @ 200 MHz/CPU in 2007
  RAMPants: Arvind (MIT), Krste Asanovíc (MIT), Derek Chiou (Texas), James Hoe (CMU), Christos Kozyrakis (Stanford), Shih-Lien Lu (Intel), Mark Oskin (Washington), David Patterson (Berkeley, Co-PI), Jan Rabaey (Berkeley), and John Wawrzynek (Berkeley, PI)
“Research Accelerator for Multiple Processors”
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Characteristics of Ideal Academic CS Research Supercomputer?
Scale – Hard problems at 1000 CPUs
Cheap – 2006 funding of academic research
Cheap to operate, Small, Low Power – $ again
Community – share SW, training, ideas, …
Simplifies debugging – high SW churn rate
Reconfigurable – test many parameters, imitate many ISAs, many organizations, …
Credible – results translate to real computers
Performance – run real OS and full apps, results overnight

## Slide 8: Why RAMP Good for Research MPP?
 | SMP | Cluster | Simulate | RAMP
Scalability (1k CPUs) | C | A | A | A
Cost (1k CPUs) | F ($40M) | C ($2-3M) | A+ ($0M) | A ($0.1-0.2M)
Cost of ownership | A | D | A | A
Power/Space (kilowatts, racks) | D (120 kw, 12 racks) | D (120 kw, 12 racks) | A+ (.1 kw, 0.1 racks) | A (1.5 kw, 0.3 racks)
Community | D | A | A | A
Observability | D | C | A+ | A+
Reproducibility | B | D | A+ | A+
Reconfigurability | D | C | A+ | A+
Credibility | A+ | A+ | F | A
Perform. (clock) | A (2 GHz) | A (3 GHz) | F (0 GHz) | C (0.1-.2 GHz)
GPA | C | B- | B | A-
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: RAMP 1 Hardware
Completed Dec. 2004 (14x17 inch 22-layer PCB)
Module:
  5 Virtex II FPGAs, 18 banks DDR2-400 memory, 20 10GigE conn.
  Administration/ maintenance ports:
    10/100 Enet
    HDMI/DVI
    USB
  ~$4K in Bill of Materials (w/o FPGAs or DRAM)
  BEE2: Berkeley Emulation Engine 2
  By John Wawrzynek and Bob Brodersen with students Chen Chang and Pierre Droz
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10
Multiple Module RAMP 1 Systems
8 compute modules (plus power supplies) in 8U rack mount chassis
2U single module tray for developers
Many topologies possible
Disk storage: via disk emulator + Network Attached Storage
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Quick Sanity Check
BEE2 uses old FPGAs (Virtex II), 4 banks DDR2-400/cpu
16 32-bit Microblazes per Virtex II FPGA, 0.75 MB memory for caches
  32 KB direct mapped Icache, 16 KB direct mapped Dcache
Assume 150 MHz, CPI is 1.5 (4-stage pipe)
  I$ Miss rate is 0.5% for SPECint2000
  D$ Miss rate is 2.8% for SPECint2000, 40% Loads/stores
BW need/CPU = 150/1.5*4B*(0.5% + 40%*2.8%) = 6.4 MB/sec
BW need/FPGA = 16*6.4 = 100 MB/s
Memory BW/FPGA = 4*200 MHz*2*8B = 12,800 MB/s
Plenty of room for tracing, …

## Slide 12: RAMP Development Plan
Distribute systems internally for RAMP 1 development
  Xilinx agreed to pay for production of a set of modules for initial contributing developers and first full RAMP system
  Others could be available if can recover costs
Release publicly available out-of-the-box MPP emulator
  Based on standard ISA (IBM Power, Sun SPARC, …) for binary compatibility
  Complete OS/libraries
  Locally modify RAMP as desired
Design next generation platform for RAMP 2
  Base on 65nm FPGAs (2 generations later than Virtex-II)
  Pending results from RAMP 1, Xilinx will cover hardware costs for initial set of RAMP 2 machines
  Find 3rd party to build and distribute systems (at near-cost), open source RAMP gateware and software
  Hope RAMP 3, 4, … self-sustaining
NSF/CRI proposal pending to help support effort
  2 full-time staff (one HW/gateware, one OS/software)
  Look for grad student support at 6 RAMP universities from industrial donations
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: RAMP Milestones
Name | Goal | Target | CPUs | Details
Red (S.U.) | Get Started | 1Q06 | 8 PowerPC 32b hard cores | Transactional memory SMP
Blue (Cal) | Scale | 3Q06 | 1024 32b soft (Microblaze) | Cluster, MPI
White 1.0 2.0 3.0 4.0 | Features | 2Q06? 3Q06? 4Q06? 1Q07? | 64 hard PPC 128? soft 32b 64? soft 64b Multiple ISAs | Cache coherent, shared address, deterministic, debug/monitor, commercial ISA
2.0 | Sell | 2H07? | 4X ‘04 FPGA | New ’06 FPGA, new board

## Slide 14
the stone soup of architecture research platforms
I/O
Patterson
Monitoring
Kozyrakis
Net Switch
Oskin
Coherence
Hoe
Cache
Asanovic
PPC
Arvind
x86
Lu
Glue-support
Chiou
Hardware
Wawrzynek
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Gateware Design Framework
Insight: almost every large building block fits inside FPGA today
  what doesn’t is between chips in real design
Supports both cycle-accurate emulation of detailed parameterized machine models and rapid functional-only emulations
Carefully counts for Target Clock Cycles
Units in any hardware design language (will work with Verilog, VHDL, BlueSpec, C, ...)
RAMP Design Language (RDL) to describe plumbing to connect units in
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Gateware Design Framework
Design composed of units that send messages over channels via ports
Units (10,000 + gates)
  CPU + L1 cache, DRAM controller….
Channels (~ FIFO)
  Lossless, point-to-point, unidirectional, in-order message delivery…
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: RAMP FAQ
Q: How will FPGA clock rate improve?
A1: 1.1X to 1.3X / 18 months
  Note that clock rate now going up slowly on desktop
A2: Goal for RAMP is system emulation, not to be the real system
  Hence, value accurate accounting of target clock cycles, parameterized design (Memory BW, network BW, …), monitor, debug vs. clock rate
  Goal is just fast enough to emulate OS, app in parallel

## Slide 18: RAMP FAQ
Q: What about power, cost, space in RAMP?
A: Using very slow clock rate, very simple CPUs in a very large FPGA (RAMP blue)
  1.5 watts per computer
  $100-$200 per computer
  5 cubic inches per computer

## Slide 19: RAMP FAQ
Q: But how can lots of researchers get RAMPs?
A1: Official plan is RAMP 2.0 available for purchase at low margin from 3rd party vendor
A2: Single board RAMP 2.0 still interesting + FPGA generation 2X CPUs/18 months
  RAMP 2.0 two generations later than RAMP 1.0, so 256 simple CPUs per board?

## Slide 20: RAMP Status
ramp.eecs.berkeley.edu
Sent NSF infrastruture proposal August 2005
Biweekly teleconferences (since June 05)
IBM, Sun donating commercial ISA, simple, industrial-strength, CPU + FPU
Technical report, RAMP Design Language
RAMP 1/RDL short course/board distribution in Berkeley for 40 people @ 6 schools Jan 06
1 Day RAMP retreat with 12 industry visitors
Berkeley style retreats 6/06, 1/07, 6/07
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: RAMP uses (internal)
Internet-in-a-Box
Patterson
TCC
Kozyrakis
Dataflow
Oskin
Reliable MP
Hoe
1M-way MT
Asanovic
BlueSpec
Arvind
x86
Lu
Net-uP
Chiou
Wawrzynek
BEE
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Multiprocessing Watering Hole
Killer app: All CS Research, Ind. Advanced Development
RAMP attracts many communities to shared artifact  Cross-disciplinary interactions  Accelerate innovation in multiprocessing
RAMP as next Standard Research Platform? (e.g., VAX/BSD Unix in 1980s)
Parallel file system
Thread scheduling
Multiprocessor switch design
Fault insertion to check dependability
Data center in a box
Internet in a box
Dataflow language/computer
Security enhancements
Router design
Compile to FPGA
Parallel languages
RAMP
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Supporters (wrote letters to NSF)
Gordon Bell (Microsoft)
Ivo Bolsens (Xilinx CTO)
Norm Jouppi (HP Labs)
Bill Kramer (NERSC/LBL)
Craig Mundie (MS CTO)
G. Papadopoulos (Sun CTO)
Justin Rattner (Intel CTO)
Ivan Sutherland (Sun Fellow)
Chuck Thacker (Microsoft)
Kees Vissers (Xilinx)
Doug Burger (Texas)
Bill Dally (Stanford)
Carl Ebeling (Washington)
Susan Eggers (Washington)
Steve Keckler (Texas)
Greg Morrisett (Harvard)
Scott Shenker (Berkeley)
Ion Stoica (Berkeley)
Kathy Yelick (Berkeley)
RAMP Participants: Arvind (MIT), Krste Asanovíc (MIT), Derek Chiou (Texas), James Hoe (CMU), Christos Kozyrakis (Stanford), Shih-Lien Lu (Intel), Mark Oskin (Washington), David Patterson (Berkeley), Jan Rabaey (Berkeley), and John Wawrzynek (Berkeley)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: RAMP Summary
RAMP accelerates HW/SW generations
  Trace anything, Reproduce everything, Tape out every day
  Emulate anything: Massive Multiprocessor, Distributed Computer,…
  Clone to check results (as fast in Berkeley as in Boston?)
Carpe Diem: Researchers need it ASAP
  FPGA technology is ready today, and getting better every year
  Stand on shoulders vs. toes: standardize on design framework, Berkeley effort on FPGA platforms (BEE, BEE2) by Wawrzynek et al
  Architects get to immediately aid colleagues via gateware
“Multiprocessor Research Watering Hole” ramp up research in multiprocessing via standard research platform  hasten sea change from sequential to parallel computing
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: CS 252 Projects
RAMP meetings Wednesdays 3:30-4:30
  February 1st (today) and February 8 meetings will be held in Alcove 611 (sixth floor - Soda Hall)
  February 15th - May 17th in 380 Soda Hall
  Big cluster, DP fl. Pt., Software, workload generation, DOS generation, …
Other projects from your own research?
Other ideas:
  How fast is Niagara (8 CPUs, each 4-way multithreaded); run unpublished benchmarks
  How fast is Mac on x86 binary translation?

## Slide 26: CS252: Administrivia
Instructor: Prof. David Patterson
Office: 635 Soda Hall, pattrsn@eecs, Office Hours: Tue 4-5
(or by appt. Contact Cecilia Pracher; cpracher@eecs)
T. A: Archana Ganapathi, archanag@eecs
Class: M/W, 11:00 - 12:30pm 203 McLaughlin (and online)
Text: Computer Architecture: A Quantitative Approach, 4th Edition (Oct, 2006), Beta, distributed free provided report errors
Wiki page : vlsi.cs.berkeley.edu/cs252-s06 Wed 2/1: Great ISA debate (4 papers) + 30 minute Prerequisite Quiz
1. Amdahl, Blaauw, and Brooks, “Architecture of the IBM System/360.” IBM Journal of Research and Development, 8(2):87-101, April 1964.
2. Lonergan and King, “Design of the B 5000 system.” Datamation, vol. 7, no. 5, pp. 28-32, May, 1961.
3. Patterson and Ditzel, “The case for the reduced instruction set computer.” Computer Architecture News, October 1980.
4. Clark and Strecker, “Comments on ‘the case for the reduced instruction set computer’," Computer Architecture News, October 1980.
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 27: 4 Papers
Read and Send your comments
  email comments to archanag@cs AND pattrsn@cs by Friday 10PM; posted on Wiki Saturday
Read, comment on wiki before class Monday
Be sure to address:
B5000 (1961) vs. IBM 360 (1964)
  What key different architecture decisions did they make?
    E.g., data size, floating point size, instruction size, registers, …
  Which largely survive to this day in current ISAs? In JVM?
RISC vs. CISC (1980)
  What arguments were made for and against RISC and CISC?
  Which has history settled?

## Slide 28: Computers in the News
The American Competitiveness Initiative commits $5.9 billion in FY 2007, and more than $136 billion over 10 years, to increase investments in research and development (R&D), strengthen education, and encourage entrepreneurship and innovation.
NY Times today: “In an echo of President Dwight D. Eisenhower's response after the United States was stunned by the launching of Sputnik in 1957, Mr. Bush called for initiatives to deal with a new threat: intensifying competition from countries like China and India. He proposed a substantial increase in financing for basic science research, called for training 70,000 new high school Advanced Placement teachers and recruiting 30,000 math and science professionals into the nation's classrooms.”

## Slide 29: SOTU Transcript
“And to keep America competitive, one commitment is necessary above all. We must continue to lead the world in human talent and creativity. Our greatest advantage in the world has always been our educated, hard-working, ambitious people, and we are going to keep that edge. Tonight I announce the American Competitiveness Initiative, to encourage innovation throughout our economy and to give our nation's children a firm grounding in math and science. “
  [American Competitiveness Initiative: www.whitehouse.gov/news/releases/2006/01/20060131-5.html ]

## Slide 30: SOTU Transcript
“First, I propose to double the federal commitment to the most critical basic research programs in the physical sciences over the next 10 years. This funding will support the work of America's most creative minds as they explore promising areas such as nanotechnology and supercomputing and alternative energy sources.
“Second, I propose to make permanent the research and development tax credit to encourage bolder private-sector initiative in technology. With more research in both the public and private sectors, we will improve our quality of life and ensure that America will lead the world in opportunity and innovation for decades to come.”

## Slide 31: SOTU Transcript
“Third, we need to encourage children to take more math and science and to make sure those courses are rigorous enough to compete with other nations. We've made a good start in the early grades with the No Child Left Behind Act, which is raising standards and lifting test scores across our country. Tonight I propose to train 70,000 high school teachers to lead Advanced Placement courses in math and science, bring 30,000 math and science professionals to teach in classrooms and give early help to students who struggle with math, so they have a better chance at good high-wage jobs. If we ensure that America's children succeed in life, they will ensure that America succeeds in the world.”

## Slide 32: SOTU Transcript
“Preparing our nation to compete in the world is a goal that all of us can share. I urge you to support the American Competitiveness Initiative, and together we will show the world what the American people can achieve.”