## Slide 1: EECS 252 Graduate Computer Architecture Lec 10 –Simultaneous Multithreading
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://vlsi.cs.berkeley.edu/cs252-s06

## Slide 2: Review from Last Time
Limits to ILP (power efficiency, compilers, dependencies …) seem to limit to 3 to 6 issue for practical options
Explicitly parallel (Data level parallelism or Thread level parallelism) is next step to performance
Coarse grain vs. Fine grained multihreading
  Only on big stall vs. every clock cycle
Simultaneous Multithreading if fine grained multithreading based on OOO superscalar microarchitecture
  Instead of replicating registers, reuse rename registers
Balance of ILP and TLP decided in marketplace

## Slide 3
Processor | Micro architecture | Fetch / Issue / Execute | Func-tional Units | Clock Rate (GHz) | Transis-tors, Die size | Power
Intel Pentium 4 Extreme | Speculative dynamically scheduled; deeply pipelined; SMT | 3/3/4 | 7 int. 1 FP | 3.8 | 125 M, 122 mm2 | 115 W
AMD Athlon 64 FX-57 | Speculative dynamically scheduled | 3/3/4 | 6 int. 3 FP | 2.8 | 114 M, 115 mm2 | 104 W
IBM Power5 (1 CPU only) | Speculative dynamically scheduled; SMT; 2 CPU cores/chip | 8/4/8 | 6 int. 2 FP | 1.9 | 200 M, 300 mm2 (est.) | 80W (est.)
Intel Itanium 2 | Statically scheduled VLIW-style | 6/5/11 | 9 int. 2 FP | 1.6 | 592 M, 423 mm2 | 130 W
Head to Head ILP competition

## Slide 4: Performance on SPECint2000

## Slide 5: Performance on SPECfp2000

## Slide 6: Normalized Performance: Efficiency
Rank | I tanium2 | Pen t I um4 | A t h l on | Powe r 5
Int/Trans | 4 | 2 | 1 | 3
FP/Trans | 4 | 2 | 1 | 3
Int/area | 4 | 2 | 1 | 3
FP/area | 4 | 2 | 1 | 3
Int/Watt | 4 | 3 | 1 | 2
FP/Watt | 2 | 4 | 3 | 1

## Slide 7: No Silver Bullet for ILP
No obvious over all leader in performance
The AMD Athlon leads on SPECInt performance followed by the Pentium 4, Itanium 2, and Power5
Itanium 2 and Power5, which perform similarly on SPECFP, clearly dominate the Athlon and Pentium 4 on SPECFP
Itanium 2 is the most inefficient processor both for Fl. Pt. and integer code for all but one efficiency measure (SPECFP/Watt)
Athlon and Pentium 4 both make good use of transistors and area in terms of efficiency,
IBM Power5 is the most effective user of energy on SPECFP and essentially tied on SPECINT

## Slide 8: Limits to ILP
Doubling issue rates above today’s 3-6 instructions per clock, say to 6 to 12 instructions, probably requires a processor to
  Issue 3 or 4 data memory accesses per cycle,
  Resolve 2 or 3 branches per cycle,
  Rename and access more than 20 registers per cycle, and
  Fetch 12 to 24 instructions per cycle.
Complexities of implementing these capabilities likely means sacrifices in maximum clock rate
  E.g, widest issue processor is the Itanium 2, but it also has the slowest clock rate, despite the fact that it consumes the most power!

## Slide 9: Limits to ILP
Most techniques for increasing performance increase power consumption
The key question is whether a technique is energy efficient: does it increase power consumption faster than it increases performance?
Multiple issue processors techniques all are energy inefficient:
  Issuing multiple instructions incurs some overhead in logic that grows faster than the issue rate grows
  Growing gap between peak issue rates and sustained performance
Number of transistors switching = f(peak issue rate), and performance = f( sustained rate), growing gap between peak and sustained performance  increasing energy per unit of performance

## Slide 10: Commentary
Itanium architecture does not represent a significant breakthrough in scaling ILP or in avoiding the problems of complexity and power consumption
Instead of pursuing more ILP, architects are increasingly focusing on TLP implemented with single-chip multiprocessors
In 2000, IBM announced the 1st commercial single-chip, general-purpose multiprocessor, the Power4, which contains 2 Power3 processors and an integrated L2 cache
  Since then, Sun Microsystems, AMD, and Intel have switch to a focus on single-chip multiprocessors rather than more aggressive uniprocessors.
Right balance of ILP and TLP is unclear today
  Perhaps right choice for server market, which can exploit more TLP, may differ from desktop, where single-thread performance may continue to be a primary requirement

## Slide 11: And in conclusion …
Limits to ILP (power efficiency, compilers, dependencies …) seem to limit to 3 to 6 issue for practical options
Explicitly parallel (Data level parallelism or Thread level parallelism) is next step to performance
Coarse grain vs. Fine grained multihreading
  Only on big stall vs. every clock cycle
Simultaneous Multithreading if fine grained multithreading based on OOO superscalar microarchitecture
  Instead of replicating registers, reuse rename registers
Itanium/EPIC/VLIW is not a breakthrough in ILP
Balance of ILP and TLP unclear in marketplace

## Slide 12: CS 252 Administrivia
Next Reading Assignment: Vector Appendix
Next Monday guest lecturer: Krste Asanovíc (MIT)
  Designer of 1st vector microprocessor
  Author of vector appendix for CA:AQA
  Ph.D. from Berkeley in 1998, took CS 252 in 1991
  Tenured Associate Professor at MIT
  On sabbatical at UCB this academic year
Next paper: “The CRAY-1 computer system”
  by R.M. Russell, Comm. of the ACM, January 1978
  Send comments on paper to TA by Monday 10PM
  Post on wiki and read on Tuesday, 30 minutes on Wednesday
Be sure to comment on vector vs. scalar speed, min. size vector faster than scalar loop, relative speed to other computers, clock rate, size of register state, memory size, no. functional units, and general impressions compared to today’s CPUs

## Slide 13: Today’s Discussion
“Simultaneous Multithreading: A Platform for Next-generation Processors,” Susan J. Eggers et al, IEEE Micro, 1997
What were worse options than SMT for 1B transistors?
What is the main extra hardware resource that SMT requires?
What is “Vertical” and “Horizontal” waste?
How does SMT differ from Multithreading?
What unit is the bottleneck for SMT
Notes: Superscalar or multiple superscalar
Mutiple instructions from different threads each clock cycle
2X Memory BW
MIPS R10000
8-way
Renames registers
OOO execution
8 HW contexts: per thread HW flushing
IFU is bottleneck
Fetch from 2 threads per clock
8 PCs, 2 threads

## Slide 14: Today’s Discussion (con’t)
“Simultaneous Multithreading: A Platform for Next-generation Processors,” Susan J. Eggers et al, IEEE Micro, 1997
How many instructions fetched per clock cycle? From how many threads?
How did it do priority?
What assumption made about computer organization before add SMT?
  When did they think it would ship?
  How compare to slide 3?
  What was memory hierarchy?
Notes: 8 instructions * 2 threads (2.8 fetching)
10% better than 1 thread at a time
The base implementation on which SMT was built featured 8-issue superscalar with 6 integer and 4 floating point ALUs. This CPU had 32 architectural registers, and 100 additional rename registers, and featured a 7-stage pipeline.
And this larger SMT registers require more delay to be accessed, thus two more stages added to allow two-cycle register reads/writes. However, from the result of their simulations, the effect of 2 additional stages is negligible: only 1.5% degradation in their simulation results.
It also featured a very generous cache hierarchy, consisting of a 128K L1 I-Cache and a 128K L1 D-Cache, with a 16Mbyte L2 cache.
Icount – highest priority to threads with fewest instructions to decode
Avoids supplying instrucitons to slow moving threads
Distributes instructions to the fast moving threads
Avoids starvign a threads

## Slide 15: Today’s Discussion (con’t)
“Simultaneous Multithreading: A Platform for Next-generation Processors,” Susan J. Eggers et al, IEEE Micro, 1997
What compare performance to?
For what workloads?
What performance advantages claimed?
  What was performance metric?
How compare to Wall’s ILP limit claims?
Notes: Superscalar
2 way(MP2), 4 way (MP4) multiple chip superscalar, Fine Grain MultiThreading
SPEC95 and Splash
Also parallel codes
2.3X multiprogrammed, 1.9X parallel vs. SS
1.3X for FGMT (so 2.3/1.3 for SMT)
6.1 instructions per cycle for SMT vs. 4.3 for MP2 and 4.2 for MP4
Claimed “fixed partitioning” hurt CMP (reduced renaming registers per processor)
Throughput (number of instructions per cycle until first thread terminates) seems to bias the comparison towards SMT. This is because SMT chooses which instructions to fetch by limiting the number of branches and memory accesses (i.e. possibly long latency ops) contrarily to the other models, which let each thread proceed. This dynamically adjusts SMT to perform more instructions in the beginning; but stopping the simulation after the first thread is over means that this advantage might never be compensated as slower instructions might not be executed and evaluated in performance.
A better measure might be the parallelism measure adopted in the Wall’s paper, which accounted for the time required by each operation executed.

## Slide 16: Time travel …
End of CS 252 in 2001 I told students to try to think about following architecture questions to think about in the future
Which ones can we answer 5 years later?
What do you think the answers are?

## Slide 17: 2001 252 Questions for Future [1/5]
What did IA-64/EPIC do well besides floating point programs?
  Was the only difference the 64-bit address v. 32-bit address?
  What happened to the AMD 64-bit address 80x86 proposal?
What happened on EPIC code size vs. x86?
Did Intel Oregon increase x86 performance so as to make Intel Santa Clara EPIC performance similar?

## Slide 18: 2001 252 Questions for Future [2/5]
Did Transmeta-like compiler-oriented translation survive vs. hardware translation into more efficient internal instruction set?
Did ILP limits really restrict practical machines to 4-issue, 4-commit?
Did we ever really get CPI below 1.0?
Did value prediction become practical?
Branch prediction: How accurate did it become?
  For real programs, how much better than 2 bit table?
Did Simultaneous Multithreading (SMT) exploit underutilized Dynamic Execution HW to get higher throughput at low extra cost?
  For multiprogrammed workload (servers) or for parallelized single program?

## Slide 19: 2001 252 Questions for Future [3/5]
Did VLIW become popular in embedded? What happened on code size?
Did vector become popular for media applications, or simply evolve SIMD?
Did DSP and general purpose microprocessors remain separate cultures, or did ISAs and cultures merge?
  Compiler oriented?
  Benchmark oriented?
  Library oriented?
  Saturation + 2’s complement

## Slide 20: 2001 252 Questions for Future [4/5]
Did emphasis switch from cost-performance to cost-performance-availability?
What support for improving software reliability? Security?

## Slide 21: 2001 252 Questions for Future [5/5]
1985-2000: 1000X performance
  Moore’s Law transistors/chip => Moore’s Law for Performance/MPU
Hennessy: industry been following a roadmap of ideas known in 1985 to exploit Instruction Level Parallelism to get 1.55X/year
  Caches, Pipelining, Superscalar, Branch Prediction, Out-of-order execution, …
ILP limits: To make performance progress in future need to have explicit parallelism from programmer vs. implicit parallelism of ILP exploited by compiler, HW?
Did Moore’s Law in transistors stop predicting microprocessor performance? Did it drop to old rate of 1.3X per year?
  Less because of processor-memory performance gap?