## Slide 1: EECS 252 Graduate Computer Architecture Lec 12 – Vector Wrap-up and Multiprocessor Introduction
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://vlsi.cs.berkeley.edu/cs252-s06

## Slide 2: Outline
Review
Vector Metrics, Terms
Cray 1 paper discussion
MP Motivation
SISD v. SIMD v. MIMD
Centralized vs. Distributed Memory
Challenges to Parallel Programming
Consistency, Coherency, Write Serialization
Write Invalidate Protocol
Example
Conclusion

## Slide 3: Properties of Vector Processors
Each result independent of previous result => long pipeline, compiler ensures no dependencies => high clock rate
Vector instructions access memory with known pattern => highly interleaved memory => amortize memory latency of over ­ 64 elements => no (data) caches required! (Do use instruction cache)
Reduces branches and branch problems in pipelines
Single vector instruction implies lots of work (­ loop) => fewer instruction fetches

## Slide 4: Operation & Instruction Count: RISC v. Vector Processor (from F. Quintana, U. Barcelona.)
Spec92fp Operations (Millions) Instructions (M)
Program RISC Vector R / V RISC Vector R / V
swim256 115 95 1.1x 115 0.8 142x
hydro2d 58 40 1.4x 58 0.8 71x
nasa7 69 41 1.7x 69 2.2 31x
su2cor 51 35 1.4x 51 1.8 29x
tomcatv 15 10 1.4x 15 1.3 11x
wave5 27 25 1.1x 27 7.2 4x
mdljdp2 32 52 0.6x 32 15.8 2x
Vector reduces ops by 1.2X, instructions by 20X

## Slide 5: Common Vector Metrics
R: MFLOPS rate on an infinite-length vector
  vector “speed of light”
  Real problems do not have unlimited vector lengths, and the start-up penalties encountered in real problems will be larger
  (Rn is the MFLOPS rate for a vector of length n)
N1/2: The vector length needed to reach one-half of R
  a good measure of the impact of start-up
NV: The vector length needed to make vector mode faster than scalar mode
  measures both start-up and speed of scalars relative to vectors, quality of connection of scalar unit to vector unit

## Slide 6: Vector Execution Time
Time = f(vector length, data dependicies, struct. hazards)
Initiation rate: rate that FU consumes vector elements (= number of lanes; usually 1 or 2 on Cray T-90)
Convoy: set of vector instructions that can begin execution in same clock (no struct. or data hazards)
Chime: approx. time for a vector operation
m convoys take m chimes; if each vector length is n, then they take approx. m x n clock cycles (ignores overhead; good approximization for long vectors)
4 convoys, 1 lane, VL=64
=> 4 x 64 = 256 clocks
(or 4 clocks per result)
1: LV V1,Rx ;load vector X
2: MULV V2,F0,V1 ;vector-scalar mult.
LV V3,Ry ;load vector Y
3: ADDV V4,V2,V3 ;add
4: SV Ry,V4 ;store the result

## Slide 7: Memory operations
32
Load/store operations move groups of data between registers and memory
Three types of addressing
  Unit stride
    Contiguous block of information in memory
    Fastest: always possible to optimize this
  Non-unit (constant) stride
    Harder to optimize memory system for all possible strides
    Prime number of data banks makes it easier to support different strides at full bandwidth
  Indexed (gather-scatter)
    Vector equivalent of register indirect
    Good for sparse arrays of data
    Increases number of programs that vectorize

## Slide 8: Interleaved Memory Layout
Great for unit stride:
  Contiguous elements in different DRAMs
  Startup time for vector operation is latency of single read
What about non-unit stride?
  Above good for strides that are relatively prime to 8
  Bad for: 2, 4
  Better: prime number of banks…!
Vector Processor
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Unpipelined
DRAM
Addr
Mod 8
= 0
Addr
Mod 8
= 1
Addr
Mod 8
= 2
Addr
Mod 8
= 4
Addr
Mod 8
= 5
Addr
Mod 8
= 3
Addr
Mod 8
= 6
Addr
Mod 8
= 7

## Slide 9: How to get full bandwidth for Unit Stride?
Memory system must sustain (# lanes x word) /clock
No. memory banks > memory latency to avoid stalls
  m banks  m words per memory lantecy l clocks
  if m < l, then gap in memory pipeline:
  clock: 0 … l l+1 l+2 … l+m- 1 l+m … 2 l
  word: -- … 0 1 2 … m-1 -- … m
  may have 1024 banks in SRAM
If desired throughput greater than one word per cycle
  Either more banks (start multiple requests simultaneously)
  Or wider DRAMS. Only good for unit stride or large data types
More banks/weird numbers of banks good to support more strides at full bandwidth
  can read paper on how to do prime number of banks efficiently

## Slide 10: Vectors Are Inexpensive
Scalar
N ops per cycle 2) circuitry
HP PA-8000
  4-way issue
  reorder buffer: 850K transistors
    incl. 6,720 5-bit register number comparators
Vector
N ops per cycle 2) circuitry
T0 vector micro
  24 ops per cycle
  730K transistors total
    only 23 5-bit register number comparators
  No floating point
Notes: 39

## Slide 11: Vectors Lower Power
Vector
One inst fetch, decode, dispatch per vector
Structured register accesses
Smaller code for high performance, less power in instruction cache misses
Bypass cache
One TLB lookup per group of loads or stores
Move only necessary data across chip boundary
Single-issue Scalar
One instruction fetch, decode, dispatch per operation
Arbitrary register accesses, adds area and power
Loop unrolling and software pipelining for high performance increases instruction cache footprint
All data passes through cache; waste power if no temporal locality
One TLB lookup per load or store
Off-chip access in whole cache lines
Notes: 41

## Slide 12: Superscalar Energy Efficiency Even Worse
Vector
Control logic grows linearly with issue width
Vector unit switches off when not in use
Vector instructions expose parallelism without speculation
Software control of speculation when desired:
  Whether to use vector mask or compress/expand for conditionals
Superscalar
Control logic grows quadratically with issue width
Control logic consumes energy regardless of available parallelism
Speculation to increase visible parallelism wastes energy
Notes: 42

## Slide 13: Vector Applications
Limited to scientific computing?
Multimedia Processing (compress., graphics, audio synth, image proc.)
Standard benchmark kernels (Matrix Multiply, FFT, Convolution, Sort)
Lossy Compression (JPEG, MPEG video and audio)
Lossless Compression (Zero removal, RLE, Differencing, LZW)
Cryptography (RSA, DES/IDEA, SHA/MD5)
Speech and handwriting recognition
Operating systems/Networking (memcpy, memset, parity, checksum)
Databases (hash/join, data mining, image/video serving)
Language run-time support (stdlib, garbage collection)
even SPECint95
Notes: 43

## Slide 14: Older Vector Machines
Machine Year Clock Regs Elements FUs LSUs
Cray 1 1976 80 MHz 8 64 6 1
Cray XMP 1983 120 MHz 8 64 8 2 L, 1 S
Cray YMP 1988 166 MHz 8 64 8 2 L, 1 S
Cray C-90 1991 240 MHz 8 128 8 4
Cray T-90 1996 455 MHz 8 128 8 4
Conv. C-1 1984 10 MHz 8 128 4 1
Conv. C-4 1994 133 MHz 16 128 3 1
Fuj. VP200 1982 133 MHz 8-256 32-1024 3 2
Fuj. VP300 1996 100 MHz 8-256 32-1024 3 2
NEC SX/2 1984 160 MHz 8+8K 256+var 16 8
NEC SX/3 1995 400 MHz 8+8K 256+var 16 8
Notes: Cray 1; fastest scalar computer + 1st commercially successful vector computer, offered another 10X
6600 1st scoreboard
Cray XMP: 3 LSUs, Multiprocessor 4 way (not by Cray)
=> YMP, C-90, T-90; 2X processors, 1.5X clock
Cray 2 went to DRAM to get more memory, not so great
Like parallel teams as Intel (486, PPro, Pentium, next one)
Japan
Fujitsu, vary number of registers elements (8x1024 or 32x256)
NEC, 8x256 + 8K of varying elements

## Slide 15: Newer Vector Computers
Cray X1
  MIPS like ISA + Vector in CMOS
NEC Earth Simulator
  Fastest computer in world for 3 years; 40 TFLOPS
  640 CMOS vector nodes

## Slide 16: Key Architectural Features of X1
New vector instruction set architecture (ISA)
  Much larger register set (32x64 vector, 64+64 scalar)
  64- and 32-bit memory and IEEE arithmetic
  Based on 25 years of experience compiling with Cray1 ISA
Decoupled Execution
  Scalar unit runs ahead of vector unit, doing addressing and control
  Hardware dynamically unrolls loops, and issues multiple loops concurrently
  Special sync operations keep pipeline full, even across barriers
   Allows the processor to perform well on short nested loops
Scalable, distributed shared memory (DSM) architecture
  Memory hierarchy: caches, local memory, remote memory
  Low latency, load/store access to entire machine (tens of TBs)
  Processors support 1000’s of outstanding refs with flexible addressing
  Very high bandwidth network
  Coherence protocol, addressing and synchronization optimized for DM

## Slide 17
Technology refresh of the X1 (0.13m)
  ~50% faster processors
  Scalar performance enhancements
  Doubling processor density
  Modest increase in memory system bandwidth
  Same interconnect and I/O
Machine upgradeable
  Can replace Cray X1 nodes with X1E nodes
Shipping the end of this year
Cray X1E Mid-life Enhancement

## Slide 18: ESS – configuration of a general purpose supercomputer
Processor Nodes (PN) Total number of processor nodes is 640. Each processor node consists of eight vector processors of 8 GFLOPS and 16GB shared memories. Therefore, total numbers of processors is 5,120 and total peak performance and main memory of the system are 40 TFLOPS and 10 TB, respectively. Two nodes are installed into one cabinet, which size is 40”x56”x80”. 16 nodes are in a cluster. Power consumption per cabinet is approximately 20 KVA.
2) Interconnection Network (IN): Each node is coupled together with more than 83,000 copper cables via single-stage crossbar switches of 16GB/s x2 (Load + Store). The total length of the cables is approximately 1,800 miles.
3) Hard Disk. Raid disks are used for the system. The capacities are 450 TB for the systems operations and 250 TB for users.
4) Mass Storage system: 12 Automatic Cartridge Systems (STK PowderHorn9310); total storage capacity is approximately 1.6 PB.
From Horst D. Simon, NERSC/LBNL, May 15, 2002, “ESS Rapid Response Meeting”

## Slide 19: Earth Simulator

## Slide 20
Earth Simulator Building

## Slide 21: ESS – complete system installed 4/1/2002

## Slide 22: Vector Summary
Vector is alternative model for exploiting ILP
If code is vectorizable, then simpler hardware, more energy efficient, and better real-time model than Out-of-order machines
Design issues include number of lanes, number of functional units, number of vector registers, length of vector registers, exception handling, conditional operations
Fundamental design issue is memory bandwidth
  With virtual address translation and caching
Will multimedia popularity revive vector architectures?

## Slide 23: CS 252 Administrivia
Next Reading Assignment: Chapter 4
Monday March 20 Quiz Evening

## Slide 24: “The CRAY-1 computer system”
by R.M. Russell, Comm. of the ACM, January 1978
Number of functional units?
  Compared to today?
Clock rate?
  Why so fast?
  How balance clock cycle?
Size of register state?
Memory size?
Memory latency?
  Compared to today?
“4 most striking features?”
Instruction set architecture?
Virtual Memory? Relocation? Protection?
Notes: 12 functional units – typically 6 to 8
80 MHz? Fast because its small; make wires same length
8 MB of memory
50 ns; faster than today on PC
1. 4 types of chips (2 NANDs, 6 ns 16x4 register file, 50 ns 1k x 1 sram)
2. Main memory speed
3. Cooling; 4x per cubic inch of CDC 7600
4. Computation
Load store, 3 address, 24 bit memory address; 4 parcels per 64 bit word; word addressed
No VM; had base (BA) and limit registers (LA)

## Slide 25: “The CRAY-1 computer system”
Floating Point Format?
  How differs from IEEE 754 FP?
Vector vs. scalar speed?
Min. size vector faster than scalar loop?
What meant by “long vector vs. short vector” computer?
Relative speed to other computers?
  Of its era?
  Pentium-4 or AMD 64?
General impressions compared to today’s CPUs
Notes: No single precession; 15 bits of exponent; 48 mantissa
Min size faster |: 2 to 4 elements
Long vector (Star) from memory, so > 100 elements before faster
5X than fastest IBM
138 MFLOPS, 250 MFLOPS peak
Opeteron or Pentium 4 get about 4 GFLOPS on linpack
Scalar was 2X faster than 7600
How many Cray-1 were shipped??? (Bell and Newell? Check Wikipedia?)
Power was limiting factor then as it is today
80 Cray-1s of all types were sold, priced from $5M to $8M.
Cray-1A, weighed 5.5 tons including the freon refrigeration system
he later Cray-1S had a slightly faster clockspeed of 12.0ns, and main memory in sizes of 1, 2 and 4 million words.
The Cray 1-S was itself replaced by the Cray-1M, the M indicating that it used less expensive MOS-based RAM in the I/O system. The 1M was supplied in only three versions, the M/1200 with 1M-word in 8 banks, or the M/2200 and M/4200 with 2 or 4M in 16 banks. All of these machines included two, three or four I/O processors, and the system added an optional second High Speed Data Channel. Users could also add an Solid-state Storage Device, a RAM disk, with 8 to 32M-words of MOS-RAM.
The CRAY-1 consumes 115kW (10^3 of those today), weighs 10,500 lbs (10^6 more than today), and has a Freon cooling system. At

## Slide 26: Outline
Review
Vector Metrics, Terms
Cray 1 paper discussion
MP Motivation
SISD v. SIMD v. MIMD
Centralized vs. Distributed Memory
Challenges to Parallel Programming
Consistency, Coherency, Write Serialization
Write Invalidate Protocol
Example
Conclusion

## Slide 27: Uniprocessor Performance (SPECint)
VAX : 25%/year 1978 to 1986
RISC + x86: 52%/year 1986 to 2002
RISC + x86: ??%/year 2002 to present
From Hennessy and Patterson, Computer Architecture: A Quantitative Approach, 4th edition, 2006
3X
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: Déjà vu all over again?
“… today’s processors … are nearing an impasse as technologies approach the speed of light..”
David Mitchell, The Transputer: The Time Is Now (1989)
Transputer had bad timing (Uniprocessor performance)  Procrastination rewarded: 2X seq. perf. / 1.5 years
“We are dedicating all of our future product development to multicore designs. … This is a sea change in computing”
Paul Otellini, President, Intel (2005)
All microprocessor companies switch to MP (2X CPUs / 2 yrs)  Procrastination penalized: 2X sequential perf. / 5 yrs
Manufacturer/Year | AMD/’05 | Intel/’06 | IBM/’04 | Sun/’05
Processors/chip | 2 | 2 | 2 | 8
Threads/Processor | 1 | 2 | 2 | 4
Threads/chip | 2 | 4 | 4 | 32
Notes: <number>
<footer>
<header>
<date/time>

## Slide 29: Other Factors  Multiprocessors
Growth in data-intensive applications
  Data bases, file servers, …
Growing interest in servers, server perf.
Increasing desktop perf. less important
  Outside of graphics
Improved understanding in how to use multiprocessors effectively
  Especially server where significant natural TLP
Advantage of leveraging design investment by replication
  Rather than unique design

## Slide 30: Flynn’s Taxonomy
Flynn classified by data and control streams in 1966
SIMD  Data Level Parallelism
MIMD  Thread Level Parallelism
MIMD popular because
  Flexible: N pgms and 1 multithreaded pgm
  Cost-effective: same MPU in desktop & MIMD
Single Instruction Single Data (SISD) (Uniprocessor) | Single Instruction Multiple Data SIMD (single PC: Vector, CM-2)
Multiple Instruction Single Data (MISD) (????) | Multiple Instruction Multiple Data MIMD (Clusters, SMP servers)
M.J. Flynn, "Very High-Speed Computers", Proc. of the IEEE, V 54, 1900-1909, Dec. 1966.

## Slide 31: Back to Basics
“A parallel computer is a collection of processing elements that cooperate and communicate to solve large problems fast.”
Parallel Architecture = Computer Architecture + Communication Architecture
2 classes of multiprocessors WRT memory:
Centralized Memory Multiprocessor
  < few dozen processor chips (and < 100 cores) in 2006
  Small enough to share single, centralized memory
Physically Distributed-Memory multiprocessor
  Larger number chips and cores than 1.
  BW demands  Memory distributed among processors

## Slide 32: Centralized vs. Distributed Memory
P
1
$
Inter
connection network
$
P
n
Mem
Mem
P
1
$
Inter
connection network
$
P
n
Mem
Mem
Centralized Memory
Distributed Memory
Scale

## Slide 33: Centralized Memory Multiprocessor
  Also called symmetric multiprocessors (SMPs) because single main memory has a symmetric relationship to all processors
  Large caches  single memory can satisfy memory demands of small number of processors
  Can scale to a few dozen processors by using a switch and by using many memory banks
  Although scaling beyond that is technically conceivable, it becomes less attractive as the number of processors sharing centralized memory increases

## Slide 34: Distributed Memory Multiprocessor
  Pro: Cost-effective way to scale memory bandwidth
    If most accesses are to local memory
  Pro: Reduces latency of local memory accesses
  Con: Communicating data between processors more complex
  Con: Must change software to take advantage of increased memory BW

## Slide 35: 2 Models for Communication and Memory Architecture
Communication occurs by explicitly passing messages among the processors: message-passing multiprocessors
Communication occurs through a shared address space (via loads and stores): shared memory multiprocessors either
  UMA (Uniform Memory Access time) for shared address, centralized memory MP
  NUMA (Non Uniform Memory Access time multiprocessor) for shared address, distributed memory MP
In past, confusion whether “sharing” means sharing physical memory (Symmetric MP) or sharing address space

## Slide 36: Challenges of Parallel Processing
First challenge is % of program inherently sequential
Suppose 80X speedup from 100 processors. What fraction of original program can be sequential?
  10%
  5%
  1%
  <1%

## Slide 37: Amdahl’s Law Answers

## Slide 38: Challenges of Parallel Processing
Second challenge is long latency to remote memory
Suppose 32 CPU MP, 2GHz, 200 ns remote memory, all local accesses hit memory hierarchy and base CPI is 0.5. (Remote access = 200/0.5 = 400 clock cycles.)
What is performance impact if 0.2% instructions involve remote access?
  1.5X
  2.0X
  2.5X

## Slide 39: CPI Equation
CPI = Base CPI + Remote request rate x Remote request cost
CPI = 0.5 + 0.2% x 400 = 0.5 + 0.8 = 1.3
No communication is 1.3/0.5 or 2.6 faster than 0.2% instructions involve local access

## Slide 40: Challenges of Parallel Processing
Application parallelism  primarily via new algorithms that have better parallel performance
Long remote latency impact  both by architect and by the programmer
For example, reduce frequency of remote accesses either by
  Caching shared data (HW)
  Restructuring the data layout to make more accesses local (SW)
Today’s lecture on HW to help latency via caches

## Slide 41: Symmetric Shared-Memory Architectures
From multiple boards on a shared bus to multiple processors inside a single chip
Caches both
  Private data are used by a single processor
  Shared data are used by multiple processors
Caching shared data  reduces latency to shared data, memory bandwidth for shared data, and interconnect bandwidth  cache coherence problem

## Slide 42: Example Cache Coherence Problem
  Processors see different values for u after event 3
  With write back caches, value written back to memory depends on happenstance of which cache flushes or writes back value when
    Processes accessing main memory may see very stale value
  Unacceptable for programming, and its frequent!
I/O devices
Memory
P
1
$
$
$
P
2
P
3
5
u
= ?
4
u
= ?
u
:5
1
u
:5
2
u
:5
3
u
= 7

## Slide 43: Example
Intuition not guaranteed by coherence
expect memory to respect order between accesses to different locations issued by a given process
  to preserve orders among accesses to same location by different processes
Coherence is not enough!
  pertains only to single location
P
1
P
2
/*Assume initial value of A and flag is 0*/
A = 1;
while (flag == 0);
/*spin idly*/
flag = 1;
print A;
Mem
P
1
P
n
Conceptual
Picture

## Slide 44: Intuitive Memory Model
P
Disk
Memory
L2
L1
100:34
100:35
100:67
Too vague and simplistic; 2 issues
Coherence defines values returned by a read
Consistency determines when a written value will be returned by a read
Coherence defines behavior to same location, Consistency defines behavior to other locations
Reading an address should return the last value written to that address
  Easy in uniprocessors, except for I/O

## Slide 45: Defining Coherent Memory System
Preserve Program Order: A read by processor P to location X that follows a write by P to X, with no writes of X by another processor occurring between the write and the read by P, always returns the value written by P
Coherent view of memory: Read by a processor to location X that follows a write by another processor to X returns the written value if the read and write are sufficiently separated in time and no other writes to X occur between the two accesses
Write serialization: 2 writes to same location by any 2 processors are seen in the same order by all processors
  If not, a processor could keep value 1 since saw as last write
  For example, if the values 1 and then 2 are written to a location, processors can never read the value of the location as 2 and then later read it as 1

## Slide 46: Write Consistency
For now assume
A write does not complete (and allow the next write to occur) until all processors have seen the effect of that write
The processor does not change the order of any write with respect to any other memory access
 if a processor writes location A followed by location B, any processor that sees the new value of B must also see the new value of A
These restrictions allow the processor to reorder reads, but forces the processor to finish writes in program order

## Slide 47: Basic Schemes for Enforcing Coherence
Program on multiple processors will normally have copies of the same data in several caches
  Unlike I/O, where its rare
Rather than trying to avoid sharing in SW, SMPs use a HW protocol to maintain coherent caches
  Migration and Replication key to performance of shared data
Migration - data can be moved to a local cache and used there in a transparent fashion
  Reduces both latency to access shared data that is allocated remotely and bandwidth demand on the shared memory
Replication – for shared data being simultaneously read, since caches make a copy of data in local cache
  Reduces both latency of access and contention for read shared data

## Slide 48: 2 Classes of Cache Coherence Protocols
Directory based — Sharing status of a block of physical memory is kept in just one location, the directory
Snooping — Every cache with a copy of data also has a copy of sharing status of block, but no centralized state is kept
  All caches are accessible via some broadcast medium (a bus or switch)
  All cache controllers monitor or snoop on the medium to determine whether or not they have a copy of a block that is requested on a bus or switch access

## Slide 49: Snoopy Cache-Coherence Protocols
Cache Controller “snoops” all transactions on the shared medium (bus or switch)
  relevant transaction if for a block it contains
  take action to ensure coherence
    invalidate, update, or supply value
  depends on state of the block and the protocol
Either get exclusive access before write via write invalidate or update all copies on write
State
Address
Data

## Slide 50: Example: Write-thru Invalidate
Must invalidate before step 3
Write update uses more broadcast medium BW  all recent MPUs use write invalidate
I/O devices
Memory
P
1
$
$
$
P
2
P
3
5
u
= ?
4
u
= ?
u
:5
1
u
:5
2
u
:5
3
u
= 7
u = 7

## Slide 51: Architectural Building Blocks
Cache block state transition diagram
  FSM specifying how disposition of block changes
    invalid, valid, dirty
Broadcast Medium Transactions (e.g., bus)
  Fundamental system design abstraction
  Logically single set of wires connect several devices
  Protocol: arbitration, command/addr, data
  Every device observes every transaction
Broadcast medium enforces serialization of read or write accesses  Write serialization
  1st processor to get medium invalidates others copies
  Implies cannot complete write until it obtains bus
  All coherence schemes require serializing accesses to same cache block
Also need to find up-to-date copy of cache block

## Slide 52: Locate up-to-date copy of data
Write-through: get up-to-date copy from memory
  Write through simpler if enough memory BW
Write-back harder
  Most recent copy can be in a cache
Can use same snooping mechanism
  Snoop every address placed on the bus
  If a processor has dirty copy of requested cache block, it provides it in response to a read request and aborts the memory access
  Complexity from retrieving cache block from a processor cache, which can take longer than retrieving it from memory
Write-back needs lower memory bandwidth  Support larger numbers of faster processors  Most multiprocessors use write-back

## Slide 53: Cache Resources for WB Snooping
Normal cache tags can be used for snooping
Valid bit per block makes invalidation easy
Read misses easy since rely on snooping
Writes  Need to know if know whether any other copies of the block are cached
  No other copies  No need to place write on bus for WB
  Other copies  Need to place invalidate on bus

## Slide 54: Cache Resources for WB Snooping
To track whether a cache block is shared, add extra state bit associated with each cache block, like valid bit and dirty bit
  Write to Shared block  Need to place invalidate on bus and mark cache block as private (if an option)
  No further invalidations will be sent for that block
  This processor called owner of cache block
  Owner then changes state from shared to unshared (or exclusive)

## Slide 55: Cache behavior in response to bus
Every bus transaction must check the cache-address tags
  could potentially interfere with processor cache accesses
A way to reduce interference is to duplicate tags
  One set for caches access, one set for bus accesses
Another way to reduce interference is to use L2 tags
  Since L2 less heavily used than L1
   Every entry in L1 cache must be present in the L2 cache, called the inclusion property
  If Snoop gets a hit in L2 cache, then it must arbitrate for the L1 cache to update the state and possibly retrieve the data, which usually requires a stall of the processor

## Slide 56: Example Protocol
Snooping coherence protocol is usually implemented by incorporating a finite-state controller in each node
Logically, think of a separate controller associated with each cache block
  That is, snooping operations or cache requests for different blocks can proceed independently
In implementations, a single controller allows multiple operations to distinct blocks to proceed in interleaved fashion
  that is, one operation may be initiated before another is completed, even through only one cache access or one bus access is allowed at time

## Slide 57: Write-through Invalidate Protocol
2 states per block in each cache
  as in uniprocessor
  state of a block is a p-vector of states
  Hardware state bits associated with blocks that are in the cache
  other blocks can be seen as being in invalid (not-present) state in that cache
Writes invalidate all other cache copies
  can have multiple simultaneous readers of block,but write invalidates them
I
V
BusWr / -
PrRd/ --
PrWr / BusWr
PrWr / BusWr
PrRd / BusRd
State Tag Data
I/O devices
Mem
P
1
$
$
P
n
Bus
State Tag Data
PrRd: Processor Read
PrWr: Processor Write
BusRd: Bus Read
BusWr: Bus Write

## Slide 58: Is 2-state Protocol Coherent?
Processor only observes state of memory system by issuing memory operations
Assume bus transactions and memory operations are atomic and a one-level cache
  all phases of one bus transaction complete before next one starts
  processor waits for memory operation to complete before issuing next
  with one-level cache, assume invalidations applied during bus transaction
All writes go to bus + atomicity
  Writes serialized by order in which they appear on bus (bus order)
  => invalidations applied to caches in bus order
How to insert reads in this order?
  Important since processors see writes through reads, so determines whether write serialization is satisfied
  But read hits may happen independently and do not appear on bus or enter directly in bus order
Let’s understand other ordering issues

## Slide 59: Ordering
Writes establish a partial order
Doesn’t constrain ordering of reads, though shared-medium (bus) will order read misses too
  any order among reads between writes is fine, as long as in program order

## Slide 60: Example Write Back Snoopy Protocol
Invalidation protocol, write-back cache
  Snoops every address on bus
  If it has a dirty copy of requested block, provides that block in response to the read request and aborts the memory access
Each memory block is in one state:
  Clean in all caches and up-to-date in memory (Shared)
  OR Dirty in exactly one cache (Exclusive)
  OR Not in any caches
Each cache block is in one state (track these):
  Shared : block can be read
  OR Exclusive : cache has only copy, its writeable, and dirty
  OR Invalid : block contains no data (in uniprocessor cache too)
Read misses: cause all caches to snoop bus
Writes to clean blocks are treated as misses

## Slide 61: Write-Back State Machine - CPU
CPU Read hit
State machine for CPU requests for each cache block
Non-resident blocks invalid
Invalid
Shared
(read/only)
Exclusive
(read/write)
CPU Read
CPU Write
Place read miss
on bus
Place Write Miss on bus
CPU Write
Place Write Miss on Bus
CPU Write Miss (?)
Write back cache block
Place write miss on bus
CPU read hit
CPU write hit
Cache Block
State
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 62: Write-Back State Machine- Bus request
State machine for bus requests for each cache block
Invalid
Shared
(read/only)
Exclusive
(read/write)
Write Back
Block; (abort
memory access)
Write miss for this block
Read miss for this block
Write miss for this block
Write Back
Block; (abort
memory access)

## Slide 63: Block-replacement
State machine for CPU requests for each cache block
Invalid
Shared
(read/only)
Exclusive
(read/write)
CPU Read
CPU Write
CPU Read hit
Place read miss
on bus
Place Write Miss on bus
CPU read miss
Write back block,
Place read miss
on bus
CPU Write
Place Write Miss on Bus
CPU Read miss
Place read miss
on bus
CPU Write Miss
Write back cache block
Place write miss on bus
CPU read hit
CPU write hit
Cache Block
State
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 64: Write-back State Machine-III
Place read miss
on bus
State machine for CPU requests for each cache block and for bus requests for each cache block
Invalid
Shared
(read/only)
Exclusive
(read/write)
CPU Read
CPU Write
CPU Read hit
Place Write Miss on bus
CPU read miss
Write back block,
Place read miss
on bus
CPU Write
Place Write Miss on Bus
CPU Read miss
Place read miss
on bus
CPU Write Miss
Write back cache block
Place write miss on bus
CPU read hit
CPU write hit
Cache Block
State
Write miss for this block
Write Back
Block; (abort
memory access)
Write miss for this block
Read miss for this block
Write Back
Block; (abort
memory access)
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 65: Example
Assumes A1 and A2 map to same cache block,
initial cache state is invalid

## Slide 66: Example
Assumes A1 and A2 map to same cache block

## Slide 67: Example
Assumes A1 and A2 map to same cache block

## Slide 68: Example
Assumes A1 and A2 map to same cache block

## Slide 69: Example
Assumes A1 and A2 map to same cache block

## Slide 70: Example
Assumes A1 and A2 map to same cache block,
but A1 != A2
Notes: Why write miss first?
Because in general, only write a piece of block, may need to read it first so that can have a full vblock; therefore, need to get
Write back is low priority event.

## Slide 71: And in Conclusion [1/2] …
1 instruction operates on vectors of data
Vector loads get data from memory into big register files, operate, and then vector store
E.g., Indexed load, store for sparse matrix
Easy to add vector to commodity instruction set
  E.g., Morph SIMD into vector
Vector is very effecient architecture for vectorizable codes, including multimedia and many scientific codes

## Slide 72: And in Conclusion [2/2] …
“End” of uniprocessors speedup => Multiprocessors
Parallelism challenges: % parallalizable, long latency to remote memory
Centralized vs. distributed memory
  Small MP vs. lower latency, larger BW for Larger MP
Message Passing vs. Shared Address
  Uniform access time vs. Non-uniform access time
Snooping cache over shared medium for smaller MP by invalidating other cached copies on write
Sharing cached data  Coherence (values returned by a read), Consistency (when a written value will be returned by a read)
Shared medium serializes writes  Write consistency