## Slide 1: EECS 252 Graduate Computer Architecture Lec 13 – Snooping Cache and Directory Based Multiprocessors
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://vlsi.cs.berkeley.edu/cs252-s06

## Slide 2: Review
1 instruction operates on vectors of data
Vector loads get data from memory into big register files, operate, and then vector store
E.g., Indexed load, store for sparse matrix
Easy to add vector to commodity instruction set
  E.g., Morph SIMD into vector
Vector is very effecient architecture for vectorizable codes, including multimedia and many scientific codes
“End” of uniprocessors speedup => Multiprocessors
Parallelism challenges: % parallalizable, long latency to remote memory
Centralized vs. distributed memory
  Small MP vs. lower latency, larger BW for Larger MP
Message Passing vs. Shared Address
  Uniform access time vs. Non-uniform access time

## Slide 3: Outline
Review
Coherence
Write Consistency
Administrivia
Snooping
Building Blocks
Snooping protocols and examples
Coherence traffic and Performance on MP
Directory-based protocols and examples (if get this far)
Conclusion

## Slide 4: Challenges of Parallel Processing
Application parallelism  primarily via new algorithms that have better parallel performance
Long remote latency impact  both by architect and by the programmer
For example, reduce frequency of remote accesses either by
  Caching shared data (HW)
  Restructuring the data layout to make more accesses local (SW)
Today’s lecture on HW to help latency via caches

## Slide 5: Symmetric Shared-Memory Architectures
From multiple boards on a shared bus to multiple processors inside a single chip
Caches both
  Private data are used by a single processor
  Shared data are used by multiple processors
Caching shared data  reduces latency to shared data, memory bandwidth for shared data, and interconnect bandwidth  cache coherence problem

## Slide 6: Example Cache Coherence Problem
  Processors see different values for u after event 3
  With write back caches, value written back to memory depends on happenstance of which cache flushes or writes back value when
    Processes accessing main memory may see very stale value
  Unacceptable for programming, and its frequent!
I/O devices
Memory
P
1
$
$
$
P
2
P
3
5
u
= ?
4
u
= ?
u
:5
1
u
:5
2
u
:5
3
u
= 7

## Slide 7: Example
Intuition not guaranteed by coherence
expect memory to respect order between accesses to different locations issued by a given process
  to preserve orders among accesses to same location by different processes
Coherence is not enough!
  pertains only to single location
P
1
P
2
/*Assume initial value of A and flag is 0*/
A = 1;
while (flag == 0);
/*spin idly*/
flag = 1;
print A;
Mem
P
1
P
n
Conceptual
Picture

## Slide 8: Intuitive Memory Model
P
Disk
Memory
L2
L1
100:34
100:35
100:67
Too vague and simplistic; 2 issues
Coherence defines values returned by a read
Consistency determines when a written value will be returned by a read
Coherence defines behavior to same location, Consistency defines behavior to other locations
Reading an address should return the last value written to that address
  Easy in uniprocessors, except for I/O

## Slide 9: Defining Coherent Memory System
Preserve Program Order: A read by processor P to location X that follows a write by P to X, with no writes of X by another processor occurring between the write and the read by P, always returns the value written by P
Coherent view of memory: Read by a processor to location X that follows a write by another processor to X returns the written value if the read and write are sufficiently separated in time and no other writes to X occur between the two accesses
Write serialization: 2 writes to same location by any 2 processors are seen in the same order by all processors
  If not, a processor could keep value 1 since saw as last write
  For example, if the values 1 and then 2 are written to a location, processors can never read the value of the location as 2 and then later read it as 1

## Slide 10: Write Consistency
For now assume
A write does not complete (and allow the next write to occur) until all processors have seen the effect of that write
The processor does not change the order of any write with respect to any other memory access
 if a processor writes location A followed by location B, any processor that sees the new value of B must also see the new value of A
These restrictions allow the processor to reorder reads, but forces the processor to finish writes in program order

## Slide 11: Basic Schemes for Enforcing Coherence
Program on multiple processors will normally have copies of the same data in several caches
  Unlike I/O, where its rare
Rather than trying to avoid sharing in SW, SMPs use a HW protocol to maintain coherent caches
  Migration and Replication key to performance of shared data
Migration - data can be moved to a local cache and used there in a transparent fashion
  Reduces both latency to access shared data that is allocated remotely and bandwidth demand on the shared memory
Replication – for reading shared data simultaneously, since caches make a copy of data in local cache
  Reduces both latency of access and contention for read shared data

## Slide 12: CS 252 Administrivia
Monday March 20 Quiz 5-8 PM 405 Soda
Due Friday: Problem Set and Comments on 2 papers
  Problem Set Assignment done in pairs
  Gene Amdahl, "Validity of the Single Processor Approach to Achieving Large-Scale Computing Capabilities", AFIPS Conference Proceedings, (30), pp. 483-485, 1967.
  Lorin Hochstein et al "Parallel Programmer Productivity: A Case Study of Novice Parallel Programmers." International Conference for High Performance Computing, Networking and Storage (SC'05). November 2005
Be sure to comment
  Amdahl: How long is paper? How much of it is Amdahl’s Law? What other comments about parallelism besides Amdahl’s Law?
  Hochstein: What programming styles investigated? What was methodology? How would you redesign the experiment they did? What other metrics would be important to capture? Assuming these results of programming productivity reflect the real world, what should architectures of the future do (or not do)?
Monday discussion of papers

## Slide 13: Outline
Review
Coherence
Write Consistency
Administrivia
Snooping
Building Blocks
Snooping protocols and examples
Coherence traffic and Performance on MP
Directory-based protocols and examples

## Slide 14: 2 Classes of Cache Coherence Protocols
Directory based — Sharing status of a block of physical memory is kept in just one location, the directory
Snooping — Every cache with a copy of data also has a copy of sharing status of block, but no centralized state is kept
  All caches are accessible via some broadcast medium (a bus or switch)
  All cache controllers monitor or snoop on the medium to determine whether or not they have a copy of a block that is requested on a bus or switch access

## Slide 15: Snoopy Cache-Coherence Protocols
Cache Controller “snoops” all transactions on the shared medium (bus or switch)
  relevant transaction if for a block it contains
  take action to ensure coherence
    invalidate, update, or supply value
  depends on state of the block and the protocol
Either get exclusive access before write via write invalidate or update all copies on write
State
Address
Data

## Slide 16: Example: Write-thru Invalidate
Must invalidate before step 3
Write update uses more broadcast medium BW  all recent MPUs use write invalidate
I/O devices
Memory
P
1
$
$
$
P
2
P
3
5
u
= ?
4
u
= ?
u
:5
1
u
:5
2
u
:5
3
u
= 7
u = 7

## Slide 17: Architectural Building Blocks
Cache block state transition diagram
  FSM specifying how disposition of block changes
    invalid, valid, exclusive
Broadcast Medium Transactions (e.g., bus)
  Fundamental system design abstraction
  Logically single set of wires connect several devices
  Protocol: arbitration, command/addr, data
  Every device observes every transaction
Broadcast medium enforces serialization of read or write accesses  Write serialization
  1st processor to get medium invalidates others copies
  Implies cannot complete write until it obtains bus
  All coherence schemes require serializing accesses to same cache block
Also need to find up-to-date copy of cache block

## Slide 18: Locate up-to-date copy of data
Write-through: get up-to-date copy from memory
  Write through simpler if enough memory BW
Write-back harder
  Most recent copy can be in a cache
Can use same snooping mechanism
  Snoop every address placed on the bus
  If a processor has dirty copy of requested cache block, it provides it in response to a read request and aborts the memory access
  Complexity from retrieving cache block from cache, which can take longer than retrieving it from memory
Write-back needs lower memory bandwidth  Support larger numbers of faster processors  Most multiprocessors use write-back

## Slide 19: Cache Resources for WB Snooping
Normal cache tags can be used for snooping
Valid bit per block makes invalidation easy
Read misses easy since rely on snooping
Writes  Need to know if know whether any other copies of the block are cached
  No other copies  No need to place write on bus for WB
  Other copies  Need to place invalidate on bus

## Slide 20: Cache Resources for WB Snooping
To track whether a cache block is shared, add extra state bit associated with each cache block, like valid bit and dirty bit
  Write to Shared block  Need to place invalidate on bus and mark cache block as private (if an option)
  No further invalidations will be sent for that block
  This processor called owner of cache block
  Owner then changes state from shared to unshared (or exclusive)

## Slide 21: Cache behavior in response to bus
Every bus transaction must check the cache-address tags
  could potentially interfere with processor cache accesses
A way to reduce interference is to duplicate tags
  One set for caches access, one set for bus accesses
Another way to reduce interference is to use L2 tags
  Since L2 less heavily used than L1
   Every entry in L1 cache must be present in the L2 cache, called the inclusion property
  If Snoop gets a hit in L2 cache, then it must arbitrate for the L1 cache to update the state and possibly retrieve the data, which usually requires a stall of the processor

## Slide 22: Example Protocol
Snooping coherence protocol is usually implemented by incorporating a finite-state controller in each node
Logically, think of a separate controller associated with each cache block
  That is, snooping operations or cache requests for different blocks can proceed independently
In implementations, a single controller allows multiple operations to distinct blocks to proceed in interleaved fashion
  that is, one operation may be initiated before another is completed, even through only one cache access or one bus access is allowed at time

## Slide 23: Write-through Invalidate Protocol
2 states per block in each cache
  as in uniprocessor
  state of a block is a p-vector of states
  Hardware state bits associated with blocks that are in the cache
  other blocks can be seen as being in invalid (not-present) state in that cache
Writes invalidate all other cache copies
  can have multiple simultaneous readers of block,but write invalidates them
I
V
BusWr / -
PrRd/ --
PrWr / BusWr
PrWr / BusWr
PrRd / BusRd
State Tag Data
I/O devices
Mem
P
1
$
$
P
n
Bus
State Tag Data
PrRd: Processor Read
PrWr: Processor Write
BusRd: Bus Read
BusWr: Bus Write

## Slide 24: Is 2-state Protocol Coherent?
Processor only observes state of memory system by issuing memory operations
Assume bus transactions and memory operations are atomic and a one-level cache
  all phases of one bus transaction complete before next one starts
  processor waits for memory operation to complete before issuing next
  with one-level cache, assume invalidations applied during bus transaction
All writes go to bus + atomicity
  Writes serialized by order in which they appear on bus (bus order)
  => invalidations applied to caches in bus order
How to insert reads in this order?
  Important since processors see writes through reads, so determines whether write serialization is satisfied
  But read hits may happen independently and do not appear on bus or enter directly in bus order
Let’s understand other ordering issues

## Slide 25: Ordering
Writes establish a partial order
Doesn’t constrain ordering of reads, though shared-medium (bus) will order read misses too
  any order among reads between writes is fine, as long as in program order

## Slide 26: Example Write Back Snoopy Protocol
Invalidation protocol, write-back cache
  Snoops every address on bus
  If it has a dirty copy of requested block, provides that block in response to the read request and aborts the memory access
Each memory block is in one state:
  Clean in all caches and up-to-date in memory (Shared)
  OR Dirty in exactly one cache (Exclusive)
  OR Not in any caches
Each cache block is in one state (track these):
  Shared : block can be read
  OR Exclusive : cache has only copy, its writeable, and dirty
  OR Invalid : block contains no data (in uniprocessor cache too)
Read misses: cause all caches to snoop bus
Writes to clean blocks are treated as misses

## Slide 27: Write-Back State Machine - CPU
CPU Read hit
State machine for CPU requests for each cache block
Non-resident blocks invalid
Invalid
Shared
(read/only)
Exclusive
(read/write)
CPU Read
CPU Write
Place read miss
on bus
Place Write Miss on bus
CPU Write
Place Write Miss on Bus
CPU Write Miss (?)
Write back cache block
Place write miss on bus
CPU read hit
CPU write hit
Cache Block
State
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 28: Write-Back State Machine- Bus request
State machine for bus requests for each cache block
Invalid
Shared
(read/only)
Exclusive
(read/write)
Write Back
Block; (abort
memory access)
Write miss for this block
Read miss for this block
Write miss for this block
Write Back
Block; (abort
memory access)

## Slide 29: Block-replacement
State machine for CPU requests for each cache block
Invalid
Shared
(read/only)
Exclusive
(read/write)
CPU Read
CPU Write
CPU Read hit
Place read miss
on bus
Place Write Miss on bus
CPU read miss
Write back block,
Place read miss
on bus
CPU Write
Place Write Miss on Bus
CPU Read miss
Place read miss
on bus
CPU Write Miss
Write back cache block
Place write miss on bus
CPU read hit
CPU write hit
Cache Block
State
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 30: Write-back State Machine-III
Place read miss
on bus
State machine for CPU requests for each cache block and for bus requests for each cache block
Invalid
Shared
(read/only)
Exclusive
(read/write)
CPU Read
CPU Write
CPU Read hit
Place Write Miss on bus
CPU read miss
Write back block,
Place read miss
on bus
CPU Write
Place Write Miss on Bus
CPU Read miss
Place read miss
on bus
CPU Write Miss
Write back cache block
Place write miss on bus
CPU read hit
CPU write hit
Cache Block
State
Write miss for this block
Write Back
Block; (abort
memory access)
Write miss for this block
Read miss for this block
Write Back
Block; (abort
memory access)
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 31: Example
Assumes A1 and A2 map to same cache block,
initial cache state is invalid

## Slide 32: Example
Assumes A1 and A2 map to same cache block

## Slide 33: Example
Assumes A1 and A2 map to same cache block

## Slide 34: Example
Assumes A1 and A2 map to same cache block

## Slide 35: Example
Assumes A1 and A2 map to same cache block

## Slide 36: Example
Assumes A1 and A2 map to same cache block,
but A1 != A2
Notes: Why write miss first?
Because in general, only write a piece of block, may need to read it first so that can have a full vblock; therefore, need to get
Write back is low priority event.

## Slide 37: Implementation Complications
Write Races:
  Cannot update cache until bus is obtained
    Otherwise, another processor may get bus first, and then write the same cache block!
  Two step process:
    Arbitrate for bus
    Place miss on bus and complete operation
  If miss occurs to block while waiting for bus, handle miss (invalidate may be needed) and then restart.
  Split transaction bus:
    Bus transaction is not atomic: can have multiple outstanding transactions for a block
    Multiple misses can interleave, allowing two caches to grab block in the Exclusive state
    Must track and prevent multiple misses for one block
Must support interventions and invalidations

## Slide 38: Implementing Snooping Caches
Multiple processors must be on bus, access to both addresses and data
Add a few new commands to perform coherency, in addition to read and write
Processors continuously snoop on address bus
  If address matches tag, either invalidate or update
Since every bus transaction checks cache tags, could interfere with CPU just to check:
  solution 1: duplicate set of tags for L1 caches just to allow checks in parallel with CPU
  solution 2: L2 cache already duplicate, provided L2 obeys inclusion with L1 cache
    block size, associativity of L2 affects L1

## Slide 39: Limitations in Symmetric Shared-Memory Multiprocessors and Snooping Protocols
Single memory accommodate all CPUs  Multiple memory banks
Bus-based multiprocessor, bus must support both coherence traffic & normal memory traffic
 Multiple buses or interconnection networks (cross bar or small point-to-point)
Opteron
  Memory connected directly to each dual-core chip
  Point-to-point connections for up to 4 chips
  Remote memory and local memory latency are similar, allowing OS Opteron as UMA computer

## Slide 40: Performance of Symmetric Shared-Memory Multiprocessors
Cache performance is combination of
Uniprocessor cache miss traffic
Traffic caused by communication
  Results in invalidations and subsequent cache misses
4th C: coherence miss
  Joins Compulsory, Capacity, Conflict

## Slide 41: Coherency Misses
True sharing misses arise from the communication of data through the cache coherence mechanism
  Invalidates due to 1st write to shared block
  Reads by another CPU of modified block in different cache
  Miss would still occur if block size were 1 word
False sharing misses when a block is invalidated because some word in the block, other than the one being read, is written into
  Invalidation does not cause a new value to be communicated, but only causes an extra cache miss
  Block is shared, but no word in block is actually shared  miss would not occur if block size were 1 word

## Slide 42: Example: True v. False Sharing v. Hit?
Time | P1 | P2 | True, False, Hit? Why?
1 | Write x1 |  | 
2 |  | Read x2 | 
3 | Write x1 |  | 
4 |  | Write x2 | 
5 | Read x2 |  | 
Assume x1 and x2 in same cache block. P1 and P2 both read x1 and x2 before.
True miss; invalidate x1 in P2
False miss; x1 irrelevant to P2
False miss; x1 irrelevant to P2
False miss; x1 irrelevant to P2
True miss; invalidate x2 in P1

## Slide 43: MP Performance 4 Processor Commercial Workload: OLTP, Decision Support (Database), Search Engine
True sharing and false sharing unchanged going from 1 MB to 8 MB (L3 cache)
Uniprocessor cache misses improve with cache size increase (Instruction, Capacity/Conflict, Compulsory)
(Memory) Cycles per Instruction

## Slide 44: MP Performance 2MB Cache Commercial Workload: OLTP, Decision Support (Database), Search Engine
True sharing, false sharing increase going from 1 to 8 CPUs
(Memory) Cycles per Instruction

## Slide 45: Outline
Review
Coherence
Write Consistency
Administrivia
Snooping
Building Blocks
Snooping protocols and examples
Coherence traffic and Performance on MP
Directory-based protocols and examples (if get this far)
Conclusion

## Slide 46: A Cache Coherent System Must:
Provide set of states, state transition diagram, and actions
Manage coherence protocol
  (0) Determine when to invoke coherence protocol
  (a) Find info about state of block in other caches to determine action
    whether need to communicate with other cached copies
  (b) Locate the other copies
  (c) Communicate with those copies (invalidate/update)
(0) is done the same way on all systems
  state of the line is maintained in the cache
  protocol is invoked if an “access fault” occurs on the line
Different approaches distinguished by (a) to (c)

## Slide 47: Bus-based Coherence
All of (a), (b), (c) done through broadcast on bus
  faulting processor sends out a “search”
  others respond to the search probe and take necessary action
Could do it in scalable network too
  broadcast to all processors, and let them respond
Conceptually simple, but broadcast doesn’t scale with p
  on bus, bus bandwidth doesn’t scale
  on scalable network, every fault leads to at least p network transactions
Scalable coherence:
  can have same cache states and state transition diagram
  different mechanisms to manage protocol

## Slide 48: Scalable Approach: Directories
Every memory block has associated directory information
  keeps track of copies of cached blocks and their states
  on a miss, find directory entry, look it up, and communicate only with the nodes that have copies if necessary
  in scalable networks, communication with directory and copies is through network transactions
Many alternatives for organizing directory information

## Slide 49: Basic Operation of Directory
• k processors.
• With each cache-block in memory: k presence-bits, 1 dirty-bit
• With each cache-block in cache: 1 valid bit, and 1 dirty (owner) bit
• Read from main memory by processor i:
  • If dirty-bit OFF then { read from main memory; turn p[i] ON; }
  • if dirty-bit ON then { recall line from dirty proc (cache state to shared); update memory; turn dirty-bit OFF; turn p[i] ON; supply recalled data to i;}
• Write to main memory by processor i:
  • If dirty-bit OFF then { supply data to i; send invalidations to all caches that have the block; turn dirty-bit ON; turn p[i] ON; ... }
  • ...

## Slide 50: Directory Protocol
Similar to Snoopy Protocol: Three states
  Shared: ≥ 1 processors have data, memory up-to-date
  Uncached (no processor hasit; not valid in any cache)
  Exclusive: 1 processor (owner) has data; memory out-of-date
In addition to cache state, must track which processors have data when in the shared state (usually bit vector, 1 if processor has copy)
Keep it simple(r):
  Writes to non-exclusive data => write miss
  Processor blocks until access completes
  Assume messages received and acted upon in order sent

## Slide 51: Directory Protocol
No bus and don’t want to broadcast:
  interconnect no longer single arbitration point
  all messages have explicit responses
Terms: typically 3 processors involved
  Local node where a request originates
  Home node where the memory location of an address resides
  Remote node has a copy of a cache block, whether exclusive or shared
Example messages on next slide: P = processor number, A = address

## Slide 52: Directory Protocol Messages (Fig 4.22)
Message type Source Destination Msg Content
Read miss Local cache Home directory P, A
  Processor P reads data at address A; make P a read sharer and request data
Write miss Local cache Home directory P, A
  Processor P has a write miss at address A; make P the exclusive owner and request data
Invalidate Home directory Remote caches A
  Invalidate a shared copy at address A
Fetch Home directory Remote cache A
  Fetch the block at address A and send it to its home directory; change the state of A in the remote cache to shared
Fetch/Invalidate Home directory Remote cache A
  Fetch the block at address A and send it to its home directory; invalidate the block in the cache
Data value reply Home directory Local cache Data
  Return a data value from the home memory (read miss response)
Data write back Remote cache Home directory A, Data
  Write back a data value for address A (invalidate response)

## Slide 53: State Transition Diagram for One Cache Block in Directory Based System
States identical to snoopy case; transactions very similar.
Transitions caused by read misses, write misses, invalidates, data fetch requests
Generates read miss & write miss msg to home directory.
Write misses that were broadcast on the bus for snooping => explicit invalidate & data fetch requests.
Note: on a write, a cache block is bigger, so need to read the full cache block

## Slide 54: CPU -Cache State Machine
State machine for CPU requests for each memory block
Invalid state if in memory
Fetch/Invalidate
send Data Write Back message
to home directory
Invalidate
Invalid
Exclusive
(read/write)
CPU Read
CPU Read hit
Send Read Miss
message
CPU Write: Send Write Miss
msg to h.d.
CPU Write: Send Write Miss message
to home directory
CPU read hit
CPU write hit
Fetch: send Data Write Back message to home directory
CPU read miss:
Send Read Miss
CPU write miss:
send Data Write Back message
and Write Miss to home directory
CPU read miss: send Data Write Back message and read miss to home directory
Shared
(read/only)
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 55: State Transition Diagram for Directory
Same states & structure as the transition diagram for an individual cache
2 actions: update of directory state & send messages to satisfy requests
Tracks all copies of memory block
Also indicates an action that updates the sharing set, Sharers, as well as sending a message

## Slide 56: Directory State Machine
State machine for Directory requests for each memory block
Uncached state if in memory
Data Write Back:
Sharers = {}
(Write back block)
Uncached
Shared
(read only)
Exclusive
(read/write)
Read miss:
Sharers = {P}
send Data Value
Reply
Write Miss:
send Invalidate
to Sharers;
then Sharers = {P};
send Data Value
Reply msg
Write Miss:
Sharers = {P};
send Data
Value Reply
msg
Read miss:
Sharers += {P};
send Fetch;
send Data Value Reply
msg to remote cache
(Write back block)
Read miss:
Sharers += {P};
send Data Value Reply
Write Miss:
Sharers = {P};
send Fetch/Invalidate;
send Data Value Reply
msg to remote cache
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 57: Example Directory Protocol
Message sent to directory causes two actions:
  Update the directory
  More messages to satisfy request
Block is in Uncached state: the copy in memory is the current value; only possible requests for that block are:
  Read miss: requesting processor sent data from memory &requestor made only sharing node; state of block made Shared.
  Write miss: requesting processor is sent the value & becomes the Sharing node. The block is made Exclusive to indicate that the only valid copy is cached. Sharers indicates the identity of the owner.
Block is Shared => the memory value is up-to-date:
  Read miss: requesting processor is sent back the data from memory & requesting processor is added to the sharing set.
  Write miss: requesting processor is sent the value. All processors in the set Sharers are sent invalidate messages, & Sharers is set to identity of requesting processor. The state of the block is made Exclusive.

## Slide 58: Example Directory Protocol
Block is Exclusive: current value of the block is held in the cache of the processor identified by the set Sharers (the owner) => three possible directory requests:
  Read miss: owner processor sent data fetch message, causing state of block in owner’s cache to transition to Shared and causes owner to send data to directory, where it is written to memory & sent back to requesting processor. Identity of requesting processor is added to set Sharers, which still contains the identity of the processor that was the owner (since it still has a readable copy). State is shared.
  Data write-back: owner processor is replacing the block and hence must write it back, making memory copy up-to-date (the home directory essentially becomes the owner), the block is now Uncached, and the Sharer set is empty.
  Write miss: block has a new owner. A message is sent to old owner causing the cache to send the value of the block to the directory from which it is sent to the requesting processor, which becomes the new owner. Sharers is set to identity of new owner, and state of block is made Exclusive.

## Slide 59: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory

## Slide 60: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory

## Slide 61: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory

## Slide 62: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory
A1
Write Back
A1

## Slide 63: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory
A1
A1

## Slide 64: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory
A1
A1

## Slide 65: Implementing a Directory
We assume operations atomic, but they are not; reality is much harder; must avoid deadlock when run out of bufffers in network (see Appendix E)
Optimizations:
  read miss or write miss in Exclusive: send data directly to requestor from owner vs. 1st to memory and then from memory to requestor

## Slide 66: Basic Directory Transactions

## Slide 67: Example Directory Protocol (1st Read)
E
S
I
P1
$
E
S
I
P2
$
D
S
U
M
Dir
ctrl
ld vA -> rd pA
Read pA
R/reply
R/req
P1: pA
S
S

## Slide 68: Example Directory Protocol (Read Share)
E
S
I
P1
$
E
S
I
P2
$
D
S
U
M
Dir
ctrl
ld vA -> rd pA
R/reply
R/req
P1: pA
ld vA -> rd pA
P2: pA
R/req
R/_
R/_
R/_
S
S
S

## Slide 69: Example Directory Protocol (Wr to shared)
E
S
I
P1
$
E
S
I
P2
$
D
S
U
M
Dir
ctrl
st vA -> wr pA
R/reply
R/req
P1: pA
P2: pA
R/req
W/req E
R/_
R/_
R/_
Invalidate pA
Read_to_update pA
Inv ACK
RX/invalidate&reply
S
S
S
D
E
reply xD(pA)
W/req E
W/_
Inv/_
Inv/_
EX

## Slide 70: Example Directory Protocol (Wr to Ex)
E
S
I
P1
$
E
S
I
P2
$
D
S
U
M
Dir
ctrl
R/reply
R/req
P1: pA
st vA -> wr pA
R/req
W/req E
R/_
R/_
R/_
Reply xD(pA)
Write_back pA
Read_toUpdate pA
RX/invalidate&reply
D
E
Inv pA
W/req E
W/_
Inv/_
Inv/_
W/req E
W/_
I
E
W/req E
RU/_

## Slide 71: A Popular Middle Ground
Two-level “hierarchy”
Individual nodes are multiprocessors, connected non-hiearchically
  e.g. mesh of SMPs
Coherence across nodes is directory-based
  directory keeps track of nodes, not individual processors
Coherence within nodes is snooping or directory
  orthogonal, but needs a good interface of functionality
SMP on a chip directory + snoop?

## Slide 72: And in Conclusion …
Caches contain all information on state of cached memory blocks
Snooping cache over shared medium for smaller MP by invalidating other cached copies on write
Sharing cached data  Coherence (values returned by a read), Consistency (when a written value will be returned by a read)
Snooping and Directory Protocols similar; bus makes snooping easier because of broadcast (snooping => uniform memory access)
Directory has extra data structure to keep track of state of all cache blocks
Distributing directory => scalable shared address multiprocessor => Cache coherent, Non uniform memory access