## Slide 1: EECS 252 Graduate Computer Architecture Lec 14 – Directory Based Multiprocessors
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://vlsi.cs.berkeley.edu/cs252-s06

## Slide 2: Review
Caches contain all information on state of cached memory blocks
Snooping cache over shared medium for smaller MP by invalidating other cached copies on write
Sharing cached data  Coherence (values returned by a read), Consistency (when a written value will be returned by a read)

## Slide 3: Outline
Review
Coherence traffic and Performance on MP
Directory-based protocols and examples
Administrivia
Synchronization
Relaxed Consistency Models
Fallacies and Pitfalls
Cautionary Tale
Conclusion

## Slide 4: Performance of Symmetric Shared-Memory Multiprocessors
Cache performance is combination of
Uniprocessor cache miss traffic
Traffic caused by communication
  Results in invalidations and subsequent cache misses
4th C: coherence miss
  Joins Compulsory, Capacity, Conflict

## Slide 5: Coherency Misses
True sharing misses arise from the communication of data through the cache coherence mechanism
  Invalidates due to 1st write to shared block
  Reads by another CPU of modified block in different cache
  Miss would still occur if block size were 1 word
False sharing misses when a block is invalidated because some word in the block, other than the one being read, is written into
  Invalidation does not cause a new value to be communicated, but only causes an extra cache miss
  Block is shared, but no word in block is actually shared  miss would not occur if block size were 1 word

## Slide 6: Example: True v. False Sharing v. Hit?
Time | P1 | P2 | True, False, Hit? Why?
1 | Write x1 |  | 
2 |  | Read x2 | 
3 | Write x1 |  | 
4 |  | Write x2 | 
5 | Read x2 |  | 
Assume x1 and x2 in same cache block. P1 and P2 both read x1 and x2 before.
True miss; invalidate x1 in P2
False miss; x1 irrelevant to P2
False miss; x1 irrelevant to P2
False miss; x1 irrelevant to P2
True miss; invalidate x2 in P1

## Slide 7: MP Performance 4 Processor Commercial Workload: OLTP, Decision Support (Database), Search Engine
True sharing and false sharing unchanged going from 1 MB to 8 MB (L3 cache)
Uniprocessor cache misses improve with cache size increase (Instruction, Capacity/Conflict, Compulsory)
(Memory) Cycles per Instruction

## Slide 8: MP Performance 2MB Cache Commercial Workload: OLTP, Decision Support (Database), Search Engine
True sharing, false sharing increase going from 1 to 8 CPUs
(Memory) Cycles per Instruction

## Slide 9: A Cache Coherent System Must:
Provide set of states, state transition diagram, and actions
Manage coherence protocol
  (0) Determine when to invoke coherence protocol
  (a) Find info about state of block in other caches to determine action
    whether need to communicate with other cached copies
  (b) Locate the other copies
  (c) Communicate with those copies (invalidate/update)
(0) is done the same way on all systems
  state of the line is maintained in the cache
  protocol is invoked if an “access fault” occurs on the line
Different approaches distinguished by (a) to (c)

## Slide 10: Bus-based Coherence
All of (a), (b), (c) done through broadcast on bus
  faulting processor sends out a “search”
  others respond to the search probe and take necessary action
Could do it in scalable network too
  broadcast to all processors, and let them respond
Conceptually simple, but broadcast doesn’t scale with p
  on bus, bus bandwidth doesn’t scale
  on scalable network, every fault leads to at least p network transactions
Scalable coherence:
  can have same cache states and state transition diagram
  different mechanisms to manage protocol

## Slide 11: Scalable Approach: Directories
Every memory block has associated directory information
  keeps track of copies of cached blocks and their states
  on a miss, find directory entry, look it up, and communicate only with the nodes that have copies if necessary
  in scalable networks, communication with directory and copies is through network transactions
Many alternatives for organizing directory information

## Slide 12: Basic Operation of Directory
• k processors.
• With each cache-block in memory: k presence-bits, 1 dirty-bit
• With each cache-block in cache: 1 valid bit, and 1 dirty (owner) bit
• Read from main memory by processor i:
  • If dirty-bit OFF then { read from main memory; turn p[i] ON; }
  • if dirty-bit ON then { recall line from dirty proc (cache state to shared); update memory; turn dirty-bit OFF; turn p[i] ON; supply recalled data to i;}
• Write to main memory by processor i:
  • If dirty-bit OFF then { supply data to i; send invalidations to all caches that have the block; turn dirty-bit ON; turn p[i] ON; ... }
  • ...

## Slide 13: Directory Protocol
Similar to Snoopy Protocol: Three states
  Shared: ≥ 1 processors have data, memory up-to-date
  Uncached (no processor hasit; not valid in any cache)
  Exclusive: 1 processor (owner) has data; memory out-of-date
In addition to cache state, must track which processors have data when in the shared state (usually bit vector, 1 if processor has copy)
Keep it simple(r):
  Writes to non-exclusive data  write miss
  Processor blocks until access completes
  Assume messages received and acted upon in order sent

## Slide 14: Directory Protocol
No bus and don’t want to broadcast:
  interconnect no longer single arbitration point
  all messages have explicit responses
Terms: typically 3 processors involved
  Local node where a request originates
  Home node where the memory location of an address resides
  Remote node has a copy of a cache block, whether exclusive or shared
Example messages on next slide: P = processor number, A = address

## Slide 15: CS 252 Administrivia
Due Friday: Problem Set and Comments on 2 papers
  Problem Set Assignment done in pairs
  Gene Amdahl, "Validity of the Single Processor Approach to Achieving Large-Scale Computing Capabilities", AFIPS Conference Proceedings, (30), pp. 483-485, 1967.
  Lorin Hochstein et al "Parallel Programmer Productivity: A Case Study of Novice Parallel Programmers." International Conference for High Performance Computing, (SC'05). November 2005
Be sure to comment
  Amdahl: How long is paper? How much of it is Amdahl’s Law? What other comments about parallelism besides Amdahl’s Law?
  Hochstein: What programming styles investigated? What was methodology? How would you redesign the experiment they did? What other metrics would be important to capture? Assuming these results of programming productivity reflect the real world, what should architectures of the future do (or not do)?
Monday March 20 Quiz 5-8 PM 405 Soda
Wed March 22 no class: project meetings in 635 Soda

## Slide 16: Computers in the News
“Core” new microarchitecture; last Pentium 4 (2000)
  Wide Dynamic Execution: 4 issue + Combine 2 simple instructions into 1 powerful (“macrofusion”)
  Advanced Digital Media Boost: All SSE instructions 1 clock cycle
  Smart Memory Access: lets one core control the whole cache when the other core is idle, and governs how the same data can be shared by both cores
  Intelligent Power Capability: shut down unneeded portions of chip
80% more performance, 40% less power
4 core chips in 2007 (2 copies of dual core?)
  CTO: "Intel is taking a conservative approach that focuses on single-thread performance. You won't see mediocre thread performance just for the sake of getting multiple cores on a die.”
CTO urged software companies to support multicore designs with software that can efficiently divide tasks among multiple execution threads. "It's really time to get onboard the multithreaded train"

## Slide 17: Directory Protocol Messages (Fig 4.22)
Message type Source Destination Msg Content
Read miss Local cache Home directory P, A
  Processor P reads data at address A; make P a read sharer and request data
Write miss Local cache Home directory P, A
  Processor P has a write miss at address A; make P the exclusive owner and request data
Invalidate Home directory Remote caches A
  Invalidate a shared copy at address A
Fetch Home directory Remote cache A
  Fetch the block at address A and send it to its home directory; change the state of A in the remote cache to shared
Fetch/Invalidate Home directory Remote cache A
  Fetch the block at address A and send it to its home directory; invalidate the block in the cache
Data value reply Home directory Local cache Data
  Return a data value from the home memory (read miss response)
Data write back Remote cache Home directory A, Data
  Write back a data value for address A (invalidate response)

## Slide 18: State Transition Diagram for One Cache Block in Directory Based System
States identical to snoopy case; transactions very similar
Transitions caused by read misses, write misses, invalidates, data fetch requests
Generates read miss & write miss message to home directory
Write misses that were broadcast on the bus for snooping  explicit invalidate & data fetch requests
Note: on a write, a cache block is bigger, so need to read the full cache block

## Slide 19: CPU -Cache State Machine
State machine for CPU requests for each memory block
Invalid state if in memory
Fetch/Invalidate
send Data Write Back message
to home directory
Invalidate
Invalid
Exclusive
(read/write)
CPU Read
CPU Read hit
Send Read Miss
message
CPU Write: Send Write Miss
msg to home directory
CPU Write: Send Write Miss message
to home directory
CPU read hit
CPU write hit
Fetch: send Data Write Back message to home directory
CPU read miss:
Send Read Miss
CPU write miss:
send Data Write Back message
and Write Miss to home directory
CPU read miss: send Data Write Back message and read miss to home directory
Shared
(read/only)
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 20: State Transition Diagram for Directory
Same states & structure as the transition diagram for an individual cache
2 actions: update of directory state & send messages to satisfy requests
Tracks all copies of memory block
Also indicates an action that updates the sharing set, Sharers, as well as sending a message

## Slide 21: Directory State Machine
State machine for Directory requests for each memory block
Uncached state if in memory
Data Write Back:
Sharers = {}
(Write back block)
Uncached
Shared
(read only)
Exclusive
(read/write)
Read miss:
Sharers = {P}
send Data Value
Reply
Write Miss:
send Invalidate
to Sharers;
then Sharers = {P};
send Data Value
Reply msg
Write Miss:
Sharers = {P};
send Data
Value Reply
msg
Read miss:
Sharers += {P};
send Fetch;
send Data Value Reply
msg to remote cache
(Write back block)
Read miss:
Sharers += {P};
send Data Value Reply
Write Miss:
Sharers = {P};
send Fetch/Invalidate;
send Data Value Reply
msg to remote cache
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 22: Example Directory Protocol
Message sent to directory causes two actions:
  Update the directory
  More messages to satisfy request
Block is in Uncached state: the copy in memory is the current value; only possible requests for that block are:
  Read miss: requesting processor sent data from memory &requestor made only sharing node; state of block made Shared.
  Write miss: requesting processor is sent the value & becomes the Sharing node. The block is made Exclusive to indicate that the only valid copy is cached. Sharers indicates the identity of the owner.
Block is Shared  the memory value is up-to-date:
  Read miss: requesting processor is sent back the data from memory & requesting processor is added to the sharing set.
  Write miss: requesting processor is sent the value. All processors in the set Sharers are sent invalidate messages, & Sharers is set to identity of requesting processor. The state of the block is made Exclusive.

## Slide 23: Example Directory Protocol
Block is Exclusive: current value of the block is held in the cache of the processor identified by the set Sharers (the owner)  three possible directory requests:
  Read miss: owner processor sent data fetch message, causing state of block in owner’s cache to transition to Shared and causes owner to send data to directory, where it is written to memory & sent back to requesting processor. Identity of requesting processor is added to set Sharers, which still contains the identity of the processor that was the owner (since it still has a readable copy). State is shared.
  Data write-back: owner processor is replacing the block and hence must write it back, making memory copy up-to-date (the home directory essentially becomes the owner), the block is now Uncached, and the Sharer set is empty.
  Write miss: block has a new owner. A message is sent to old owner causing the cache to send the value of the block to the directory from which it is sent to the requesting processor, which becomes the new owner. Sharers is set to identity of new owner, and state of block is made Exclusive.

## Slide 24: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory

## Slide 25: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory

## Slide 26: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory

## Slide 27: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory
A1
Write Back
A1

## Slide 28: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory
A1
A1

## Slide 29: Example
P2: Write 20 to A1
A1 and A2 map to the same cache block (but different memory block addresses A1 ≠ A2)
Processor 1
Processor 2
Interconnect
Memory
Directory
A1
A1

## Slide 30: Implementing a Directory
We assume operations atomic, but they are not; reality is much harder; must avoid deadlock when run out of buffers in network (see Appendix E)
Optimizations:
  read miss or write miss in Exclusive: send data directly to requestor from owner vs. 1st to memory and then from memory to requestor

## Slide 31: Basic Directory Transactions

## Slide 32: Example Directory Protocol (1st Read)
E
S
I
P1
$
E
S
I
P2
$
D
S
U
M
Dir
ctrl
ld vA -> rd pA
Read pA
R/reply
R/req
P1: pA
S
S

## Slide 33: Example Directory Protocol (Read Share)
E
S
I
P1
$
E
S
I
P2
$
D
S
U
M
Dir
ctrl
ld vA -> rd pA
R/reply
R/req
P1: pA
ld vA -> rd pA
P2: pA
R/req
R/_
R/_
R/_
S
S
S

## Slide 34: Example Directory Protocol (Wr to shared)
E
S
I
P1
$
E
S
I
P2
$
D
S
U
M
Dir
ctrl
st vA -> wr pA
R/reply
R/req
P1: pA
P2: pA
R/req
W/req E
R/_
R/_
R/_
Invalidate pA
Read_to_update pA
Inv ACK
RX/invalidate&reply
S
S
S
D
E
reply xD(pA)
W/req E
W/_
Inv/_
EX

## Slide 35: Example Directory Protocol (Wr to Ex)
E
S
I
P1
$
E
S
I
P2
$
D
S
U
M
Dir
ctrl
R/reply
R/req
P1: pA
st vA -> wr pA
R/req
W/req E
R/_
R/_
R/_
Reply xD(pA)
Write_back pA
Read_toUpdate pA
RX/invalidate&reply
D
E
Inv pA
W/req E
W/_
Inv/_
Inv/_
W/req E
W/_
I
E
W/req E
RU/_

## Slide 36: A Popular Middle Ground
Two-level “hierarchy”
Individual nodes are multiprocessors, connected non-hiearchically
  e.g. mesh of SMPs
Coherence across nodes is directory-based
  directory keeps track of nodes, not individual processors
Coherence within nodes is snooping or directory
  orthogonal, but needs a good interface of functionality
SMP on a chip directory + snoop?

## Slide 37: Synchronization
Why Synchronize? Need to know when it is safe for different processes to use shared data
Issues for Synchronization:
  Uninterruptable instruction to fetch and update memory (atomic operation);
  User level synchronization operation using this primitive;
  For large scale MPs, synchronization can be a bottleneck; techniques to reduce contention and latency of synchronization

## Slide 38: Uninterruptable Instruction to Fetch and Update Memory
Atomic exchange: interchange a value in a register for a value in memory
  0  synchronization variable is free
  1  synchronization variable is locked and unavailable
  Set register to 1 & swap
  New value in register determines success in getting lock 0 if you succeeded in setting the lock (you were first) 1 if other processor had already claimed access
  Key is that exchange operation is indivisible
Test-and-set: tests a value and sets it if the value passes the test
Fetch-and-increment: it returns the value of a memory location and atomically increments it
  0  synchronization variable is free

## Slide 39: Uninterruptable Instruction to Fetch and Update Memory
Hard to have read & write in 1 instruction: use 2 instead
Load linked (or load locked) + store conditional
  Load linked returns the initial value
  Store conditional returns 1 if it succeeds (no other store to same memory location since preceding load) and 0 otherwise
Example doing atomic swap with LL & SC:
try: mov R3,R4 ; mov exchange value ll R2,0(R1) ; load linked sc R3,0(R1) ; store conditional beqz R3,try ; branch store fails (R3 = 0) mov R4,R2 ; put load value in R4
Example doing fetch & increment with LL & SC:
try: ll R2,0(R1) ; load linked addi R2,R2,#1 ; increment (OK if reg–reg) sc R2,0(R1) ; store conditional beqz R2,try ; branch store fails (R2 = 0)

## Slide 40: User Level Synchronization—Operation Using this Primitive
Spin locks: processor continuously tries to acquire, spinning around a loop trying to get the lock li R2,#1 lockit: exch R2,0(R1) ;atomic exchange bnez R2,lockit ;already locked?
What about MP with cache coherency?
  Want to spin on cache copy to avoid full memory latency
  Likely to get cache hits for such variables
Problem: exchange includes a write, which invalidates all other copies; this generates considerable bus traffic
Solution: start by simply repeatedly reading the variable; when it changes, then try exchange (“test and test&set”):
try: li R2,#1 lockit: lw R3,0(R1) ;load var bnez R3,lockit ;≠ 0  not free  spin exch R2,0(R1) ;atomic exchange bnez R2,try ;already locked?

## Slide 41: Another MP Issue: Memory Consistency Models
What is consistency? When must a processor see the new value? e.g., seems that
P1: A = 0; P2: B = 0;
..... .....
A = 1; B = 1;
L1: if (B == 0) ... L2: if (A == 0) ...
Impossible for both if statements L1 & L2 to be true?
  What if write invalidate is delayed & processor continues?
Memory consistency models: what are the rules for such cases?
Sequential consistency: result of any execution is the same as if the accesses of each processor were kept in order and the accesses among different processors were interleaved  assignments before ifs above
  SC: delay all memory accesses until all invalidates done

## Slide 42: Memory Consistency Model
Schemes faster execution to sequential consistency
Not an issue for most programs; they are synchronized
  A program is synchronized if all access to shared data are ordered by synchronization operations
  write (x) ... release (s) {unlock} ... acquire (s) {lock} ... read(x)
Only those programs willing to be nondeterministic are not synchronized: “data race”: outcome f(proc. speed)
Several Relaxed Models for Memory Consistency since most programs are synchronized; characterized by their attitude towards: RAR, WAR, RAW, WAW to different addresses

## Slide 43: Relaxed Consistency Models: The Basics
Key idea: allow reads and writes to complete out of order, but to use synchronization operations to enforce ordering, so that a synchronized program behaves as if the processor were sequentially consistent
  By relaxing orderings, may obtain performance advantages
  Also specifies range of legal compiler optimizations on shared data
  Unless synchronization points are clearly defined and programs are synchronized, compiler could not interchange read and write of 2 shared data items because might affect the semantics of the program
3 major sets of relaxed orderings:
W→R ordering (all writes completed before next read)
  Because retains ordering among writes, many programs that operate under sequential consistency operate under this model, without additional synchronization. Called processor consistency
W → W ordering (all writes completed before next write)
R → W and R → R orderings, a variety of models depending on ordering restrictions and how synchronization operations enforce ordering
Many complexities in relaxed consistency models; defining precisely what it means for a write to complete; deciding when processors can see values that it has written

## Slide 44: Mark Hill observation
Instead, use speculation to hide latency from strict consistency model
  If processor receives invalidation for memory reference before it is committed, processor uses speculation recovery to back out computation and restart with invalidated memory reference
Aggressive implementation of sequential consistency or processor consistency gains most of advantage of more relaxed models
Implementation adds little to implementation cost of speculative processor
Allows the programmer to reason using the simpler programming models

## Slide 45: Cross Cutting Issues: Performance Measurement of Parallel Processors
Performance: how well scale as increase Proc
Speedup fixed as well as scaleup of problem
  Assume benchmark of size n on p processors makes sense: how scale benchmark to run on m * p processors?
  Memory-constrained scaling: keeping the amount of memory used per processor constant
  Time-constrained scaling: keeping total execution time, assuming perfect speedup, constant
Example: 1 hour on 10 P, time ~ O(n3), 100 P?
  Time-constrained scaling: 1 hour  101/3n  2.15n scale up
  Memory-constrained scaling: 10n size  103/10  100X or 100 hours! 10X processors for 100X longer???
  Need to know application well to scale: # iterations, error tolerance

## Slide 46: Fallacy: Amdahl’s Law doesn’t apply to parallel computers
Since some part linear, can’t go 100X?
1987 claim to break it, since 1000X speedup
  researchers scaled the benchmark to have a data set size that is 1000 times larger and compared the uniprocessor and parallel execution times of the scaled benchmark. For this particular algorithm the sequential portion of the program was constant independent of the size of the input, and the rest was fully parallel—hence, linear speedup with 1000 processors
Usually sequential scale with data too

## Slide 47: Fallacy: Linear speedups are needed to make multiprocessors cost-effective
Mark Hill & David Wood 1995 study
Compare costs SGI uniprocessor and MP
Uniprocessor = $38,400 + $100 * MB
MP = $81,600 + $20,000 * P + $100 * MB
1 GB, uni = $138k v. mp = $181k + $20k * P
What speedup for better MP cost performance?
8 proc = $341k; $341k/138k  2.5X
16 proc  need only 3.6X, or 25% linear speedup
Even if need some more memory for MP, not linear

## Slide 48: Fallacy: Scalability is almost free
“build scalability into a multiprocessor and then simply offer the multiprocessor at any point on the scale from a small number of processors to a large number”
Cray T3E scales to 2048 CPUs vs. 4 CPU Alpha
  At 128 CPUs, it delivers a peak bisection BW of 38.4 GB/s, or 300 MB/s per CPU (uses Alpha microprocessor)
  Compaq Alphaserver ES40 up to 4 CPUs and has 5.6 GB/s of interconnect BW, or 1400 MB/s per CPU
Build apps that scale requires significantly more attention to load balance, locality, potential contention, and serial (or partly parallel) portions of program. 10X is very hard

## Slide 49: Pitfall: Not developing SW to take advantage (or optimize for) multiprocessor architecture
SGI OS protects the page table data structure with a single lock, assuming that page allocation is infrequent
Suppose a program uses a large number of pages that are initialized at start-up
Program parallelized so that multiple processes allocate the pages
But page allocation requires lock of page table data structure, so even an OS kernel that allows multiple threads will be serialized at initialization (even if separate processes)

## Slide 50: Answers to 1995 Questions about Parallelism
In the 1995 edition of this text, we concluded the chapter with a discussion of two then current controversial issues.
What architecture would very large scale, microprocessor-based multiprocessors use?
What was the role for multiprocessing in the future of microprocessor architecture?
Answer 1. Large scale multiprocessors did not become a major and growing market  clusters of single microprocessors or moderate SMPs
Answer 2. Astonishingly clear. For at least for the next 5 years, future MPU performance comes from the exploitation of TLP through multicore processors vs. exploiting more ILP

## Slide 51: Cautionary Tale
Key to success of birth and development of ILP in 1980s and 1990s was software in the form of optimizing compilers that could exploit ILP
Similarly, successful exploitation of TLP will depend as much on the development of suitable software systems as it will on the contributions of computer architects
Given the slow progress on parallel software in the past 30+ years, it is likely that exploiting TLP broadly will remain challenging for years to come

## Slide 52: And in Conclusion …
Snooping and Directory Protocols similar; bus makes snooping easier because of broadcast (snooping  uniform memory access)
Directory has extra data structure to keep track of state of all cache blocks
Distributing directory  scalable shared address multiprocessor  Cache coherent, Non uniform memory access
MPs are highly effective for multiprogrammed workloads
MPs proved effective for intensive commercial workloads, such as OLTP (assuming enough I/O to be CPU-limited), DSS applications (where query optimization is critical), and large-scale, web searching applications