## Slide 1: EECS 252 Graduate Computer Architecture Lec 15 – T1 (“Niagara”) and Papers Discussion
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://vlsi.cs.berkeley.edu/cs252-s06

## Slide 2: Review
Caches contain all information on state of cached memory blocks
Snooping cache over shared medium for smaller MP by invalidating other cached copies on write
Sharing cached data  Coherence (values returned by a read), Consistency (when a written value will be returned by a read)
Snooping and Directory Protocols similar; bus makes snooping easier because of broadcast (snooping => uniform memory access)
Directory has extra data structure to keep track of state of all cache blocks
Distributing directory => scalable shared address multiprocessor => Cache coherent, Non uniform memory access

## Slide 3: Outline
Consistency
Cross Cutting Issues
Fallacies and Pitfalls
Administrivia
Sun T1 (“Niagara”) Multiprocessor
2 paper discussion

## Slide 4: Another MP Issue: Memory Consistency Models
What is consistency? When must a processor see the new value? e.g., seems that
P1: A = 0; P2: B = 0;
..... .....
A = 1; B = 1;
L1: if (B == 0) ... L2: if (A == 0) ...
Impossible for both if statements L1 & L2 to be true?
  What if write invalidate is delayed & processor continues?
Memory consistency models: what are the rules for such cases?
Sequential consistency: result of any execution is the same as if the accesses of each processor were kept in order and the accesses among different processors were interleaved  assignments before ifs above
  SC: delay all memory accesses until all invalidates done

## Slide 5: Memory Consistency Model
Schemes faster execution to sequential consistency
Not an issue for most programs; they are synchronized
  A program is synchronized if all access to shared data are ordered by synchronization operations
  write (x) ... release (s) {unlock} ... acquire (s) {lock} ... read(x)
Only those programs willing to be nondeterministic are not synchronized: “data race”: outcome f(proc. speed)
Several Relaxed Models for Memory Consistency since most programs are synchronized; characterized by their attitude towards: RAR, WAR, RAW, WAW to different addresses

## Slide 6: Relaxed Consistency Models: The Basics
Key idea: allow reads and writes to complete out of order, but to use synchronization operations to enforce ordering, so that a synchronized program behaves as if the processor were sequentially consistent
  By relaxing orderings, may obtain performance advantages
  Also specifies range of legal compiler optimizations on shared data
  Unless synchronization points are clearly defined and programs are synchronized, compiler could not interchange read and write of 2 shared data items because might affect the semantics of the program
3 major sets of relaxed orderings:
W→R ordering (all writes completed before next read)
  Because retains ordering among writes, many programs that operate under sequential consistency operate under this model, without additional synchronization. Called processor consistency
W → W ordering (all writes completed before next write)
R → W and R → R orderings, a variety of models depending on ordering restrictions and how synchronization operations enforce ordering
Many complexities in relaxed consistency models; defining precisely what it means for a write to complete; deciding when processors can see values that it has written

## Slide 7: Mark Hill observation
Instead, use speculation to hide latency from strict consistency model
  If processor receives invalidation for memory reference before it is committed, processor uses speculation recovery to back out computation and restart with invalidated memory reference
Aggressive implementation of sequential consistency or processor consistency gains most of advantage of more relaxed models
Implementation adds little to implementation cost of speculative processor
Allows the programmer to reason using the simpler programming models

## Slide 8: Cross Cutting Issues: Performance Measurement of Parallel Processors
Performance: how well scale as increase Proc
Speedup fixed as well as scaleup of problem
  Assume benchmark of size n on p processors makes sense: how scale benchmark to run on m * p processors?
  Memory-constrained scaling: keeping the amount of memory used per processor constant
  Time-constrained scaling: keeping total execution time, assuming perfect speedup, constant
Example: 1 hour on 10 P, time ~ O(n3), 100 P?
  Time-constrained scaling: 1 hour  101/3n  2.15n scale up
  Memory-constrained scaling: 10n size  103/10  100X or 100 hours! 10X processors for 100X longer???
  Need to know application well to scale: # iterations, error tolerance

## Slide 9: Fallacy: Amdahl’s Law doesn’t apply to parallel computers
Since some part linear, can’t go 100X?
1987 claim to break it, since 1000X speedup
  researchers scaled the benchmark to have a data set size that is 1000 times larger and compared the uniprocessor and parallel execution times of the scaled benchmark. For this particular algorithm the sequential portion of the program was constant independent of the size of the input, and the rest was fully parallel—hence, linear speedup with 1000 processors
Usually sequential scale with data too

## Slide 10: Fallacy: Linear speedups are needed to make multiprocessors cost-effective
Mark Hill & David Wood 1995 study
Compare costs SGI uniprocessor and MP
Uniprocessor = $38,400 + $100 * MB
MP = $81,600 + $20,000 * P + $100 * MB
1 GB, uni = $138k v. mp = $181k + $20k * P
What speedup for better MP cost performance?
8 proc = $341k; $341k/138k  2.5X
16 proc  need only 3.6X, or 25% linear speedup
Even if need some more memory for MP, not linear

## Slide 11: Fallacy: Scalability is almost free
“build scalability into a multiprocessor and then simply offer the multiprocessor at any point on the scale from a small number of processors to a large number”
Cray T3E scales to 2048 CPUs vs. 4 CPU Alpha
  At 128 CPUs, it delivers a peak bisection BW of 38.4 GB/s, or 300 MB/s per CPU (uses Alpha microprocessor)
  Compaq Alphaserver ES40 up to 4 CPUs and has 5.6 GB/s of interconnect BW, or 1400 MB/s per CPU
Build apps that scale requires significantly more attention to load balance, locality, potential contention, and serial (or partly parallel) portions of program. 10X is very hard

## Slide 12: Pitfall: Not developing SW to take advantage (or optimize for) multiprocessor architecture
SGI OS protects the page table data structure with a single lock, assuming that page allocation is infrequent
Suppose a program uses a large number of pages that are initialized at start-up
Program parallelized so that multiple processes allocate the pages
But page allocation requires lock of page table data structure, so even an OS kernel that allows multiple threads will be serialized at initialization (even if separate processes)

## Slide 13: Answers to 1995 Questions about Parallelism
In the 1995 edition of this text, we concluded the chapter with a discussion of two then current controversial issues.
What architecture would very large scale, microprocessor-based multiprocessors use?
What was the role for multiprocessing in the future of microprocessor architecture?
Answer 1. Large scale multiprocessors did not become a major and growing market  clusters of single microprocessors or moderate SMPs
Answer 2. Astonishingly clear. For at least for the next 5 years, future MPU performance comes from the exploitation of TLP through multicore processors vs. exploiting more ILP

## Slide 14: Cautionary Tale
Key to success of birth and development of ILP in 1980s and 1990s was software in the form of optimizing compilers that could exploit ILP
Similarly, successful exploitation of TLP will depend as much on the development of suitable software systems as it will on the contributions of computer architects
Given the slow progress on parallel software in the past 30+ years, it is likely that exploiting TLP broadly will remain challenging for years to come

## Slide 15: CS 252 Administrivia
Wednesday March 15 MP Future Directions and Review
Monday March 20 Quiz 5-8 PM 405 Soda
Monday March 20 lecture – Q&A, problem sets with Archana
Wednesday March 22 no class: project meetings in 635 Soda
Spring Break March 27 – March 31
Chapter 6 Storage
Interconnect Appendix

## Slide 16: T1 (“Niagara”)
Target: Commercial server applications
  High thread level parallelism (TLP)
    Large numbers of parallel client requests
  Low instruction level parallelism (ILP)
    High cache miss rates
    Many unpredictable branches
    Frequent load-load dependencies
Power, cooling, and space are major concerns for data centers
Metric: Performance/Watt/Sq. Ft.
Approach: Multicore, Fine-grain multithreading, Simple pipeline, Small L1 caches, Shared L2

## Slide 17: T1 Architecture
Also ships with 6 or 4 processors

## Slide 18: T1 pipeline
Single issue, in-order, 6-deep pipeline: F, S, D, E, M, W
3 clock delays for loads & branches.
Shared units:
  L1 $, L2 $
  TLB
  X units
  pipe registers
Hazards:
  Data
  Structural

## Slide 19: T1 Fine-Grained Multithreading
Each core supports four threads and has its own level one caches (16KB for instructions and 8 KB for data)
Switching to a new thread on each clock cycle
Idle threads are bypassed in the scheduling
  Waiting due to a pipeline delay or cache miss
  Processor is idle only when all 4 threads are idle or stalled
Both loads and branches incur a 3 cycle delay that can only be hidden by other threads
A single set of floating point functional units is shared by all 8 cores
  floating point performance was not a focus for T1

## Slide 20: Memory, Clock, Power
16 KB 4 way set assoc. I$/ core
8 KB 4 way set assoc. D$/ core
3MB 12 way set assoc. L2 $ shared
  4 x 750KB independent banks
  crossbar switch to connect
  2 cycle throughput, 8 cycle latency
  Direct link to DRAM & Jbus
  Manages cache coherence for the 8 cores
  CAM based directory
Coherency is enforced among the L1 caches by a directory associated with each L2 cache block
Used to track which L1 caches have copies of an L2 block
By associating each L2 with a particular memory bank and enforcing the subset property, T1 can place the directory at L2 rather than at the memory, which reduces the directory overhead
L1 data cache is write-through, only invalidation messages are required; the data can always be retrieved from the L2 cache
1.2 GHz at 72W typical, 79W peak power consumption
Write through
  allocate LD
  no-allocate ST

## Slide 21: Miss Rates: L2 Cache Size, Block Size
T1

## Slide 22: Miss Latency: L2 Cache Size, Block Size
T1

## Slide 23: CPI Breakdown of Performance
Benchmark | Per Thread CPI | Per core CPI | Effective CPI for 8 cores | Effective IPC for 8 cores
TPC-C | 7.20 | 1.80 | 0.23 | 4.4
SPECJBB | 5.60 | 1.40 | 0.18 | 5.7
SPECWeb99 | 6.60 | 1.65 | 0.21 | 4.8

## Slide 24: Not Ready Breakdown
TPC-C - store buffer full is largest contributor
SPEC-JBB - atomic instructions are largest contributor
SPECWeb99 - both factors contribute

## Slide 25: Performance: Benchmarks + Sun Marketing
Benchmark\Architecture | Sun Fire T2000 | IBM p5-550 with 2 dual-core Power5 chips | Dell PowerEdge
SPECjbb2005 (Java server software) business operations/ sec | 63,378 | 61,789 | 24,208 (SC1425 with dual single-core Xeon)
SPECweb2005 (Web server performance) | 14,001 | 7,881 | 4,850 (2850 with two dual-core Xeon processors)
NotesBench (Lotus Notes performance) | 16,061 | 14,740 | 
Space, Watts, and Performance

## Slide 26: HP marketing view of T1 Niagara
Sun’s radical UltraSPARC T1 chip is made up of individual cores that have much slower single thread performance when compared to the higher performing cores of the Intel Xeon, Itanium, AMD Opteron or even classic UltraSPARC processors.
The Sun Fire T2000 has poor floating-point performance, by Sun’s own admission.
The Sun Fire T2000 does not support commerical Linux or Windows® and requires a lock-in to Sun and Solaris.
The UltraSPARC T1, aka CoolThreads, is new and unproven, having just been introduced in December 2005.
In January 2006, a well-known financial analyst downgraded Sun on concerns over the UltraSPARC T1’s limitation to only the Solaris operating system, unique requirements, and longer adoption cycle, among other things. [10]
Where is the compelling value to warrant taking such a risk?
http://h71028.www7.hp.com/ERC/cache/280124-0-0-0-121.html

## Slide 27: Microprocessor Comparison
Processor | SUN T1 | Opteron | Pentium D | IBM Power 5
Cores | 8 | 2 | 2 | 2
Instruction issues / clock / core | 1 | 3 | 3 | 4
Peak instr. issues / chip | 8 | 6 | 6 | 8
Multithreading | Fine-grained | No | SMT | SMT
L1 I/D in KB per core | 16/8 | 64/64 | 12K uops/16 | 64/32
L2 per core/shared | 3 MB shared | 1MB / core | 1MB/ core | 1.9 MB shared
Clock rate (GHz) | 1.2 | 2.4 | 3.2 | 1.9
Transistor count (M) | 300 | 233 | 230 | 276
Die size (mm2) | 379 | 199 | 206 | 389
Power (W) | 79 | 110 | 130 | 125

## Slide 28: Performance Relative to Pentium D

## Slide 29: Performance/mm2, Performance/Watt

## Slide 30: Niagara 2
Improve performance by increasing threads supported per chip from 32 to 64
  8 cores * 8 threads per core
Floating-point unit for each core, not for each chip
Hardware support for encryption standards EAS, 3DES, and elliptical-curve cryptography
Niagara 2 will add a number of 8x PCI Express interfaces directly into the chip in addition to integrated 10Gigabit Ethernet XAU interfaces and Gigabit Ethernet ports.
Integrated memory controllers will shift support from DDR2 to FB-DIMMs and double the maximum amount of system memory.
Kevin Krewell
“Sun's Niagara Begins CMT Flood -
The Sun UltraSPARC T1 Processor Released”
Microprocessor Report, January 3, 2006

## Slide 31: Amdahl’s Law Paper
Gene Amdahl, "Validity of the Single Processor Approach to Achieving Large-Scale Computing Capabilities", AFIPS Conference Proceedings, (30), pp. 483-485, 1967.
How long is paper?
How much of it is Amdahl’s Law?
What other comments about parallelism besides Amdahl’s Law?
Notes: 4th paragraph has Amdahl’s Law
Irregular boundaries
Inhomogeneous interriors
Computations dependent on many state varieables
Propagation rates of physical effects may be different
Rate of convergenece, or convergence at all depends on order of going along axes

## Slide 32: Parallel Programmer Productivity
Lorin Hochstein et al "Parallel Programmer Productivity: A Case Study of Novice Parallel Programmers." International Conference for High Performance Computing, Networking and Storage (SC'05). Nov. 2005
What did they study?
What is argument that novice parallel programmers are a good target for High Performance Computing?
How can account for variability in talent between programmers?
What programmers studied?
What programming styles investigated?
How big multiprocessor?
How measure quality?
How measure cost?
Notes: Within subject study; lots of examples; measure difference between programmers
Grad classes at Maryland, USC, UCSB, MIT
Diaries and measuring programming time on tools
Message Passing (MPI) vs. Shared Memory (OpenMP)
Also Parallel Matlab (StarP), and Parallel C (XMT)
Cost = effort time: Keep track of programmer experience
Also Lines of Code expansion over the sequential program
Cost/LOC
8 Processors, Speedup = quality

## Slide 33: Parallel Programmer Productivity
Lorin Hochstein et al "Parallel Programmer Productivity: A Case Study of Novice Parallel Programmers." International Conference for High Performance Computing, Networking and Storage (SC'05). Nov. 2005
What hypotheses investigated?
What were results?
Assuming these results of programming productivity reflect the real world, what should architectures of the future do (or not do)?
How would you redesign the experiment they did?
What other metrics would be important to capture?
Role of Human Subject Experiments in Future of Computer Systems Evaluation?
Notes: Can novices achieve speedup?
Yes 4X
MPI requires mode code?
Yes 2X-4X
OpenMP requires more code?
10%
Will require more time than serial?
MPI: 2.5X time
OpenMP: 10% more time
Cost per line of code
2 minute/LOC serial
5 minutes/LOC MPI
25 minutes/LOC OpenMP
Code Expansion factor?