## Slide 1: EECS 252 Graduate Computer Architecture Lec 16 – Papers, MP Future Directions, and Midterm Review
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://vlsi.cs.berkeley.edu/cs252-s06

## Slide 2: Outline
ILP
Compiler techniques to increase ILP
Loop Unrolling
Static Branch Prediction
Dynamic Branch Prediction
Overcoming Data Hazards with Dynamic Scheduling
(Start) Tomasulo Algorithm
Conclusion

## Slide 3: Amdahl’s Law Paper
Gene Amdahl, "Validity of the Single Processor Approach to Achieving Large-Scale Computing Capabilities", AFIPS Conference Proceedings, (30), pp. 483-485, 1967.
How long is paper?
How much of it is Amdahl’s Law?
What other comments about parallelism besides Amdahl’s Law?
Notes: 4th paragraph has Amdahl’s Law
Irregular boundaries
Inhomogeneous interriors
Computations dependent on many state varieables
Propagation rates of physical effects may be different
Rate of convergenece, or convergence at all depends on order of going along axes

## Slide 4: Parallel Programmer Productivity
Lorin Hochstein et al "Parallel Programmer Productivity: A Case Study of Novice Parallel Programmers." International Conference for High Performance Computing, Networking and Storage (SC'05). Nov. 2005
What did they study?
What is argument that novice parallel programmers are a good target for High Performance Computing?
How can account for variability in talent between programmers?
What programmers studied?
What programming styles investigated?
How big multiprocessor?
How measure quality?
How measure cost?
Notes: Within subject study; lots of examples; measure difference between programmers
Grad classes at Maryland, USC, UCSB, MIT
Diaries and measuring programming time on tools
Message Passing (MPI) vs. Shared Memory (OpenMP)
Also Parallel Matlab (StarP), and Parallel C (XMT)
Cost = effort time: Keep track of programmer experience
Also Lines of Code expansion over the sequential program
Cost/LOC
8 Processors, Speedup = quality

## Slide 5: Parallel Programmer Productivity
Lorin Hochstein et al "Parallel Programmer Productivity: A Case Study of Novice Parallel Programmers." International Conference for High Performance Computing, Networking and Storage (SC'05). Nov. 2005
What hypotheses investigated?
What were results?
Assuming these results of programming productivity reflect the real world, what should architectures of the future do (or not do)?
How would you redesign the experiment they did?
What other metrics would be important to capture?
Role of Human Subject Experiments in Future of Computer Systems Evaluation?
Notes: Can novices achieve speedup?
Yes 4X
MPI requires mode code?
Yes 2X-4X
OpenMP requires more code?
10%
Will require more time than serial?
MPI: 2.5X time
OpenMP: 10% more time
Cost per line of code
2 minute/LOC serial
5 minutes/LOC MPI
25 minutes/LOC OpenMP
Code Expansion factor?

## Slide 6: CS 252 Administrivia
Monday March 20 Quiz 5-8 PM 405 Soda
Monday March 20 lecture – Q&A, problem sets with Archana
Wednesday March 22 no class: project meetings in 635 Soda
Spring Break March 27 – March 31
Chapter 5 Advanced Memory Hierarchy
Chapter 6 Storage
Interconnect Appendix

## Slide 7: High Level Message
Everything is changing
Old conventional wisdom is out
We DESPERATELY need a new architectural solution for microprocessors based on parallelism
  My focus is “All purpose” computers vs. “single purpose” computers  Each company gets to design one
Need to create a “watering hole” to bring everyone together to quickly find that solution
  architects, language designers, application experts, numerical analysts, algorithm designers, programmers, …

## Slide 8: Outline
Part I: A New Agenda for Computer Architecture
  Old Conventional Wisdom vs. New Conventional Wisdom
  New Metrics for Success
  Innovating at HW/SW interface without compilers
  New Classification for Architectures and Apps
Part II: A “Watering Hole” for Parallel Systems
  Research Accelerator for Multiple Processors
Conclusion
Notes: Key Advice on a bad career
Send part alternatives
First point is selecting a problem. Those who know the university promotion system know that promotion committees ask the question:
Is this person the leading person in their field?
How do you do that? First piece of bad advice

## Slide 9: Conventional Wisdom (CW) in Computer Architecture
Old CW: Power is free, Transistors expensive
New CW: “Power wall” Power expensive, Xtors free (Can put more on chip than can afford to turn on)
Old: Multiplies are slow, Memory access is fast
New: “Memory wall” Memory slow, multiplies fast (200 clocks to DRAM memory, 4 clocks for FP multiply)
Old : Increasing Instruction Level Parallelism via compilers, innovation (Out-of-order, speculation, VLIW, …)
New CW: “ILP wall” diminishing returns on more ILP
New: Power Wall + Memory Wall + ILP Wall = Brick Wall
  Old CW: Uniprocessor performance 2X / 1.5 yrs
  New CW: Uniprocessor performance only 2X / 5 yrs?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Uniprocessor Performance (SPECint)
VAX : 25%/year 1978 to 1986
RISC + x86: 52%/year 1986 to 2002
RISC + x86: ??%/year 2002 to present
From Hennessy and Patterson, Computer Architecture: A Quantitative Approach, 4th edition, 2006
 Sea change in chip design: multiple “cores” or processors per chip
3X
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Sea Change in Chip Design
Intel 4004 (1971): 4-bit processor, 2312 transistors, 0.4 MHz, 10 micron PMOS, 11 mm2 chip
Processor is the new transistor?
RISC II (1983): 32-bit, 5 stage pipeline, 40,760 transistors, 3 MHz, 3 micron NMOS, 60 mm2 chip
125 mm2 chip, 0.065 micron CMOS = 2312 RISC II+FPU+Icache+Dcache
  RISC II shrinks to  0.02 mm2 at 65 nm
  Caches via DRAM or 1 transistor SRAM (www.t-ram.com) ?
  Proximity Communication via capacitive coupling at > 1 TB/s ? (Ivan Sutherland @ Sun / Berkeley)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Déjà vu all over again?
“… today’s processors … are nearing an impasse as technologies approach the speed of light..”
David Mitchell, The Transputer: The Time Is Now (1989)
Transputer had bad timing (Uniprocessor performance)  Procrastination rewarded: 2X seq. perf. / 1.5 years
“We are dedicating all of our future product development to multicore designs. … This is a sea change in computing”
Paul Otellini, President, Intel (2005)
All microprocessor companies switch to MP (2X CPUs / 2 yrs)  Procrastination penalized: 2X sequential perf. / 5 yrs
Manufacturer/Year | AMD/’05 | Intel/’06 | IBM/’04 | Sun/’05
Processors/chip | 2 | 2 | 2 | 8
Threads/Processor | 1 | 2 | 2 | 4
Threads/chip | 2 | 4 | 4 | 32
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: 21st Century Computer Architecture
Old CW: Since cannot know future programs, find set of old programs to evaluate designs of computers for the future
  E.g., SPEC2006
What about parallel codes?
  Few available, tied to old models, languages, architectures, …
New approach: Design computers of future for numerical methods important in future
Claim: key methods for next decade are 7 dwarves (+ a few), so design for them!
  Representative codes may vary over time, but these numerical methods will be important for > 10 years

## Slide 14: High-end simulation in the physical sciences = 7 numerical methods:
Structured Grids (including locally structured grids, e.g. Adaptive Mesh Refinement)
Unstructured Grids
Fast Fourier Transform
Dense Linear Algebra
Sparse Linear Algebra
Particles
Monte Carlo
Well-defined targets from algorithmic, software, and architecture standpoint
Phillip Colella’s “Seven dwarfs”
If add 4 for embedded, covers all 41 EEMBC benchmarks
  8. Search/Sort
  9. Filter
  10. Combinational logic
  11. Finite State Machine
Note: Data sizes (8 bit to 32 bit) and types (integer, character) differ, but algorithms the same
Slide from “Defining Software Requirements for Scientific Computing”, Phillip Colella, 2004

## Slide 15: 6/11 Dwarves Covers 24/30 SPEC
SPECfp
  8 Structured grid
    3 using Adaptive Mesh Refinement
  2 Sparse linear algebra
  2 Particle methods
  5 TBD: Ray tracer, Speech Recognition, Quantum Chemistry, Lattice Quantum Chromodynamics (many kernels inside each benchmark?)
SPECint
  8 Finite State Machine
  2 Sorting/Searching
  2 Dense linear algebra (data type differs from dwarf)
  1 TBD: 1 C compiler (many kernels?)

## Slide 16: 21st Century Measures of Success
Old CW: Don’t waste resources on accuracy, reliability
  Speed kills competition
  Blame Microsoft for crashes
New CW: SPUR is critical for future of IT
  Security
  Privacy
  Usability (cost of ownership)
  Reliability
Success not limited to performance/cost
“20th century vs. 21st century C&C: the SPUR manifesto,” Communications of the ACM , 48:3, 2005.

## Slide 17: 21st Century Code Generation
Old CW: Takes a decade for compilers to introduce an architecture innovation
New approach: “Auto-tuners” 1st run variations of program on computer to find best combinations of optimizations (blocking, padding, …) and algorithms, then produce C code to be compiled for that computer
  E.g., PHiPAC (BLAS), Atlas (BLAS), Sparsity (Sparse linear algebra), Spiral (DSP), FFT-W
  Can achieve 10X over conventional compiler
One Auto-tuner per dwarf?
  Exist for Dense Linear Algebra, Sparse Linear Algebra, Spectral
Notes: <number>
<footer>
<header>
<date/time>
Autotuners is fine. I had a slightly longer list I was working on before seeing Krste's mail. PHiPAC: Dense linear algebra (Krste, Jim, Jeff Bilmes and others at UCB) PHiPAC = Portable High Performance Ansi C FFTW: Fastest Fourier Transforms in the West (from Matteo Frigo and Steve Johnson at MIT; Matteo is now at IBM) Atlas: Dense linear algebra now the "standard" for many BLAS implementations; used in Matlab, for example. (Jack Dongarra, Clint Whaley et al) Sparsity: Sparse linear algebra (Eun-Jin Im and Kathy at UCB) Spiral: DSP algorithms including FFTs and other transforms (Markus Pueschel, José M. F. Moura et al) OSKI: Sparse linear algebra (Rich Vuduc, Jim and Kathy, From the Bebop project at UCB) In addition there are groups at Rice, USC, UIUC, Cornell, UT Austin, UCB (Titanium), LLNL and others working on compilers that include an auto-tuning (Search-based) optimization phase. Both the Bebop group and the Atlas group have done work on automatic tuning of collective communication routines for supercomputers/clusters, but this is ongoing. I'll send a slide with an autotuning example later. Kathy

## Slide 18: Sparse Matrix – Search for Blocking
Reference
Best: 4x2
Mflop/s
Mflop/s
for finite element problem [Im, Yelick, Vuduc, 2005]
Notes: <number>
<footer>
<header>
<date/time>
[NOTE: This slide has some animation in it.]
Consider the following experiment in which we implement SpMV using BCSR format for the matrix shown in the previous slide at all block sizes that divide 8x8—16 implementations in all. These implementations fully unroll the innermost loop and use scalar replacement for the source and destination vectors. You might reasonably expect performance to increase relatively smoothly as r and c increase, but this is clearly not the case!
Platform: 900 MHz Itanium-2, 3.6 Gflop/s peak speed. Intel v8.0 compiler.
Good speedups (4x) but at an unexpected block size (4x2).
Figure taken from Im, Yelick, Vuduc, IJHPCA 2005 paper.

## Slide 19: Best Sparse Blocking for 8 Computers
All possible column block sizes selected for 8 computers; How could compiler know?
 | Intel Pentium M |  | Sun Ultra 2, Sun Ultra 3, AMD Opteron
IBM Power 4, Intel/HP Itanium | Intel/HP Itanium 2 | IBM Power 3 | 
8
4
2
1
1
2
4
8
row block size (r)
column block size (c)

## Slide 20: Operand Size and Type
Programmer should be able to specify data size, type independent of algorithm
1 bit (Boolean*)
8 bits (Integer, ASCII)
16 bits (Integer, DSP fixed pt, Unicode*)
32 bits (Integer, SP Fl. Pt., Unicode*)
64 bits (Integer, DP Fl. Pt.)
128 bits (Integer*, Quad Precision Fl. Pt.*)
1024 bits (Crypto*)
* Not supported well in most programming languages and optimizing compilers

## Slide 21: Style of Parallelism
Data Level Parallel
(Same operation
lots of data, 1 PC)
  Programmer wants code to run on as many parallel architectures as possible so (if possible)
  Architect wants to run as many different types of parallel programs as possible so
Simpler Programming model,
Less HW Control
More Flexible, More HW Control
Inst. Level Parallel
(Different operations
lots of data, 1 PC)
Thread Level Parallel
(Different operations
lots of data, N PCs)
Separate address
spaces
Single address space

## Slide 22: Parallel Framework – Apps (so far)
Original 7 dwarves: 6 data parallel, 1 Sep. Addr.TLP
Bonus 4 dwarves: 2 data parallel, 2 Separate Addr. TLP
EEMBC (Embedded): DLP 19, 12 Separate Addr. TLP
SPEC (Desktop): 14 DLP, 2 Separate Address TLP
E E
M
B
C
E E
M
B
C
S
P
E
C
S
P
E
C
D
w
a
r
f
S
D
W
A
R
F
S
Most New Architectures
Most Important Apps?
DLP ILP
TLP
Separate Addresses
Shared Address

## Slide 23: Amount of Explicit Parallelism
Crypto
Boolean
Given natural operand size and level of parallelism, how parallel is computer or how must parallelism available in application?
Proposed Parallel Framework
More performance,
Better power efficiency
Easy for Programmer
Simpler Prog. model
More flexible

## Slide 24: Amount of Explicit Parallelism
Crypto
Boolean
Original 7 dwarves: 6 data parallel, 1 Sep. Addr.TLP
Bonus 4 dwarves: 2 data parallel, 2 Separate Addr. TLP
EEMBC (Embedded): DLP 19, 12 Separate Addr. TLP
SPEC (Desktop): 14 DLP, 2 Separate Address TLP
E E
M
B
C
S
P
E
C
D
W
A
R
F
S
E E
M
B
C
S
P
E
C
D
W
A
R
F
S

## Slide 25: What Computer Architecture brings to Table
Other fields often borrow ideas from architecture
Quantitative Principles of Design
  Take Advantage of Parallelism
  Principle of Locality
  Focus on the Common Case
  Amdahl’s Law
  The Processor Performance Equation
Careful, quantitative comparisons
  Define, quantity, and summarize relative performance
  Define and quantity relative cost
  Define and quantity dependability
  Define and quantity power
Culture of anticipating and exploiting advances in technology
Culture of well-defined interfaces that are carefully implemented and thoroughly checked

## Slide 26: 1) Taking Advantage of Parallelism
Increasing throughput of server computer via multiple processors or multiple disks
Detailed HW design
  Carry lookahead adders uses parallelism to speed up computing sums from linear to logarithmic in number of bits per operand
  Multiple memory banks searched in parallel in set-associative caches
Pipelining: overlap instruction execution to reduce the total time to complete an instruction sequence.
  Not every instruction depends on immediate predecessor  executing instructions completely/partially in parallel possible
  Classic 5-stage pipeline: 1) Instruction Fetch (Ifetch), 2) Register Read (Reg), 3) Execute (ALU), 4) Data Memory Access (Dmem), 5) Register Write (Reg)

## Slide 27: Three Generic Data Hazards
Read After Write (RAW) InstrJ tries to read operand before InstrI writes it
Caused by a “Dependence” (in compiler nomenclature). This hazard results from an actual need for communication.
I: add r1,r2,r3
J: sub r4,r1,r3

## Slide 28: Three Generic Data Hazards
Write After Read (WAR) InstrJ writes operand before InstrI reads it
Called an “anti-dependence” by compiler writers. This results from reuse of the name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Reads are always in stage 2, and
  Writes are always in stage 5
I: sub r4,r1,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 29: Three Generic Data Hazards
Write After Write (WAW) InstrJ writes operand before InstrI writes it.
Called an “output dependence” by compiler writers This also results from the reuse of name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Writes are always in stage 5
Will see WAR and WAW in more complicated pipes
I: sub r1,r4,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 30: Software Scheduling to Avoid Load Hazards
Try producing fast code for
a = b + c;
d = e – f;
assuming a, b, c, d ,e, and f in memory.
Slow code:
LW Rb,b
LW Rc,c
ADD Ra,Rb,Rc
SW a,Ra
LW Re,e
LW Rf,f
SUB Rd,Re,Rf
SW d,Rd
Fast code:
LW Rb,b
LW Rc,c
LW Re,e
ADD Ra,Rb,Rc
LW Rf,f
SW a,Ra
SUB Rd,Re,Rf
SW d,Rd
Compiler optimizes for performance. Hardware checks for safety.

## Slide 31: 2) The Principle of Locality
The Principle of Locality:
  Program access a relatively small portion of the address space at any instant of time.
Two Different Types of Locality:
  Temporal Locality (Locality in Time): If an item is referenced, it will tend to be referenced again soon (e.g., loops, reuse)
  Spatial Locality (Locality in Space): If an item is referenced, items whose addresses are close by tend to be referenced soon (e.g., straight-line code, array access)
Last 30 years, HW relied on locality for memory perf.
P
MEM
$
Notes: The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
This is kind of like in real life, we all have a lot of friends. But at any given time most of us can only keep in touch with a small group of them.
There are two different types of locality: Temporal and Spatial. Temporal locality is the locality in time which says if an item is referenced, it will tend to be referenced again soon.
This is like saying if you just talk to one of your friends, it is likely that you will talk to him or her again soon.
This makes sense. For example, if you just have lunch with a friend, you may say, let’s go to the ball game this Sunday. So you will talk to him again soon.
Spatial locality is the locality in space. It says if an item is referenced, items whose addresses are close by tend to be referenced soon.
Once again, using our analogy. We can usually divide our friends into groups. Like friends from high school, friends from work, friends from home.
Let’s say you just talk to one of your friends from high school and she may say something like: “So did you hear so and so just won the lottery.”
You probably will say NO, I better give him a call and find out more.
So this is an example of spatial locality. You just talked to a friend from your high school days. As a result, you end up talking to another high school friend. Or at least in this case, you hope he still remember you are his friend.
+3 = 10 min. (X:50)

## Slide 32: 3) Focus on the Common Case
Common sense guides computer design
  Since its engineering, common sense is valuable
In making a design trade-off, favor the frequent case over the infrequent case
  E.g., Instruction fetch and decode unit used more frequently than multiplier, so optimize it 1st
  E.g., If database server has 50 disks / processor, storage dependability dominates system dependability, so optimize it 1st
Frequent case is often simpler and can be done faster than the infrequent case
  E.g., overflow is rare when adding 2 numbers, so improve performance by optimizing more common case of no overflow
  May slow down overflow, but overall performance improved by optimizing for the normal case
What is frequent case and how much performance improved by making case faster => Amdahl’s Law

## Slide 33: 4) Amdahl’s Law
Best you could ever hope to do:

## Slide 34: 5) Processor performance equation
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle
Inst Count CPI Clock Rate
Program X
Compiler X (X)
Inst. Set. X X
Organization X X
Technology X
inst count
CPI
Cycle time

## Slide 35: Latency Lags Bandwidth (last ~20 years)
Performance Milestones
Processor: ‘286, ‘386, ‘486, Pentium, Pentium Pro, Pentium 4 (21x,2250x)
Ethernet: 10Mb, 100Mb, 1000Mb, 10000 Mb/s (16x,1000x)
Memory Module: 16bit plain DRAM, Page Mode DRAM, 32b, 64b, SDRAM, DDR SDRAM (4x,120x)
Disk : 3600, 5400, 7200, 10000, 15000 RPM (8x, 143x)
CPU high,
Memory low (“Memory Wall”)
Notes: <number>
<footer>
<header>
<date/time>
Processor: 2250X, 22X Latency

## Slide 36: Rule of Thumb for Latency Lagging BW
In the time that bandwidth doubles, latency improves by no more than a factor of 1.2 to 1.4
  (and capacity improves faster than bandwidth)
Stated alternatively: Bandwidth improves by more than the square of the improvement in Latency

## Slide 37: Define and quantity power ( 1 / 2)
For CMOS chips, traditional dominant energy consumption has been in switching transistors, called dynamic power
For mobile devices, energy better metric
For a fixed task, slowing clock rate (frequency switched) reduces power, but not energy
Capacitive load a function of number of transistors connected to output and technology, which determines capacitance of wires and transistors
Dropping voltage helps both, so went from 5V to 1V
To save energy & dynamic power, most CPUs now turn off clock of inactive modules (e.g. Fl. Pt. Unit)

## Slide 38: Define and quantity power (2 / 2)
Because leakage current flows even when a transistor is off, now static power important too
Leakage current increases in processors with smaller transistor sizes
Increasing the number of transistors increases power even if they are turned off
In 2006, goal for leakage is 25% of total power consumption; high performance designs at 40%
Very low power systems even gate voltage to inactive modules to control loss due to leakage

## Slide 39: Define and quantity cost ICs
For cost effective dies, cost  f(die_area2)
In 2006:  = 4, 12” (30 cm) wafer = $5k - $6k, Defect_Density = 0.4/cm2

## Slide 40: Define and quantity dependability
Module reliability = measure of continuous service accomplishment (or time to failure). 2 metrics
Mean Time To Failure (MTTF) measures Reliability
Failures In Time (FIT) = 1/MTTF, the rate of failures
  Traditionally reported as failures per billion hours of operation
Mean Time To Repair (MTTR) measures Service Interruption
  Mean Time Between Failures (MTBF) = MTTF+MTTR
Module availability measures service as alternate between the 2 states of accomplishment and interruption (number between 0 and 1, e.g. 0.9)
Module availability = MTTF / ( MTTF + MTTR)

## Slide 41: Example calculating reliability
If modules have exponentially distributed lifetimes (age of module does not affect probability of failure), overall failure rate is the sum of failure rates of the modules
Calculate FIT and MTTF for 10 disks (1M hour MTTF per disk), 1 disk controller (0.5M hour MTTF), and 1 power supply (0.2M hour MTTF):

## Slide 42: How Summarize Suite Performance
Since ratios, proper mean is geometric mean (SPECRatio unitless, so arithmetic mean meaningless)
Geometric mean of the ratios is the same as the ratio of the geometric means
Ratio of geometric means = Geometric mean of performance ratios  choice of reference computer is irrelevant!
These two points make geometric mean of ratios attractive to summarize performance

## Slide 43: How Summarize Suite Performance
Does a single mean well summarize performance of programs in benchmark suite?
Can decide if mean a good predictor by characterizing variability of distribution using standard deviation
Like geometric mean, geometric standard deviation is multiplicative rather than arithmetic
Can simply take the logarithm of SPECRatios, compute the standard mean and standard deviation, and then take the exponent to convert back:

## Slide 44: Summary #1/3: The Cache Design Space
Several interacting dimensions
  cache size
  block size
  associativity
  replacement policy
  write-through vs write-back
  write allocation
The optimal choice is a compromise
  depends on access characteristics
    workload
    use (I-cache, D-cache, TLB)
  depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 45: Summary #2/3: Caches
The Principle of Locality:
  Program access a relatively small portion of the address space at any instant of time.
    Temporal Locality: Locality in Time
    Spatial Locality: Locality in Space
Three Major Categories of Cache Misses:
  Compulsory Misses: sad facts of life. Example: cold start misses.
  Capacity Misses: increase cache size
  Conflict Misses: increase cache size and/or associativity. Nightmare Scenario: ping pong effect!
Write Policy: Write Through vs. Write Back
Today CPU time is a function of (ops, cache misses) vs. just f(ops): affects Compilers, Data structures, and Algorithms

## Slide 46: Summary #3/3: TLB, Virtual Memory
Page tables map virtual address to physical address
TLBs are important for fast translation
TLB misses are significant in processor performance
  funny times, as most systems can’t access all of 2nd level cache without TLB misses!
Caches, TLBs, Virtual Memory all understood by examining how they deal with 4 questions: 1) Where can block be placed? 2) How is block found? 3) What block is replaced on miss? 4) How are writes handled?
Today VM allows many processes to share single memory without having to swap all processes to disk; today VM protection is more important than memory hierarchy benefits, but computers insecure
Notes: Let’s do a short review of what you learned last time.
Virtual memory was originally invented as another level of memory hierarchy such that programers, faced with main memory much smaller than their programs, do not have to manage the loading and unloading portions of their program in and out of memory.
It was a controversial proposal at that time because very few programers believed software can manage the limited amount of memory resource as well as human.
This all changed as DRAM size grows exponentially in the last few decades.
Nowadays, the main function of virtual memory is to allow multiple processes to share the same main memory so we don’t have to swap all the non-active processes to disk.
Consequently, the most important function of virtual memory these days is to provide memory protection.
The most common technique, but we like to emphasis not the only technique, to translate virtual memory address to physical memory address is to use a page table.
TLB, or translation lookaside buffer, is one of the most popular hardware techniques to reduce address translation time.
Since TLB is so effective in reducing the address translation time, what this means is that TLB misses will have a significant negative impact on processor performance.
+3 = 3 min. (X:43)

## Slide 47: Instruction-Level Parallelism (ILP)
Basic Block (BB) ILP is quite small
  BB: a straight-line code sequence with no branches in except to the entry and no branches out except at the exit
  average dynamic branch frequency 15% to 25% => 4 to 7 instructions execute between a pair of branches
  Plus instructions in BB likely to depend on each other
To obtain substantial performance enhancements, we must exploit ILP across multiple basic blocks
Simplest: loop-level parallelism to exploit parallelism among iterations of a loop. E.g.,
for (i=1; i<=1000; i=i+1) x[i] = x[i] + y[i];

## Slide 48: Loop-Level Parallelism
Exploit loop-level parallelism to parallelism by “unrolling loop” either by
dynamic via branch prediction or
static via loop unrolling by compiler
(Another way is vectors, to be covered later)
Determining instruction dependence is critical to Loop Level Parallelism
If 2 instructions are
  parallel, they can execute simultaneously in a pipeline of arbitrary depth without causing any stalls (assuming no structural hazards)
  dependent, they are not parallel and must be executed in order, although they may often be partially overlapped

## Slide 49: Dynamic Branch Prediction
Performance = ƒ(accuracy, cost of misprediction)
Branch History Table: Lower bits of PC address index table of 1-bit values
  Says whether or not branch taken last time
  No address check
Problem: in a loop, 1-bit BHT will cause two mispredictions (avg is 9 iteratios before exit):
  End of loop case, when it exits instead of looping as before
  First time through loop on next time through code, when it predicts exit instead of looping

## Slide 50: Dynamic Branch Prediction
Solution: 2-bit scheme where change prediction only if get misprediction twice
Red: stop, not taken
Green: go, taken
Adds hysteresis to decision making process
T
T
NT
NT
Predict Taken
Predict Not
Taken
Predict Taken
Predict Not
Taken
T
NT
T
NT

## Slide 51: Why can Tomasulo overlap iterations of loops?
Register renaming
  Multiple iterations use different physical destinations for registers (dynamic loop unrolling).
Reservation stations
  Permit instruction issue to advance past integer control flow operations
  Also buffer old values of registers - totally avoiding the WAR stall
Other perspective: Tomasulo building data flow dependency graph on the fly

## Slide 52: Tomasulo’s scheme offers 2 major advantages
Distribution of the hazard detection logic
  distributed reservation stations and the CDB
  If multiple instructions waiting on single result, & each instruction has other operand, then instructions can be released simultaneously by broadcast on CDB
  If a centralized register file were used, the units would have to read their results from the registers when register buses are available
Elimination of stalls for WAW and WAR hazards

## Slide 53: Tomasulo Drawbacks
Complexity
  delays of 360/91, MIPS 10000, Alpha 21264, IBM PPC 620 in CA:AQA 2/e, but not in silicon!
Many associative stores (CDB) at high speed
Performance limited by Common Data Bus
  Each CDB must go to multiple functional units high capacitance, high wiring density
  Number of functional units that can complete per cycle limited to one!
    Multiple CDBs  more FU logic for parallel assoc stores
Non-precise interrupts!
  We will address this later

## Slide 54: Tomasulo
Reservations stations: renaming to larger set of registers + buffering source operands
  Prevents registers as bottleneck
  Avoids WAR, WAW hazards
  Allows loop unrolling in HW
Not limited to basic blocks (integer units gets ahead, beyond branches)
Helps cache misses as well
Lasting Contributions
  Dynamic scheduling
  Register renaming
  Load/store disambiguation
360/91 descendants are Intel Pentium 4, IBM Power 5, AMD Athlon/Opteron, …

## Slide 55: ILP
Leverage Implicit Parallelism for Performance: Instruction Level Parallelism
Loop unrolling by compiler to increase ILP
Branch prediction to increase ILP
Dynamic HW exploiting ILP
  Works when can’t know dependence at compile time
  Can hide L1 cache misses
  Code for one machine runs well on another

## Slide 56: Limits to ILP
Most techniques for increasing performance increase power consumption
The key question is whether a technique is energy efficient: does it increase power consumption faster than it increases performance?
Multiple issue processors techniques all are energy inefficient:
  Issuing multiple instructions incurs some overhead in logic that grows faster than the issue rate grows
  Growing gap between peak issue rates and sustained performance
Number of transistors switching = f(peak issue rate), and performance = f( sustained rate), growing gap between peak and sustained performance  increasing energy per unit of performance

## Slide 57: Limits to ILP
Doubling issue rates above today’s 3-6 instructions per clock, say to 6 to 12 instructions, probably requires a processor to
  Issue 3 or 4 data memory accesses per cycle,
  Resolve 2 or 3 branches per cycle,
  Rename and access more than 20 registers per cycle, and
  Fetch 12 to 24 instructions per cycle.
Complexities of implementing these capabilities likely means sacrifices in maximum clock rate
  E.g, widest issue processor is the Itanium 2, but it also has the slowest clock rate, despite the fact that it consumes the most power!

## Slide 58: Limits to ILP
Initial HW Model here; MIPS compilers.
Assumptions for ideal/perfect machine to start:
1. Register renaming – infinite virtual registers => all register WAW & WAR hazards are avoided
2. Branch prediction – perfect; no mispredictions
3. Jump prediction – all jumps perfectly predicted (returns, case statements) 2 & 3  no control dependencies; perfect speculation & an unbounded buffer of instructions available
4. Memory-address alias analysis – addresses known & a load can be moved before a store provided addresses not equal; 1&4 eliminates all but RAW
Also: perfect caches; 1 cycle latency for all instructions (FP *,/); unlimited instructions issued/clock cycle;

## Slide 59
 | New Model | Model | Power 5
Instructions Issued per clock | 64 | Infinite | 4
Instruction Window Size | 2048 | Infinite | 200
Renaming Registers | 256 Int + 256 FP | Infinite | 48 integer + 40 Fl. Pt.
Branch Prediction | 8K 2-bit | Perfect | Tournament
Cache | Perfect | Perfect | 64KI, 32KD, 1.92MB L2, 36 MB L3
Memory Alias | Perfect v. Stack v. Inspect v. none | Perfect | Perfect
Limits to ILP HW Model comparison

## Slide 60: More Realistic HW: Memory Address Alias Impact Figure 3.6
Change 2048 instr window, 64 instr issue, 8K 2 level Prediction, 256 renaming registers
None
Global/Stack perf; heap conflicts
Perfect
Inspec. Assem.
FP: 4 - 45
(Fortran,
no heap)
Integer: 4 - 9
IPC

## Slide 61: Realistic HW: Window Impact (Figure 3.7)
Perfect disambiguation (HW), 1K Selective Prediction, 16 entry return, 64 registers, issue as many as window
64
16
256
Infinite
32
128
8
4
Integer: 6 - 12
FP: 8 - 45
IPC

## Slide 62: Vector Instruction Set Advantages
Compact
  one short instruction encodes N operations
Expressive, tells hardware that these N operations:
  are independent
  use the same functional unit
  access disjoint registers
  access registers in the same pattern as previous instructions
  access a contiguous block of memory (unit-stride load/store)
  access memory in a known pattern (strided load/store)
Scalable
  can run same object code on more parallel pipelines or lanes

## Slide 63: Vector Execution Time
Time = f(vector length, data dependicies, struct. hazards)
Initiation rate: rate that FU consumes vector elements (= number of lanes; usually 1 or 2 on Cray T-90)
Convoy: set of vector instructions that can begin execution in same clock (no struct. or data hazards)
Chime: approx. time for a vector operation
m convoys take m chimes; if each vector length is n, then they take approx. m x n clock cycles (ignores overhead; good approximization for long vectors)
4 convoys, 1 lane, VL=64
=> 4 x 64 = 256 clocks
(or 4 clocks per result)
1: LV V1,Rx ;load vector X
2: MULV V2,F0,V1 ;vector-scalar mult.
LV V3,Ry ;load vector Y
3: ADDV V4,V2,V3 ;add
4: SV Ry,V4 ;store the result

## Slide 64: MP and caches
Caches contain all information on state of cached memory blocks
Snooping cache over shared medium for smaller MP by invalidating other cached copies on write
Sharing cached data  Coherence (values returned by a read), Consistency (when a written value will be returned by a read)
Snooping and Directory Protocols similar; bus makes snooping easier because of broadcast (snooping => uniform memory access)
Directory has extra data structure to keep track of state of all cache blocks
Distributing directory => scalable shared address multiprocessor => Cache coherent, Non uniform memory access

## Slide 65: Microprocessor Comparison
Processor | SUN T1 | Opteron | Pentium D | IBM Power 5
Cores | 8 | 2 | 2 | 2
Instruction issues / clock / core | 1 | 3 | 3 | 4
Peak instr. issues / chip | 8 | 6 | 6 | 8
Multithreading | Fine-grained | No | SMT | SMT
L1 I/D in KB per core | 16/8 | 64/64 | 12K uops/16 | 64/32
L2 per core/shared | 3 MB shared | 1MB / core | 1MB/ core | 1.9 MB shared
Clock rate (GHz) | 1.2 | 2.4 | 3.2 | 1.9
Transistor count (M) | 300 | 233 | 230 | 276
Die size (mm2) | 379 | 199 | 206 | 389
Power (W) | 79 | 110 | 130 | 125

## Slide 66: Performance Relative to Pentium D

## Slide 67: Performance/mm2, Performance/Watt