## Slide 1: EECS 252 Graduate Computer Architecture Lec 18 – Storage
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://vlsi.cs.berkeley.edu/cs252-s06

## Slide 2: Review
Virtual Machine Revival
  Overcome security flaws of modern OSes
  Processor performance no longer highest priority
  Manage Software, Manage Hardware
“… VMMs give OS developers another opportunity to develop functionality no longer practical in today’s complex and ossified operating systems, where innovation moves at geologic pace .”
[Rosenblum and Garfinkel, 2005]
Virtualization challenges for processor, virtual memory, I/O
  Paravirtualization, ISA upgrades to cope with those difficulties
Xen as example VMM using paravirtualization
  2005 performance on non-I/O bound, I/O intensive apps: 80% of native Linux without driver VM, 34% with driver VM
Opteron memory hierarchy still critical to performance

## Slide 3: Case for Storage
Shift in focus from computation to communication and storage of information
  E.g., Cray Research/Thinking Machines vs. Google/Yahoo
  “The Computing Revolution” (1960s to 1980s)  “The Information Age” (1990 to today)
Storage emphasizes reliability and scalability as well as cost-performance
What is “Software king” that determines which HW acually features used?
  Operating System for storage
  Compiler for processor
Also has own performance theory—queuing theory—balances throughput vs. response time

## Slide 4: Outline
Magnetic Disks
RAID
Administrivia
Advanced Dependability/Reliability/Availability
I/O Benchmarks, Performance and Dependability
Intro to Queueing Theory (if we have time)
Conclusion

## Slide 5: Disk Figure of Merit: Areal Density
Bits recorded along a track
  Metric is Bits Per Inch (BPI)
Number of tracks per surface
  Metric is Tracks Per Inch (TPI)
Disk Designs Brag about bit density per unit area
  Metric is Bits Per Square Inch: Areal Density = BPI x TPI

## Slide 6: Historical Perspective
1956 IBM Ramac — early 1970s Winchester
  Developed for mainframe computers, proprietary interfaces
  Steady shrink in form factor: 27 in. to 14 in.
Form factor and capacity drives market more than performance
1970s developments
  5.25 inch floppy disk formfactor (microcode into mainframe)
  Emergence of industry standard disk interfaces
Early 1980s: PCs and first generation workstations
Mid 1980s: Client/server computing
  Centralized storage on file server
    accelerates disk downsizing: 8 inch to 5.25
  Mass market disk drives become a reality
    industry standards: SCSI, IPI, IDE
    5.25 inch to 3.5 inch drives for PCs, End of proprietary interfaces
1900s: Laptops => 2.5 inch drives
2000s: What new devices leading to new drives?

## Slide 7: Future Disk Size and Performance
Continued advance in capacity (60%/yr) and bandwidth (40%/yr)
Slow improvement in seek, rotation (8%/yr)
Time to read whole disk
Year Sequentially Randomly (1 sector/seek)
1990 4 minutes 6 hours
2000 12 minutes 1 week(!)
2006 56 minutes 3 weeks (SCSI)
2006 171 minutes 7 weeks (SATA)
Notes: Capacity: 80 GB * 2^5 = 2.5 TB
BW 30 MB/s * 1.4^5 = 160 MB/s
seek 6 / 1.1^5 = 4 ms
RPM 10000 => 20000? (3 to 1.5)
to read sequentially = 260 minutes or 4.4 hours!
To read randomly = 316 days or 1 year

## Slide 8: Use Arrays of Small Disks?
14”
10”
5.25”
3.5”
3.5”
Disk Array: 1 disk design
Conventional: 4 disk designs
Low End
High End
Katz and Patterson asked in 1987:
  Can smaller disks be used to close gap in performance between disks and CPUs?

## Slide 9: Advantages of Small Formfactor Disk Drives
Low cost/MB
High MB/volume
High MB/watt
Low cost/Actuator
Cost and Environmental Efficiencies

## Slide 10: Replace Small Number of Large Disks with Large Number of Small Disks! (1988 Disks)
Capacity
Volume
Power
Data Rate
I/O Rate
MTTF
Cost
IBM 3390K
20 GBytes
97 cu. ft.
3 KW
15 MB/s
600 I/Os/s
250 KHrs
$250K
IBM 3.5" 0061
320 MBytes
0.1 cu. ft.
11 W
1.5 MB/s
55 I/Os/s
50 KHrs
$2K
x70
23 GBytes
11 cu. ft.
1 KW
120 MB/s
3900 IOs/s
??? Hrs
$150K
Disk Arrays have potential for large data and I/O rates, high MB per cu. ft., high MB per KW, but what about reliability?
9X
3X
8X
6X

## Slide 11: Array Reliability
Reliability of N disks = Reliability of 1 Disk ÷ N
  50,000 Hours ÷ 70 disks = 700 hours
Disk system MTTF: Drops from 6 years to 1 month!
• Arrays (without redundancy) too unreliable to be useful!
Hot spares support reconstruction in parallel with
access: very high media availability can be achieved

## Slide 12: Redundant Arrays of (Inexpensive) Disks
Files are "striped" across multiple disks
Redundancy yields high data availability
  Availability: service still provided to user, even if some components failed
Disks will still fail
Contents reconstructed from data redundantly stored in the array
   Capacity penalty to store redundant info
   Bandwidth penalty to update redundant info

## Slide 13: Redundant Arrays of Inexpensive Disks RAID 1: Disk Mirroring/Shadowing
• Each disk is fully duplicated onto its “mirror”
Very high availability can be achieved
• Bandwidth sacrifice on write:
Logical write = two physical writes
  • Reads may be optimized
• Most expensive solution: 100% capacity overhead
(RAID 2 not interesting, so skip)
recovery
group

## Slide 14: Redundant Array of Inexpensive Disks RAID 3: Parity Disk
P
10010011
11001101
10010011
. . .
logical record
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
P contains sum of
other disks per stripe mod 2 (“parity”)
If disk fails, subtract
P from sum of other disks to find missing information
Striped physical
records

## Slide 15: RAID 3
Sum computed across recovery group to protect against hard disk failures, stored in P disk
Logically, a single high capacity, high transfer rate disk: good for large transfers
Wider arrays reduce capacity costs, but decreases availability
33% capacity cost for parity if 3 data disks and 1 parity disk

## Slide 16: Inspiration for RAID 4
RAID 3 relies on parity disk to discover errors on Read
But every sector has an error detection field
To catch errors on read, rely on error detection field vs. the parity disk
Allows independent reads to different disks simultaneously

## Slide 17: Redundant Arrays of Inexpensive Disks RAID 4: High I/O Rate Parity
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Address
Stripe
Insides of 5 disks
Example:
small read D0 & D5, large write D12-D15

## Slide 18: Inspiration for RAID 5
RAID 4 works well for small reads
Small writes (write to one disk):
  Option 1: read other data disks, create new sum and write to Parity Disk
  Option 2: since P has old sum, compare old data to new data, add the difference to P
Small writes are limited by Parity Disk: Write to D0, D5 both also write to P disk
D0
D1
D2
D3
P
D4
D5
D6
P
D7

## Slide 19: Redundant Arrays of Inexpensive Disks RAID 5: High I/O Rate Interleaved Parity
Independent writes
possible because of
interleaved parity
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Addresses
Example: write to D0, D5 uses disks 0, 1, 3, 4

## Slide 20: Problems of Disk Arrays: Small Writes
D0
D1
D2
D3
P
D0'
+
+
D0'
D1
D2
D3
P'
new
data
old
data
old
parity
XOR
XOR
(1. Read)
(2. Read)
(3. Write)
(4. Write)
RAID-5: Small Write Algorithm
1 Logical Write = 2 Physical Reads + 2 Physical Writes

## Slide 21: CS252: Administrivia
Wed 4/12 – Mon 4/17 Storage (Ch 6)
RAMP Blue meeting Today 3:30-4 380 Soda
Makeup Pizza: LaVal’s on Euclid, 6-7 PM
Project Update Meeting Wednesday 4/19
Monday 4/24 Quiz 2 5-8 PM (Mainly Ch 4 to 6)
Wed 4/26 Bad Career Advice / Bad Talk Advice
Project Presentations Monday 5/1 (all day)
Project Posters 5/3 Wednesday (11-1 in Soda)
Final Papers due Friday 5/5 (email Archana, who will post papers on class web site)
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 22: CS252: Administrivia
Fri 4/14 Read, comment RAID Paper and Homework. Be sure to answer
  What was main motivation for RAID in paper?
  Did prediction of processor performance and disk capacity hold?
  How propose balance performance and capacity of RAID 1 to RAID 5? What do you think of it?
  What were some of the open issues? Which were significant
  In retrospect, what do you think were important contributions? What did the authors get wrong?
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 23: RAID 6: Recovering from 2 failures
Why > 1 failure recovery?
  operator accidentally replaces the wrong disk during a failure
  since disk bandwidth is growing more slowly than disk capacity, the MTT Repair a disk in a RAID system is increasing increases the chances of a 2nd failure during repair since takes longer
  reading much more data during reconstruction meant increasing the chance of an uncorrectable media failure, which would result in data loss

## Slide 24: RAID 6: Recovering from 2 failures
Network Appliance’s row-diagonal parity or RAID-DP
Like the standard RAID schemes, it uses redundant space based on parity calculation per stripe
Since it is protecting against a double failure, it adds two check blocks per stripe of data.
  If p+1 disks total, p-1 disks have data; assume p=5
Row parity disk is just like in RAID 4
  Even parity across the other 4 data blocks in its stripe
Each block of the diagonal parity disk contains the even parity of the blocks in the same diagonal

## Slide 25: Example p = 5
Row diagonal parity starts by recovering one of the 4 blocks on the failed disk using diagonal parity
  Since each diagonal misses one disk, and all diagonals miss a different disk, 2 diagonals are only missing 1 block
Once the data for those blocks is recovered, then the standard RAID recovery scheme can be used to recover two more blocks in the standard RAID 4 stripes
Process continues until two failed disks are restored
Data Disk 0 | Data Disk 1 | Data Disk 2 | Data Disk 3 | Row Parity | Diagonal Parity
0 | 1 | 2 | 3 | 4 | 0
1 | 2 | 3 | 4 | 0 | 1
2 | 3 | 4 | 0 | 1 | 2
3 | 4 | 0 | 1 | 2 | 3
4 | 0 | 1 | 2 | 3 | 4
0 | 1 | 2 | 3 | 4 | 0

## Slide 26: Berkeley History: RAID-I
RAID-I (1989)
  Consisted of a Sun 4/280 workstation with 128 MB of DRAM, four dual-string SCSI controllers, 28 5.25-inch SCSI disks and specialized disk striping software
Today RAID is $24 billion dollar industry, 80% nonPC disks sold in RAIDs

## Slide 27: Summary: RAID Techniques: Goal was performance, popularity due to reliability of storage
• Disk Mirroring, Shadowing (RAID 1)
Each disk is fully duplicated onto its "shadow"
Logical write = two physical writes
100% capacity overhead
• Parity Data Bandwidth Array (RAID 3)
Parity computed horizontally
Logically a single high data bw disk
• High I/O Rate Parity Array (RAID 5)
Interleaved parity blocks
Independent reads and writes
Logical write = 2 reads + 2 writes
1
0
0
1
0
0
1
1
1
1
0
0
1
1
0
1
1
0
0
1
0
0
1
1
0
0
1
1
0
0
1
0
1
0
0
1
0
0
1
1
1
0
0
1
0
0
1
1

## Slide 28: Definitions
Examples on why precise definitions so important for reliability
Is a programming mistake a fault, error, or failure?
  Are we talking about the time it was designed or the time the program is run?
  If the running program doesn’t exercise the mistake, is it still a fault/error/failure?
If an alpha particle hits a DRAM memory cell, is it a fault/error/failure if it doesn’t change the value?
  Is it a fault/error/failure if the memory doesn’t access the changed bit?
  Did a fault/error/failure still occur if the memory had error correction and delivered the corrected value to the CPU?

## Slide 29: IFIP Standard terminology
Computer system dependability: quality of delivered service such that reliance can be placed on service
Service is observed actual behavior as perceived by other system(s) interacting with this system’s users
Each module has ideal specified behavior, where service specification is agreed description of expected behavior
A system failure occurs when the actual behavior deviates from the specified behavior
failure occurred because an error, a defect in module
The cause of an error is a fault
When a fault occurs it creates a latent error, which becomes effective when it is activated
When error actually affects the delivered service, a failure occurs (time from error to failure is error latency)

## Slide 30: Fault v. (Latent) Error v. Failure
An error is manifestation in the system of a fault, a failure is manifestation on the service of an error
Is If an alpha particle hits a DRAM memory cell, is it a fault/error/failure if it doesn’t change the value?
  Is it a fault/error/failure if the memory doesn’t access the changed bit?
  Did a fault/error/failure still occur if the memory had error correction and delivered the corrected value to the CPU?
An alpha particle hitting a DRAM can be a fault
if it changes the memory, it creates an error
error remains latent until effected memory word is read
if the effected word error affects the delivered service, a failure occurs

## Slide 31: Fault Categories
Hardware faults: Devices that fail, such alpha particle hitting a memory cell
Design faults: Faults in software (usually) and hardware design (occasionally)
Operation faults: Mistakes by operations and maintenance personnel
Environmental faults: Fire, flood, earthquake, power failure, and sabotage
Also by duration:
Transient faults exist for limited time and not recurring
Intermittent faults cause a system to oscillate between faulty and fault-free operation
Permanent faults do not correct themselves over time

## Slide 32: Fault Tolerance vs Disaster Tolerance
Fault-Tolerance (or more properly, Error-Tolerance): mask local faults (prevent errors from becoming failures)
  RAID disks
  Uninterruptible Power Supplies
  Cluster Failover
Disaster Tolerance: masks site errors (prevent site errors from causing service failures)
  Protects against fire, flood, sabotage,..
  Redundant system and service at remote site.
  Use design diversity
From Jim Gray’s “Talk at UC Berkeley on Fault Tolerance " 11/9/00
Notes: <number>
<footer>
<header>
<date/time>
There have been a variety of technologies introduced to address your growing need for high-availability servers.
The simplest of these is Data Mirroring, which continuously duplicates all disk writes onto a mirrored set of disks, possibly at a remote disaster recovery site. Today you can get Data Mirroring products for Windows NT Server from a few vendors, including Octopus (http://www.octopus.com) and Vinca (http://www.vinca.com). These solutions provide excellent protection for your data, even in the event of a metropolis-wide disaster. However, they’re not high-availability solutions that have the ability to detect all types of hardware or software failure, and they have at best limited abilities to automatically restart applications. (For example, users must manually reconnect to the new server, plus any applications running on the recovery server are canceled as if it had been the server that failed.)
Server Mirroring like Novell SFT III (Server Fault Tolerance) is a high-availability capability that both protects your data and provides for automatic detection of failures plus restart of selected applications. Server Mirroring provides excellent reliability, but at a very high cost since it requires an idle “standby” server that does no productive work except when the primary server fails. There are also very few applications which can take advantage of proprietary server mirroring solutions like Novell SFT III.
At the high end are true “fault tolerant” systems like the excellent “NonStop” systems from Tandem. These systems are able to detect and almost instantly recover from virtually any single hardware or software failure. Most bank transactions, for example, run on this type of system. This level of reliability comes with a very high price tag, however, and each solution is based on a proprietary, single-vendor set of hardware.
And, finally, there’s another high-availability technology which seems to offer the best of all these capabilities: clustering...

## Slide 33: Case Studies - Tandem Trends Reported MTTF by Component
1985 1987 1990
SOFTWARE 2 53 33 Years
HARDWARE 29 91 310 Years
MAINTENANCE 45 162 409 Years
OPERATIONS 99 171 136 Years
ENVIRONMENT 142 214 346 Years
SYSTEM 8 20 21 Years
Problem: Systematic Under-reporting
From Jim Gray’s “Talk at UC Berkeley on Fault Tolerance " 11/9/00

## Slide 34: Is Maintenance the Key?
VAX crashes ‘85, ‘93 [Murp95]; extrap. to ‘01
Sys. Man.: N crashes/problem, SysAdmin action
  Actions: set params bad, bad config, bad app install
HW/OS 70% in ‘85 to 28% in ‘93. In ‘01, 10%?
Rule of Thumb: Maintenance 10X HW
  so over 5 year product life, ~ 95% of cost is maintenance
Notes: <number>
<footer>
<header>
<date/time>
[Murp95] Murphy, B.; Gent, T. Measuring system and software reliability using an automated data collection process. Quality and Reliability Engineering International, vol.11, (no.5), Sept.-Oct. 1995. p.341-53.

## Slide 35: HW Failures in Real Systems: Tertiary Disks
A cluster of 20 PCs in seven 7-foot high, 19-inch wide racks with 368 8.4 GB, 7200 RPM, 3.5-inch IBM disks. The PCs are P6-200MHz with 96 MB of DRAM each. They run FreeBSD 3.0 and the hosts are connected via switched 100 Mbit/second Ethernet

## Slide 36: Does Hardware Fail Fast? 4 of 384 Disks that failed in Tertiary Disk

## Slide 37: High Availability System Classes Goal: Build Class 6 Systems
Availability
90.%
99.%
99.9%
99.99%
99.999%
99.9999%
99.99999%
System Type
Unmanaged
Managed
Well Managed
Fault Tolerant
High-Availability
Very-High-Availability
Ultra-Availability
Unavailable
(min/year)
50,000
5,000
500
50
5
.5
.05
Availability
Class
1
2
3
4
5
6
7
UnAvailability = MTTR/MTBF
can cut it in ½ by cutting MTTR or MTBF
From Jim Gray’s “Talk at UC Berkeley on Fault Tolerance " 11/9/00

## Slide 38: How Realistic is "5 Nines"?
HP claims HP-9000 server HW and HP-UX OS can deliver 99.999% availability guarantee “in certain pre-defined, pre-tested customer environments”
  Application faults?
  Operator faults?
  Environmental faults?
Collocation sites (lots of computers in 1 building on Internet) have
  1 network outage per year (~1 day)
  1 power failure per year (~1 day)
Microsoft Network unavailable recently for a day due to problem in Domain Name Server: if only outage per year, 99.7% or 2 Nines

## Slide 39: Outline
Magnetic Disks
RAID
Administrivia
Advanced Dependability/Reliability/Availability
I/O Benchmarks, Performance and Dependability
Intro to Queueing Theory (if we have time)
Conclusion

## Slide 40: I/O Performance
Response time = Queue + Device Service time
100%
Response
Time (ms)
Throughput
(% total BW)
0
100
200
300
0%
Proc
Queue
IOC
Device
Metrics:
Response Time
vs. Throughput

## Slide 41: I/O Benchmarks
For better or worse, benchmarks shape a field
  Processor benchmarks classically aimed at response time for fixed sized problem
  I/O benchmarks typically measure throughput, possibly with upper limit on response times (or 90% of response times)
Transaction Processing (TP) (or On-line TP=OLTP)
  If bank computer fails when customer withdraw money, TP system guarantees account debited if customer gets $ & account unchanged if no $
  Airline reservation systems & banks use TP
Atomic transactions makes this work
Classic metric is Transactions Per Second (TPS)

## Slide 42: I/O Benchmarks: Transaction Processing
Early 1980s great interest in OLTP
  Expecting demand for high TPS (e.g., ATM machines, credit cards)
  Tandem’s success implied medium range OLTP expands
  Each vendor picked own conditions for TPS claims, report only CPU times with widely different I/O
  Conflicting claims led to disbelief of all benchmarks  chaos
1984 Jim Gray (Tandem) distributed paper to Tandem + 19 in other companies propose standard benchmark
Published “A measure of transaction processing power,” Datamation, 1985 by Anonymous et. al
  To indicate that this was effort of large group
  To avoid delays of legal department of each author’s firm
  Still get mail at Tandem to author “Anonymous”
Led to Transaction Processing Council in 1988
  www.tpc.org

## Slide 43: I/O Benchmarks: TP1 by Anon et. al
DebitCredit Scalability: size of account, branch, teller, history function of throughput
  TPS Number of ATMs Account-file size
  10 1,000 0.1 GB
  100 10,000 1.0 GB
  1,000 100,000 10.0 GB
  10,000 1,000,000 100.0 GB
  Each input TPS =>100,000 account records, 10 branches, 100 ATMs
  Accounts must grow since a person is not likely to use the bank more frequently just because the bank has a faster computer!
Response time: 95% transactions take ≤ 1 second
Report price (initial purchase price + 5 year maintenance = cost of ownership)
Hire auditor to certify results

## Slide 44: Unusual Characteristics of TPC
Price is included in the benchmarks
  cost of HW, SW, and 5-year maintenance agreements included  price-performance as well as performance
The data set generally must scale in size as the throughput increases
  trying to model real systems, demand on system and size of the data stored in it increase together
The benchmark results are audited
  Must be approved by certified TPC auditor, who enforces TPC rules  only fair results are submitted
Throughput is the performance metric but response times are limited
  eg, TPC-C: 90% transaction response times < 5 seconds
An independent organization maintains the benchmarks
  COO ballots on changes, meetings, to settle disputes...

## Slide 45: TPC Benchmark History/Status

## Slide 46: I/O Benchmarks via SPEC
SFS 3.0 Attempt by NFS companies to agree on standard benchmark
  Run on multiple clients & networks (to prevent bottlenecks)
  Same caching policy in all clients
  Reads: 85% full block & 15% partial blocks
  Writes: 50% full block & 50% partial blocks
  Average response time: 40 ms
  Scaling: for every 100 NFS ops/sec, increase capacity 1GB
Results: plot of server load (throughput) vs. response time & number of users
  Assumes: 1 user => 10 NFS ops/sec
  3.0 for NSF 3.0
Added SPECMail (mailserver), SPECWeb (webserver) benchmarks

## Slide 47: 2005 Example SPEC SFS Result: NetApp FAS3050c NFS servers
2.8 GHz Pentium Xeon microprocessors, 2 GB of DRAM per processor, 1GB of Non-volatile memory per system
4 FDDI networks; 32 NFS Daemons, 24 GB file size
168 fibre channel disks: 72 GB, 15000 RPM, 2 or 4 FC controllers

## Slide 48: Availability benchmark methodology
Goal: quantify variation in QoS metrics as events occur that affect system availability
Leverage existing performance benchmarks
  to generate fair workloads
  to measure & trace quality of service metrics
Use fault injection to compromise system
  hardware faults (disk, memory, network, power)
  software faults (corrupt input, driver error returns)
  maintenance events (repairs, SW/HW upgrades)
Examine single-fault and multi-fault workloads
  the availability analogues of performance micro- and macro-benchmarks

## Slide 49: Example single-fault result
Compares Linux and Solaris reconstruction
  Linux: minimal performance impact but longer window of vulnerability to second fault
  Solaris: large perf. impact but restores redundancy fast
Linux
Solaris

## Slide 50: Reconstruction policy (2)
Linux: favors performance over data availability
  automatically-initiated reconstruction, idle bandwidth
  virtually no performance impact on application
  very long window of vulnerability (>1hr for 3GB RAID)
Solaris: favors data availability over app. perf.
  automatically-initiated reconstruction at high BW
  as much as 34% drop in application performance
  short window of vulnerability (10 minutes for 3GB)
Windows: favors neither!
  manually-initiated reconstruction at moderate BW
  as much as 18% app. performance drop
  somewhat short window of vulnerability (23 min/3GB)

## Slide 51: Introduction to Queueing Theory
More interested in long term, steady state than in startup => Arrivals = Departures
Little’s Law: Mean number tasks in system = arrival rate x mean reponse time
  Observed by many, Little was first to prove
Applies to any system in equilibrium, as long as black box not creating or destroying tasks
Arrivals
Departures
Notes: Old and New Testament by Kleirock
Regret skipping as grad student

## Slide 52: Deriving Little’s Law
Timeobserve = elapsed time that observe a system
Numbertask = number of task during Timeobserve
Timeaccumulated = sum of elapsed times for each task
Then
Mean number tasks in system = Timeaccumulated / Timeobserve
Mean response time = Timeaccumulated / Numbertask
Arrival Rate = Numbertask / Timeobserve
Factoring RHS of 1st equation
Timeaccumulated / Timeobserve = Timeaccumulated / Numbertask x
Numbertask / Timeobserve
Then get Little’s Law:
Mean number tasks in system = Arrival Rate x Mean response time

## Slide 53: A Little Queuing Theory: Notation
Notation: Timeserver average time to service a task Average service rate = 1 / Timeserver (traditionally µ) Timequeue average time/task in queue Timesystem average time/task in system = Timequeue + Timeserver Arrival rate avg no. of arriving tasks/sec (traditionally λ)
Lengthserver average number of tasks in service Lengthqueue average length of queue Lengthsystem average number of tasks in service = Lengthqueue + Lengthserver Little’s Law: Lengthserver = Arrival rate x Timeserver (Mean number tasks = arrival rate x mean service time)
Proc
IOC
Device
Queue
server
System
Notes: Sometimes Queue called waiting line, System called Queue

## Slide 54: Server Utilization
For a single server, service rate = 1 / Timeserver
Server utilization must be between 0 and 1, since system is in equilibrium (arrivals = departures); often called traffic intensity, traditionally ρ)
Server utilization = mean number tasks in service = Arrival rate x Timeserver
What is disk utilization if get 50 I/O requests per second for disk and average disk service time is 10 ms (0.01 sec)?
Server utilization = 50/sec x 0.01 sec = 0.5
Or server is busy on average 50% of time

## Slide 55: Time in Queue vs. Length of Queue
We assume First In First Out (FIFO) queue
Relationship of time in queue (Timequeue) to mean number of tasks in queue (Lengthqueue) ?
Timequeue = Lengthqueue x Timeserver + “Mean time to complete service of task when new task arrives if server is busy”
New task can arrive at any instant; how predict last part?
To predict performance, need to know sometime about distribution of events

## Slide 56: Poisson Distribution of Random Variables
A variable is random if it takes one of a specified set of values with a specified probability
  you cannot know exactly what its next value will be, but you may know the probability of all possible values
I/O Requests can be modeled by a random variable because OS normally switching between several processes generating independent I/O requests
  Also given probabilistic nature of disks in seek and rotational delays
Can characterize distribution of values of a random variable with discrete values using a histogram
  Divides range between the min & max values into buckets
  Histograms then plot the number in each bucket as columns
  Works for discrete values e.g., number of I/O requests?
What about if not discrete? Very fine buckets

## Slide 57: Characterizing distribution of a random variable
Need mean time and a measure of variance
For mean, use weighted arithmetic mean(WAM):
fi = frequency of task i
Ti = time for tasks I
weighted arithmetic mean = f1T1 + f2T2 + . . . +fnTn
For variance, instead of standard deviation, use Variance (square of standard deviation) for WAM:
Variance = (f1T12 + f2T22 + . . . +fnTn2) – WAM2
  If time is miliseconds, Variance units are square milliseconds!
Got a unitless measure of variance?

## Slide 58: Squared Coefficient of Variance (C2)
C2 = Variance / WAM2
  Unitless measure
C = sqrt(Variance)/WAM = StDev/WAM
Trying to characterize random events, but to predict performance need distribution of random events where math is tractable
Most popular such distribution is exponential distribution, where C = 1
Note using constant to characterize variability about the mean
  Invariance of C over time  history of events has no impact on probability of an event occurring now
  Called memoryless, an important assumption to predict behavior
  (Suppose not; then have to worry about the exact arrival times of requests relative to each other  make math considerably less tractable!)
Most widely used exponential distribution is Poisson

## Slide 59: Poisson Distribution
Most widely used exponential distribution is Poisson
Described by probability mass function:
Probability (k) = e-a x ak / k!
  where a = Rate of events x Elapsed time
If interarrival times are exponentially distributed and use arrival rate from above for rate of events, number of arrivals in time interval t is a Poisson process
Time in Queue vs. Length of Queue?
½ x Arimetic mean x (1 +C2)

## Slide 60: Summary
Disks: Arial Density now 30%/yr vs. 100%/yr in 2000s
TPC: price performance as normalizing configuration feature
  Auditing to ensure no foul play
  Throughput with restricted response time is normal measure
Fault  Latent errors in system  Failure in service
Components often fail slowly
Real systems: problems in maintenance, operation as well as hardware, software
Queuing models assume state of equilibrium: input rate = output rate
Little’s Law: Lengthsystem = rate x Timesystem (Mean number customers = arrival rate x mean service time)
Proc
IOC
Device
Queue
server
System