## Slide 1: EECS 252 Graduate Computer Architecture Lec 18 – Storage
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~pattrsn
http://vlsi.cs.berkeley.edu/cs252-s06

## Slide 2: Review
Disks: Arial Density now 30%/yr vs. 100%/yr in 2000s
TPC: price performance as normalizing configuration feature
  Auditing to ensure no foul play
  Throughput with restricted response time is normal measure
Fault  Latent errors in system  Failure in service
Components often fail slowly
Real systems: problems in maintenance, operation as well as hardware, software

## Slide 3: Introduction to Queueing Theory
More interested in long term, steady state than in startup => Arrivals = Departures
Little’s Law: Mean number tasks in system = arrival rate x mean reponse time
  Observed by many, Little was first to prove
Applies to any system in equilibrium, as long as black box not creating or destroying tasks
Arrivals
Departures
Notes: Old and New Testament by Kleirock
Regret skipping as grad student

## Slide 4: Deriving Little’s Law
Timeobserve = elapsed time that observe a system
Numbertask = number of (overlapping) tasks during Timeobserve
Timeaccumulated = sum of elapsed times for each task
Then
Mean number tasks in system = Timeaccumulated / Timeobserve
Mean response time = Timeaccumulated / Numbertask
Arrival Rate = Numbertask / Timeobserve
Factoring RHS of 1st equation
Timeaccumulated / Timeobserve = Timeaccumulated / Numbertask x
Numbertask / Timeobserve
Then get Little’s Law:
Mean number tasks in system = Arrival Rate x Mean response time

## Slide 5: A Little Queuing Theory: Notation
Notation: Timeserver average time to service a task Average service rate = 1 / Timeserver (traditionally µ) Timequeue average time/task in queue Timesystem average time/task in system = Timequeue + Timeserver Arrival rate avg no. of arriving tasks/sec (traditionally λ)
Lengthserver average number of tasks in service Lengthqueue average length of queue Lengthsystem average number of tasks in service = Lengthqueue + Lengthserver Little’s Law: Lengthserver = Arrival rate x Timeserver (Mean number tasks = arrival rate x mean service time)
Proc
IOC
Device
Queue
server
System
Notes: Sometimes Queue called waiting line, System called Queue

## Slide 6: Server Utilization
For a single server, service rate = 1 / Timeserver
Server utilization must be between 0 and 1, since system is in equilibrium (arrivals = departures); often called traffic intensity, traditionally ρ)
Server utilization = mean number tasks in service = Arrival rate x Timeserver
What is disk utilization if get 50 I/O requests per second for disk and average disk service time is 10 ms (0.01 sec)?
Server utilization = 50/sec x 0.01 sec = 0.5
Or server is busy on average 50% of time

## Slide 7: Time in Queue vs. Length of Queue
We assume First In First Out (FIFO) queue
Relationship of time in queue (Timequeue) to mean number of tasks in queue (Lengthqueue) ?
Timequeue = Lengthqueue x Timeserver + “Mean time to complete service of task when new task arrives if server is busy”
New task can arrive at any instant; how predict last part?
To predict performance, need to know sometime about distribution of events

## Slide 8: Distribution of Random Variables
A variable is random if it takes one of a specified set of values with a specified probability
  Cannot know exactly next value, but may know probability of all possible values
I/O Requests can be modeled by a random variable because OS normally switching between several processes generating independent I/O requests
  Also given probabilistic nature of disks in seek and rotational delays
Can characterize distribution of values of a random variable with discrete values using a histogram
  Divides range between the min & max values into buckets
  Histograms then plot the number in each bucket as columns
  Works for discrete values e.g., number of I/O requests?
What about if not discrete? Very fine buckets

## Slide 9: Characterizing distribution of a random variable
Need mean time and a measure of variance
For mean, use weighted arithmetic mean (WAM):
fi = frequency of task i
Ti = time for tasks I
weighted arithmetic mean = f1T1 + f2T2 + . . . +fnTn
For variance, instead of standard deviation, use Variance (square of standard deviation) for WAM:
Variance = (f1T12 + f2T22 + . . . +fnTn2) – WAM2
  If time is miliseconds, Variance units are square milliseconds!
Got a unitless measure of variance?

## Slide 10: Squared Coefficient of Variance (C2)
C2 = Variance / WAM2  C = sqrt(Variance)/WAM = StDev/WAM
  Unitless measure
Trying to characterize random events, but need distribution of random events with tractable math
Most popular such distribution is exponential distribution, where C = 1
Note using constant to characterize variability about the mean
  Invariance of C over time  history of events has no impact on probability of an event occurring now
  Called memoryless, an important assumption to predict behavior
  (Suppose not; then have to worry about the exact arrival times of requests relative to each other  make math not tractable!)

## Slide 11: Poisson Distribution
Most widely used exponential distribution is Poisson
Described by probability mass function:
Probability (k) = e-a x ak / k!
  where a = Rate of events x Elapsed time
If interarrival times exponentially distributed & use arrival rate from above for rate of events, number of arrivals in time interval t is a Poisson process

## Slide 12: Time in Queue
Time new task must wait for server to complete a task assuming server busy
  Assuming it’s a Poisson process
Average residual service time = ½ x Arithmetic mean x (1 + C2)
  When distribution is not random & all values = average  standard deviation is 0  C is 0  average residual service time = half average service time
  When distribution is random & Poisson  C is 1  average residual service time = weighted arithmetic mean

## Slide 13: Time in Queue
All tasks in queue (Lengthqueue) ahead of new task must be completed before task can be serviced
  Each task takes on average Timeserver
  Task at server takes average residual service time to complete
Chance server is busy is server utilization  expected time for service is Server utilization  Average residual service time
Timequeue = Lengthqueue + Timeserver + Server utilization x Average residual service time
Substituting definitions for Lengthqueue, Average residual service time, & rearranging:
Timequeue = Timeserver x Server utilization/(1-Server utilization)

## Slide 14: Time in Queue vs. Length of Queue
Lengthqueue = Arrival rate x Timequeue
  Little’s Law applied to the components of the black box since they must also be in equilibrium
Given
  Timequeue = Timeserver x Server utilization/(1-Server utilization)
  Arrival rate  Timeserver = Server utilization
 Lengthqueue = Server utilization2 /(1-Server utilization)
Mean no. requests in queue slide 6? (50%)
Lengthqueue = (0.5)2 / (1-0.5) = 0.25/0.5 = 0.5
 0.5 requests on average in queue

## Slide 15: M/M/1 Queuing Model
System is in equilibrium
Times between 2 successive requests arriving, “interarrival times”, are exponentially distributed
Number of sources of requests is unlimited “infinite population model”
Server can start next job immediately
Single queue, no limit to length of queue, and FIFO discipline, so all tasks in line must be completed
There is one server
Called M/M/1 (book also derives M/M/m)
  Exponentially random request arrival (C2 = 1)
  Exponentially random service time (C2 = 1)
  1 server
  M standing for Markov, mathematician who defined and analyzed the memoryless processes

## Slide 16: CS252: Administrivia
Fun talking during Pizza last Wednesday
Project Update Meeting Wednesday 4/19, 10 to 12:30
  635 Soda. Meeting signup online?
Monday 4/24 Quiz 2 5-8 PM in room ?
  (Mainly Ch 4 to 6)
Wed 4/26 Bad Career Advice / Bad Talk Advice ? / Goodbye to Computer Architecture / Your Cal Cultural History
Project Presentations Monday 5/1 (all day)
Project Posters 5/3 Wednesday (11-1 in Soda)
Final Papers due Friday 5/5
  Email Archana, who will post papers on class web site
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 17: Example
40 disk I/Os / sec, requests are exponentially distributed, and average service time is 20 ms
 Arrival rate/sec = 40, Timeserver = 0.02 sec
On average, how utilized is the disk?
Server utilization = Arrival rate  Timeserver = 40 x 0.02 = 0.8 = 80%
What is the average time spent in the queue?
Timequeue = Timeserver x Server utilization/(1-Server utilization)
= 20 ms x 0.8/(1-0.8) = 20 x 4 = 80 ms
What is the average response time for a disk request, including the queuing time and disk service time?
Timesystem=Timequeue + Timeserver = 80+20 ms = 100 ms

## Slide 18: How much better with 2X faster disk?
Average service time is 10 ms
 Arrival rate/sec = 40, Timeserver = 0.01 sec
On average, how utilized is the disk?
Server utilization = Arrival rate  Timeserver = 40 x 0.01 = 0.4 = 40%
What is the average time spent in the queue?
Timequeue = Timeserver x Server utilization/(1-Server utilization)
= 10 ms x 0.4/(1-0.4) = 10 x 2/3 = 6.7 ms
What is the average response time for a disk request, including the queuing time and disk service time?
Timesystem=Timequeue + Timeserver=6.7+10 ms = 16.7 ms
6X faster response time with 2X faster disk!

## Slide 19: Value of Queueing Theory in practice
Learn quickly do not try to utilize resource 100% but how far should back off?
Allows designers to decide impact of faster hardware on utilization and hence on response time
Works surprisingly well

## Slide 20: Cross cutting Issues: Buses  point-to-point links and switches
Standard | width | length | Clock rate | MB/s | Max
(Parallel) ATA | 8b | 0.5 m | 133 MHz | 133 | 2
Serial ATA | 2b | 2 m | 3 GHz | 300 | ?
(Parallel) SCSI | 16b | 12 m | 80 MHz (DDR) | 320 | 15
Serial Attach SCSI | 1b | 10 m | -- | 375 | 16,256
PCI | 32/64 | 0.5 m | 33 / 66 MHz | 533 | ?
PCI Express | 2b | 0.5 m | 3 GHz | 250 | ?
No. bits and BW is per direction  2X for both directions (not shown).
Since use fewer wires, commonly increase BW via versions with 2X-12X the number of wires and BW

## Slide 21: Storage Example: Internet Archive
Goal of making a historical record of the Internet
  Internet Archive began in 1996
  Wayback Machine interface perform time travel to see what the website at a URL looked like in the past
It contains over a petabyte (1015 bytes), and is growing by 20 terabytes (1012 bytes) of new data per month
In addition to storing the historical record, the same hardware is used to crawl the Web every few months to get snapshots of the Interne.

## Slide 22: Internet Archive Cluster
1U storage node PetaBox GB2000 from Capricorn Technologies
Contains 4 500 GB Parallel ATA (PATA) disk drives, 512 MB of DDR266 DRAM, one 10/100/1000 Ethernet interface, and a 1 GHz C3 Processor from VIA (80x86).
Node dissipates  80 watts
40 GB2000s in a standard VME rack,  80 TB of raw storage capacity
40 nodes are connected with a 48-port 10/100 or 10/100/1000 Ethernet switch
Rack dissipates about 3 KW
1 PetaByte = 12 racks

## Slide 23: Estimated Cost
Via processor, 512 MB of DDR266 DRAM, ATA disk controller, power supply, fans, and enclosure = $500
7200 RPM Parallel ATA drives holds 500 GB = $375.
48-port 10/100/1000 Ethernet switch and all cables for a rack = $3000.
Cost $84,500 for a 80-TB rack.
160 Disks are  60% of the cost

## Slide 24: Estimated Performance
7200 RPM Parallel ATA drives holds 500 GB, has an average time seek of 8.5 ms, transfers at 50 MB/second from the disk. The PATA link speed is 133 MB/second.
  performance of the VIA processor is 1000 MIPS.
  operating system uses 50,000 CPU instructions for a disk I/O.
  network protocol stacks uses 100,000 CPU instructions to transmit a data block between the cluster and the external world
ATA controller overhead is 0.1 ms to perform a disk I/O.
Average I/O size is 16 KB for accesses to the historical record via the Wayback interface, and 50 KB when collecting a new snapshot
Disks are limit:  75 I/Os/s per disk, 300/s per node, 12000/s per rack, or about 200 to 600 Mbytes / sec Bandwidth per rack
Switch needs to support 1.6 to 3.8 Gbits/second over 40 Gbit/sec links

## Slide 25: Estimated Reliability
CPU/memory/enclosure MTTF is 1,000,000 hours (x 40)
PATA Disk MTTF is 125,000 hours (x 160)
PATA controller MTTF is 500,000 hours (x 40)
Ethernet Switch MTTF is 500,000 hours (x 1)
Power supply MTTF is 200,000 hours (x 40)
Fan MTTF is 200,000 hours (x 40)
PATA cable MTTF is 1,000,000 hours (x 40)
MTTF for the system is 531 hours ( 3 weeks)
70% of time failures are disks
20% of time failures are fans or power supplies

## Slide 26: RAID Paper Discussion
What was main motivation for RAID in paper?
Did prediction of processor performance and disk capacity hold?
What were the performance figures of merit to compare RAID levels?
What RAID groups sizes were in the paper? Are they realistic? Why?
Why would RAID 2 (ECC) have lower predicted MTTF than RAID 3 (Parity)?
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 27: RAID Paper Discussion
How propose balance performance and capacity of RAID 1 to RAID 5? What do you think of it?
What were some of the open issues? Which were significant?
In retrospect, what do you think were important contributions?
What did the authors get wrong?
In retrospect:
  RAID in Hardware vs. RAID in Software
  Rated MTTF vs. in the field
  Synchronization of disks in an array
  EMC ($10B sales in 2005) and RAID
  Who invented RAID?
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 28: Summary
Little’s Law: Lengthsystem = rate x Timesystem (Mean number customers = arrival rate x mean service time)
Appreciation for relationship of latency and utilization:
Timesystem= Timeserver +Timequeue
Timequeue = Timeserver x Server utilization/(1-Server utilization)
Clusters for storage as well as computation
RAID paper: Its reliability, not performance, that matters for storage
Proc
IOC
Device
Queue
server
System