## Slide 1: Fast and Efficient Genome Analysis via New Algorithms and Architectures
Can Firtina
canfirtina@gmail.com
https://canfirtina.com 6 May 2025 Inria – GenScale & Symbiose

## Slide 2: The Goal of Computing: Beyond Numbers
“The purpose of computing is [to gain] insight, not numbers”
Richard Hamming
"Numerical Methods for Scientists and Engineers," Richard Hamming, 1962.

## Slide 3: Computing is Bottlenecked by Data
Large recommender systems
Large Language Models
Graph/Tree Processing
Genomics

## Slide 4: Computing is Bottlenecked by Data
Large recommender systems
Large Language Models
Graph/Tree Processing
Genomics
Data movement → Performance & Energy Bottleneck

## Slide 5: Problems with Data Analysis Today
Special-Purpose Machine
for Data Generation
FAST
General-Purpose Machine
for Data Analysis
SLOW
Processing capabilities oblivious to data analysis requirements
Large amounts of data movement

## Slide 6: Data Movement Dominates Performance
Microprocessor
Main Memory
Storage (SSD/HDD)
Sequencing
Machine
Data movement dominates performance and is a major system energy bottleneck (accounting for 40%-62%)
- Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS 2018
- Kestor et al., “Quantifying the Energy Cost of Data Movement in Scientific Applications,” IISWC 2013
- Pandiyan and Wu, “Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms,” IISWC 2014
Data Movement
Single memory request consumes >160 - 800 more energy compared to performing an addition operation

## Slide 7
We need to co-design algorithms and architecture to handle data well

## Slide 8: Pushing Towards New Architectures
GPUs
Heterogeneous
Processors &
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
FPGAs
Modern systems
?
Sequencing Machine

## Slide 9: Pushing Towards New Architectures
GPUs
Heterogeneous
Processors &
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
FPGAs
Modern systems
?
Sequencing Machine

## Slide 10: Algorithm-Architecture Co-design is Critical
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Computer Architecture (expanded view)

## Slide 11: Accelerating Genome Analysis [DAC ‘23]
Onur Mutlu and Can Firtina, "Accelerating Genome Analysis via Algorithm-Architecture Co-Design" Invited Special Session Paper in Proceedings of the 60th Design Automation Conference (DAC), San Francisco, CA, USA, July 2023. [Related Invited Paper] [arXiv version] [Slides (pptx) (pdf)] [Talk Video at DAC 2023] (38 minutes, including Q&A)

## Slide 12: Analyzing Genomes Reveals Key Insights
Detecting pathogens in the environment
Rapid surveillance of disease outbreaks
Altering genomes to solve fundamental challenges of life
Personalized Medicine

## Slide 13: Generating the Entire Genomic Sequence
Whole Genome: 6.4B bps
(Non-human-readable)
CGAAATGCC...AGATTAAACGCT...TGCCCTAA...GAATGGCGT
Whole Human Genome: 6.4B bps (Human-readable)
Raw Genomic Data (Human-readable?)
Sequencing Device
Translator (Basecalling)
AI

## Slide 14: Genomic Data: Giant Jigsaw Puzzle to Solve
CGAAATGCC...AGATTAAACGCT...TGCCCTAA...GAATGGCGT
Human (Reference) Genome: 3.2 Billion bps (haploid)
Unknown origins
?
Non-identical reference genome
Small pieces (reads)
Large volume of data to analyze
AAATGG
Read: ~100 – 100,000 bps
?
Scale: ~
CGAAATGCC...AGATTAAATGGT...TGCCCTAA...GAATGGCGT
Entire Genomic Sequence of an Organism
Data Science for Massive Datasets (TBs to PBs)

## Slide 15: Solving the Puzzle: The Naïve Way
CGAAATGCC...AGATTAAACGCT...TGCCCTAA...GAATGGCGT
Human (Reference) Genome: 3.2 Billion bps (haploid)
AAATGG
Pairwise Approximate String Matching
(Alignment)
Entire Genome
For All Reads
Years

## Slide 16: Solving the Puzzle: The Practical Way
CGAAATGCC...AGATTAAACGCT...TGCCCTAA...GAATGGCGT
Performing the costly computations only for a few regions
Goal: Quickly and accurately reduce the search space
Read Mapping
Hash
0x01
Indexing
Hash Table
0x00
0x01
0xFF
…
Hash
Positions
2,64,…
13,21
1,101,…
Sketching
Reference Genome
Store
Query
Chaining
Hash Matches
Seeding
Hash
0x00
Sketching
Read
Alignment
DP Calculations
AAATGG
AAATGG
AAATGG
Exact Match
AAA
AAA
CTA
AAT
AAA

## Slide 17: A Common Genome Analysis Pipeline
Assembly
Variant Calling
Metagenomics
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Downstream Analysis
Raw Reads
Read Mapping
Basecalling (Translator)
AAATGTGGTCCATTG
Basecalled (Translated) Reads

## Slide 18: Genome Analysis is Energy Inefficient
Raw Reads
Read Mapping
Basecalling (Translator)
- Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS 2018
- Kestor et al., “Quantifying the Energy Cost of Data Movement in Scientific Applications,” IISWC 2013
- Pandiyan and Wu, “Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms,” IISWC 2014
Single memory request consumes >160 - 800 more energy compared to performing an addition operation
Costly and large volumes of data movement
Power-Hungry Devices
AAATGTGGTCCATTG
Basecalled (Translated) Reads

## Slide 19: Genome Analysis is Computationally Costly
Chart: Runtime (Hour)
| Basecalling + Read Mapping | Assembly
Heterogeneous System (with CPUs and GPUs) | 16 | 1.5
Significant computation and energy overhead

## Slide 20: Limited Application Scope and Accuracy
Energy-efficient analysis for Resource-constrained devices
Urgent analysis within minutes
Large-scale analysis without sacrificing accuracy and performance

## Slide 21
Enabling New Directions in Genome Analysis via New Algorithms

## Slide 22: New Frontiers: Raw Signal Analysis [ISMB ‘23]
Can Firtina, Nika Mansouri Ghiasi, Joel Lindegger, Gagandeep Singh, Meryem Banu Cavlak, Haiyu Mao, and Onur Mutlu, "RawHash: Enabling Fast and Accurate Real-Time Analysis of Raw Nanopore Signals for Large Genomes" Proceedings of the 31st Annual Conference on Intelligent Systems for Molecular Biology (ISMB) and the 22nd European Conference on Computational Biology (ECCB), July 2023 [Online link at Bioinformatics Journal] [arXiv version] [Slides (pptx) (pdf)] [Talk Video at ISMB/ECCB 2023] (19 minutes) [RawHash Source Code]

## Slide 23: Real-Time Raw Signal Analysis [Bioinform. ‘24]
Can Firtina, Melina Soysal, Joël Lindegger, and Onur Mutlu, "RawHash2: Mapping Raw Nanopore Signals Using Hash-Based Seeding and Adaptive Quantization" Bioinformatics, July 2024. [Online link at Bioinformatics Journal] [arXiv version] [RawHash Talk Video] (19 minutes) [RawHash2 Source Code]

## Slide 24: New Directions: Assembling Raw Signals
Can Firtina, Maximilian Mordig, Harun Mustafa, Sayan Goswami, Nika Mansouri Ghiasi, Stefano Mercogliano, Furkan Eris, Joël Lindegger, Andre Kahles, and Onur Mutlu "Rawsamble: Overlapping and Assembling Raw Nanopore Signals using a Hash-based Seeding Mechanism" arXiv, October 2024 [arXiv version] [Talk Video at CSHL Data Science 2024] (16 minutes) [Source Code]
arXiv
Source code

## Slide 25: Quickly Aligning Raw Signals
Joel Lindegger, Can Firtina, Nika Mansouri Ghiasi, Mohammad Sadrosadati, Mohammed Alser, and Onur Mutlu, "RawAlign: Accurate, Fast, and Scalable Raw Nanopore Signal Mapping via Combining Seeding and Alignment" IEEE Access, December 2024. [Online link at IEEE Access Journal] [arXiv version] [RawAlign Source Code]

## Slide 26: Tolerating Noise in String Matching [NARGAB ‘23]
Can Firtina, Jisung Park, Mohammed Alser, Jeremie S. Kim, Damla Senol Cali, Taha Shahroodi, Nika Mansouri Ghiasi, Gagandeep Singh, Konstantinos Kanellopoulos, Can Alkan, and Onur Mutlu, "BLEND: A Fast, Memory-Efficient, and Accurate Mechanism to Find Fuzzy Seed Matches in Genome Analysis" NAR Genomics and Bioinformatics, March 2023. [Online link at NAR Genomics and Bioinformatics Journal] [arXiv version] [bioRxiv version] [Talk Video at RECOMB 2023] (23 minutes) [BLEND Source Code]

## Slide 27: Mitigating Useless Computations [TCBB ‘24]
Jeremie S. Kim*, Can Firtina*, Meryem Banu Cavlak, Damla Senol Cali, Nastaran Hajinazar, Mohammed Alser, Can Alkan, and Onur Mutlu, "AirLift: A Fast and Comprehensive Technique for Remapping Alignments between Reference Genomes" IEEE/ACM TCBB, August 2024. [Online link at IEEE/ACM TCBB Journal] [arXiv version] Presented at the 21st Asia Pacific Bioinformatics Conference (APBC), Changsha, China, April 2023. [Slides (pptx) (pdf)] [Talk Video at BIO-Arch 2023 Workshop] (22 minutes) [AirLift Source Code]
*Equal contribution

## Slide 28: Mitigating Useless Computations [Bioinform. ‘22]
Jeremie S. Kim, Can Firtina, Meryem Banu Cavlak, Damla Senol Cali, Can Alkan, and Onur Mutlu, "FastRemap: A Tool for Quickly Remapping Reads between Genome Assemblies" Bioinformatics, October 2022. [Online link at Bioinformatics Journal] [arXiv preprint] [FastRemap Source Code]

## Slide 29
Utilizing AI/ML in Genome Analysis via New Algorithms and Architectures

## Slide 30: Error Correction using ML [Bioinform. ‘20]
Can Firtina, Jeremie S. Kim, Mohammed Alser, Damla Senol Cali, A. Ercument Cicek, Can Alkan, and Onur Mutlu, "Apollo: A Sequencing-Technology-Independent, Scalable, and Accurate Assembly Polishing Algorithm" Bioinformatics, June 2020. [Online link at Bioinformatics Journal] [arXiv version] [Slides (pptx)][(pdf)] [Source Code]

## Slide 31: Accelerating ML & Genome Graphs [TACO ‘24]
Can Firtina, Kamlesh Pillai, Gurpreet S. Kalsi, Bharathwaj Suresh, Damla Senol Cali, Jeremie S. Kim, Taha Shahroodi, Meryem Banu Cavlak, Joel Lindegger, Mohammed Alser, Juan Gomez Luna, Sreenivas Subramoney and Onur Mutlu, "ApHMM: Accelerating Profile Hidden Markov Models for Fast and Energy-efficient Genome Analysis" ACM Transactions on Architecture and Code Optimization (TACO), Feb 2024. [ACM Digital Library version] [arXiv version] Presented at the 19th HiPEAC Conference, Munich, Germany, January 2024. [Slides (pptx) (pdf)] [Talk Video HiPEAC 2024] (35 minutes) [ApHMM Source Code]

## Slide 32: Translating Raw Signals using ML [Genome. Biol. ‘24]
Gagandeep Singh, Mohammed Alser, Kristof Denolf, Can Firtina, Alireza Khodamoradi, Meryem Banu Cavlak, Henk Corporaal and Onur Mutlu, "RUBICON: A Framework for Designing Efficient Deep Learning-Based Genomic Basecallers" Genome Biology, February 2024. [arXiv version] [Online link at Genome Biology Journal] [RUBICON Source Code]

## Slide 33: Eliminating Useless Basecalling [Front. In Genetics ‘24]
M. Banu Cavlak, Gagandeep Singh, Mohammed Alser, Can Firtina, Joel Lindegger, Mohammad Sadrosadati, Nika Mansouri Ghiasi, Can Alkan, and Onur Mutlu, "TargetCall: Eliminating the Wasted Computation in Basecalling via Pre-Basecalling Filtering" Frontiers in Genetics, October 2024. [Online link at Frontiers in Genetics Journal] [arXiv Version] [Talk Video at BIO-Arch 2023 Workshop] [TargetCall Source Code]

## Slide 34: ML-based Genome Analysis via PIM [MICRO ‘22]
Haiyu Mao, Mohammed Alser, Mohammad Sadrosadati, Can Firtina, Akanksha Baranwal, Damla Senol Cali, Aditya Manglik, Nour Almadhoun Alserr, and Onur Mutlu, "GenPIP: In-Memory Acceleration of Genome Analysis via Tight Integration of Basecalling and Read Mapping" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (25 minutes)] [arXiv version]

## Slide 35: Basecalling using PIM [MICRO ‘23]
Taha Shahroodi, Gagandeep Singh, Mahdi Zahedi, Haiyu Mao, Joel Lindegger, Can Firtina, Stephan Wong, Onur Mutlu, and Said Hamdioui, "Swordfish: A Framework for Evaluating Deep Neural Network-based Basecalling using Computation-In-Memory with Non-Ideal Memristors" Proceedings of the 56th International Symposium on Microarchitecture (MICRO), Toronto, ON, Canada, November 2023. [Slides (pptx) (pdf)] [arXiv version]

## Slide 36
Fast, Accurate, and Efficient Genome Analysis via Algorithm-Architecture co-design

## Slide 37: Accelerating String Matching [MICRO ‘20]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lightning Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 38: Accelerating Genome Graphs [ISCA ‘22]
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika Mansouri Ghiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [Slides (pptx) (pdf)] [arXiv version] [SeGraM Source Code and Datasets] [Talk Video (22 minutes)]

## Slide 39: In-Storage Filtering for Genomics [ASPLOS ‘22]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, Feb 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]

## Slide 40: In-Storage Metagenomics [ISCA ‘24]
Nika Mansouri Ghiasi, Mohammad Sadrosadati, Harun Mustafa, Arvid Gollwitzer, Can Firtina, Julien Eudine, Haiyu Mao, Joel Lindegger, Meryem Banu Cavlak, Mohammed Alser, Jisung Park, and Onur Mutlu, "MegIS: High-Performance and Low-Cost Metagenomic Analysis with In-Storage Processing" Proceedings of the 51st Annual International Symposium on Computer Architecture (ISCA), Buenos Aires, Argentina, July 2024. [Slides (pptx) (pdf)] [arXiv version]

## Slide 41: Accelerating Genome Analysis [DAC ‘23]
Onur Mutlu and Can Firtina, "Accelerating Genome Analysis via Algorithm-Architecture Co-Design" Invited Special Session Paper in Proceedings of the 60th Design Automation Conference (DAC), San Francisco, CA, USA, July 2023. [Related Invited Paper] [arXiv version] [Slides (pptx) (pdf)] [Talk Video at DAC 2023] (38 minutes, including Q&A)

## Slide 42: My Involvements During my Ph.D.
First/Co-First Author Publications
Today’s Talk
Algorithm & Hardware Design for AI in Genome Analysis
[Bioinformatics'20]
[ACM TACO'24]
[Genome Biology'24]
[Front. in Genetics'24]
Real-Time and Raw Sequencing Data Analysis
[ISMB/ECCB'23]
[Bioinformatics'24]
[IEEE Access'24]
[arXiv'24 & HiTSeq'24]
Accurate and Fast Algorithm Design for Read Mapping
[Bioinformatics'22]
[NARGAB'23 & RECOMB'23]
[arXiv'23]
[arXiv'23]
[IEEE/ACM TCBB'24]
Data-Centric Architectures for Genome Analysis
[MICRO'20]
[MICRO'22]
[ISCA'22]
[ASPLOS'22]
[IEEE Access'22]
[MICRO'23]
[ISCA'24]
Reviews: [CSBJ'22] [DAC'23] [Nature Protocols'24]
Goal: Enable Fast, Energy-Efficient, Accurate, and Scalable Genome Analysis by Designing Algorithms and Architectures

## Slide 43: Today’s Talk
Significant computation and energy overhead
Limited accuracy and application scope
Algorithm & Hardware Design for AI in Genome Analysis
3
ApHMM (TACO'24 & HiPEAC'24)
  Accelerating ML operations in Genome Graphs
Real-Time and Raw Sequencing Data Analysis
1
RawHash (ISMB/ECCB'23)
  Enabling real-time and accurate read mapping without basecalling
2
Rawsamble (arXiv'24 & HiTSeq'24)
  Enabling new applications by assembling raw sequencing data

## Slide 44: Today’s Talk
Significant computation and energy overhead
Limited accuracy and application scope
Algorithm & Hardware Design for AI in Genome Analysis
3
ApHMM (TACO'24 & HiPEAC'24)
  Accelerating ML operations in Genome Graphs
Real-Time and Raw Sequencing Data Analysis
1
RawHash (ISMB/ECCB'23)
  Enabling real-time and accurate read mapping without basecalling
2
Rawsamble (arXiv'24 & HiTSeq'24)
  Enabling new applications by assembling raw sequencing data
RawHash
Rawsamble
ApHMM
Future Research

## Slide 45: Basecalling is Accurate yet Costly
Raw Reads
Read Mapping
Basecalling (Translator)
Costly
AI Models
AAATGTGGTCCATTG
Basecalled Reads
Highly accurate reads
Noisy Raw Signals
How to make this pipeline cheaper?
RawHash
Rawsamble
ApHMM
Future Research

## Slide 46: Can We Survive Without Translation?
Raw Reads
Read Mapping
Reference Genome
CTGCGTAGCAGCGTAATAG
...
...
How to communicate without an accurate translator?
Noisy Raw Signals
RawHash
Rawsamble
ApHMM
Future Research

## Slide 47: Can We Survive With Noisy Signal Analysis?
Raw Reads
Read Mapping
Reference Genome
CTGCGTAGCAGCGTAATAG
...
...
-0.06,0.24,-0.74,
...
...
Reference-to-Signal Conversion
Raw Signal Analysis
How to identify similarity between noisy signals?
Noisy Raw Signals
RawHash
Rawsamble
ApHMM
Future Research

## Slide 48: Noise in Raw Electrical Signals
Key Idea: Perform similarity estimation based on vector similarity search
[ , , , , ]
-0.22
0.96
-0.75
-0.06
-0.49
Raw Signals:
-0.21
1.01
-0.76
-0.05
-0.51
Raw Signals:
Problem: Too Costly for Large Genomes
[ , , , , ]
Sequencing CTGCGTAGCA
Sequencing CTGCGTAGCA
Nearest Neighbor Search
Observation: Identical molecules generate similar raw signals
RawHash
Rawsamble
ApHMM
Future Research

## Slide 49: Scalability Issues Limit Real-Time Analysis
Genome Size Increase: 150
2.4
9.2
28
No Real-Time Analysis for Larger Genomes: Searching mechanism does not scale well
RawHash
Rawsamble
ApHMM
Future Research

## Slide 50: Benefits of Real-Time Analysis
Sequencing
Analysis
Time
Reducing sequencing time and cost by stopping sequencing early
✓
Reducing latency by overlapping analysis with sequencing
✓
Completely Sequenced Read
Sequenced Bases
Sequencing & Real-Time Analysis
Reduced Latency
Partially Sequenced Read
Sequencing is stopped early with a real-time decision
Reduced Sequencing Time (and Cost)
RawHash
Rawsamble
ApHMM
Future Research

## Slide 51: Goal
Enable Fast, Accurate, and Scalable Real-Time Analysis for Larger Genomes
RawHash
Rawsamble
ApHMM
Future Research

## Slide 52: Key Idea
[ , , , , ]
RawHash
Rawsamble
ApHMM
Future Research
-0.22
0.96
-0.75
-0.06
-0.49
Raw Signals:
-0.21
1.01
-0.76
-0.05
-0.51
Raw Signals:
Key Idea: Perform similarity estimation based on quick exact matches
Challenge: How to generate the same hash value for similar enough signals with various noise types?
Hash
Hash
0x77db
0x77db
Fast Match
CTGCGT
[ , , , , ]

## Slide 53: RawHash Key Idea – Quantization
Range of raw signals (normalized)
-3.00
+3.00
0
1
2
3
4
5
6
7
8
9
14
15
10
11
12
13
Bucket #
CTGCGT
-0.06
-0.07
-0.05
-0.05
-0.06
Enables matching raw signals by eliminating slight differences
✓
Quantize
Quantize
Quantize
Quantize
Quantize
RawHash
Rawsamble
ApHMM
Future Research

## Slide 54: How to Better Quantize Signals?
Range of raw signals (normalized)
-3.00
+3.00
0
1
2
3
4
5
6
7
8
9
14
15
10
11
12
13
Bucket #
Equal-width buckets leads to unbalanced bucket loading
✕
Reduced uniqueness and poor resource utilization
✕
-3.00
+3.00
200
400
600
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
K-mer count
RawHash
Rawsamble
ApHMM
Future Research

## Slide 55: Adaptive Quantization
Key Idea: Quantizing raw signals with non-equal bucket widths by leveraging raw signal distribution
-3.00
3.00
K-mer count
Better bucket utilization
✓
Range of raw signals (normalized)
-3.00
+3.00
0
1
2
3
4
5
6
7
8
9
14
15
10
11
12
13
Bucket #
RawHash
Rawsamble
ApHMM
Future Research

## Slide 56: RawHash Key Idea – Hash-based Matching
Sequencing CTGCGTAGCA
-0.22
0.96
-0.75
-0.06
-0.49
Hash
0x77db
Fast and Accurate Match
RawHash
Rawsamble
ApHMM
Future Research
[ , , , , ]
Key Contribution: The first hash-based search (and indexing) mechanism for raw signals
Quantize
0b0111
Quantize
0b0111
Quantize
0b0110
Quantize
0b1011
Quantize
0b0110
Pack
0b01110111011010110110
Hash
0x77db

## Slide 57: Real-Time Analysis Benefits from Fast Search
Genome Size Increase: 150
2.4
9.2
28
Real-time Analysis for Human Genomes: Fast search instead of costly neighbor search
RawHash
Rawsamble
ApHMM
Future Research

## Slide 58: Fast Search Leads to Accurate Search
Best accuracy for all genomes: Hash values span longer sequences than vectors -> More unique and informative matches
(Almost) Identical accuracy to basecalled analysis:
Is the small difference because RawHash is even better?
RawHash
Rawsamble
ApHMM
Future Research

## Slide 59: RawHash is Open Source
RawHash
Rawsamble
ApHMM
Future Research

## Slide 60: RawHash’s Impact
RawHash
Several works building on RawHash:
Alignment without basecalling [IEEE Access'24]
Assembly without basecalling [arXiv’24]
In-storage processing [Accepted to ICS'25]
In-memory processing [Unpublished work]
Collaboration with Industry to Accelerate Genome Analysis
[Ongoing]
Collaboration with Medical Centers to Accelerate Sequence-to-Answer
[Ongoing]
RawHash
Rawsamble
ApHMM
Future Research

## Slide 61: Today’s Talk
Significant computation and energy overhead
Limited accuracy and application scope
Algorithm & Hardware Design for AI in Genome Analysis
3
ApHMM (TACO'24 & HiPEAC'24)
  Accelerating ML operations in Genome Graphs
Real-Time and Raw Sequencing Data Analysis
1
RawHash (ISMB/ECCB'23)
  Enabling real-time and accurate read mapping without basecalling
2
Rawsamble (arXiv'24 & HiTSeq'24)
  Enabling new applications by assembling raw sequencing data
RawHash
Rawsamble
ApHMM
Future Research

## Slide 62: Today’s Talk
Significant computation and energy overhead
Limited accuracy and application scope
Algorithm & Hardware Design for AI in Genome Analysis
3
ApHMM (TACO'24 & HiPEAC'24)
  Accelerating ML operations in Genome Graphs
Real-Time and Raw Sequencing Data Analysis
1
RawHash (ISMB/ECCB'23)
  Enabling real-time and accurate read mapping without basecalling
2
Rawsamble (arXiv'24 & HiTSeq'24)
  Enabling new applications by assembling raw sequencing data
RawHash
Rawsamble
ApHMM
Future Research

## Slide 63
Pushing the Boundaries of Application Scope via New Algorithms

## Slide 64: Beyond Reference Mapping: Overlapping
TGCTGCAATCGTGATCCGAAGTCAGCCGTAGTGGACCACCGGTAAGCT
TGCTGCAA
CTGCAATC
TGATCCGA
CGAAGTCA
TCAGCCGT
CGTAGTGG
AGTGGACC
CCACCGGT
GGTAAGCT
Raw Nanopore Signals
Hash-Based Seeding and Mapping
Raw Nanopore Signals
Reference Signals
Reference Genome (Converted to Signals)
Challenge: Reference genome is not always available
Assembly: Constructing genome from overlapping reads
Existing solutions cannot find overlapping reads without basecalling
✕
RawHash
Rawsamble
ApHMM
Future Research

## Slide 65: Challenges with Overlapping Raw Signals
Hash-Based Seeding and Mapping
Challenge: Finding many useful overlapping pairs (all-vs-all overlapping)
Challenge: Identifying hash matches when both signals are noisy
Challenge: Generating long paths from useful overlaps
RawHash
Rawsamble
ApHMM
Future Research

## Slide 66
The first mechanism that can perform all-vs-all overlapping from raw signals
Rawsamble
RawHash
Rawsamble
ApHMM
Future Research

## Slide 67: Eliminating Basecalling from the Pipeline
Basecalling (CPU) + Overlapping
Rawsamble
Basecalling (GPU) + Overlapping
SARS-CoV-2
E. coli
Yeast
Green Algae
Human
Geo. Mean
Elapsed Time (Normalized to Rawsamble)
Average speedup of 60 than CPU-based basecalling: Eliminating basecalling leaves a significant room for performance improvements
Average speedup of 2 than the GPU-based basecalling: GPU vs. GPU comparison is likely to provide even better results
59.70
1.99
RawHash
Rawsamble
ApHMM
Future Research

## Slide 68: Key Results – First Ever Assemblies
First assemblies ever constructed without basecalling
~400 longer assembled pieces than the average read length: Informative overlaps lead to longer paths
It is time to rethink if we want to translate individual reads separately
E. coli Assembly (From the Rawsamble Overlaps)
RawHash
Rawsamble
ApHMM
Future Research

## Slide 69: Today’s Talk
Significant computation and energy overhead
Limited accuracy and application scope
Algorithm & Hardware Design for AI in Genome Analysis
3
ApHMM (TACO'24 & HiPEAC'24)
  Accelerating ML operations in Genome Graphs
Real-Time and Raw Sequencing Data Analysis
1
RawHash (ISMB/ECCB'23)
  Enabling real-time and accurate read mapping without basecalling
2
Rawsamble (arXiv'24 & HiTSeq'24)
  Enabling new applications by assembling raw sequencing data
RawHash
Rawsamble
ApHMM
Future Research

## Slide 70: Today’s Talk
Significant computation and energy overhead
Limited accuracy and application scope
Algorithm & Hardware Design for AI in Genome Analysis
3
ApHMM (TACO'24 & HiPEAC'24)
  Accelerating ML operations in Genome Graphs
Real-Time and Raw Sequencing Data Analysis
1
RawHash (ISMB/ECCB'23)
  Enabling real-time and accurate read mapping without basecalling
2
Rawsamble (arXiv'24 & HiTSeq'24)
  Enabling new applications by assembling raw sequencing data
RawHash
Rawsamble
ApHMM
Future Research

## Slide 71: Algorithm Design Demands General-Purpose Computing Capabilities
RawHash
Rawsamble
ApHMM
Future Research

## Slide 72: Algorithm Design Demand General-Purpose Computing Capabilities
Function 2
Function 4
RawHash
Rawsamble
ApHMM
Future Research
General-Purpose Systems
(e.g., CPUs)
Function 1
Function 3
Your Favorite Output
Your Favorite Algorithm
Paid Costs for Generality:
Supporting unnecessary operations
Inefficient data and control flow
Limited parallelism & bandwidth
High latency &
Substantial energy

## Slide 73: Great Algorithms Demand Specialization
RawHash
Rawsamble
ApHMM
Future Research
Goal: Avoid wasting computation & energy
Opportunities: Better data flow with minimal latency & power
Everyone’s Favorite Algorithm
Function 2
Function 1
Function 3
Function 1
Function 2
Function 3
Application-Specific Architecture
Paid Costs for Specialization:
Poor programmability
High manufacturing and engineering costs
Efficient processors customized for the task
Better parallelism

## Slide 74: Acceleration Efforts for AI and Genomics
RawHash
Rawsamble
ApHMM
Future Research
Google’s TPUs:
Cerebras WSE-3 The largest ML accelerator chip
NVIDIA H100

## Slide 75
Important and Commonly Used Applications Demand Specialization

## Slide 76: Graphs in Genomics
Graphs are commonly used to identify variations between sequences
To avoid redundant comparisons and storage
To provide rich information
on expected variations
Reference Genome Graph
RawHash
Rawsamble
ApHMM
Future Research

## Slide 77: Graph-Based Applications in Genomics
RawHash
Rawsamble
ApHMM
Future Research
Protein
Protein
Family #1
Protein
Family #2
Protein Family Search
with Graph Alignment
GCCCATATGGTTAAGCTT
CCCT
TGCT
GCTA
CCTA
GCTT
ATGC
AAGC
CCCT
GCTT
GCCCTTATGCTTAAGCTA
Error Correction with Probabilistic Graphs
GCCC-TATGGTTAAGCTT
GCCCATATGATTAAGCTT
GCCCATATGGTTAAGCTT
GCCCATATGGTTAAGCTT
GCCCGTATGGTT--GCTT
GCCCATATGCTTAAGCTT
GCCC---TGGTTAAGCT-
GCCCATATCCTTAAGCTT
Multiple Sequence Alignment

## Slide 78: A Common Graph Structure in Genomics
A
C
T
T
D
I
I
I
I
D
D
A: 0.1
T: 0.2
G: 0.6
C: 0.1
A: 0.9
T: 0.1
G: 0.0
C: 0.0
A: 0.1
T: 0.1
G: 0.1
C: 0.7
A: 0.2
T: 0.2
G: 0.2
C: 0.4
0.2
0.4
0.7
0.6
0.3
0.1
RawHash
Rawsamble
ApHMM
Future Research
Profile Hidden Markov Models (PHMMs): A probabilistic graph structure

## Slide 79: Underlying ML Technique in Genomic Graphs
Forward Calculations
Backward Calculations
Updating Transition Probabilities
Updating Emission Probabilities
RawHash
Rawsamble
ApHMM
Future Research

## Slide 80: Underlying ML Technique in Genomic Graphs
Forward Calculations
Backward Calculations
RawHash
Rawsamble
ApHMM
Future Research
Function 1
Function 1
Function 2
Function 2
Function 3
Function 4
Updating Transition Probabilities
Updating Emission Probabilities

## Slide 81: Costly Use of ML in Genomic Graphs
45.76%
51.44%
98.57%
RawHash
Rawsamble
ApHMM
Future Research
Cost of Using Machine Learning (ML) in pHMMs:

## Slide 82: Goal
Enable rapid and power-efficient use of the underlying ML technique in genome graphs
RawHash
Rawsamble
ApHMM
Future Research

## Slide 83: Key Approach: HW-SW Co-Design
SW
HW
Reduce redundant data storage by utilizing the fixed data pattern
Reduce unnecessary computations with quick filtering
Avoid repeated operations by utilizing lookup tables
Reduce data movement by processing data where it makes sense
Flexible and efficient hardware design
RawHash
Rawsamble
ApHMM
Future Research

## Slide 84: HW: Simple Data Pattern in DP Calculations
A
T
G
T
Simple Pattern
A
D
I
D
C
I
D
T
I
RawHash
Rawsamble
ApHMM
Future Research
Store and access data where it makes sense
Many Different Patterns
Dynamic Programming (DP) Operations:
DP Operations in pHMMs:
Frequent off-chip access
DP Computation in pHMMs
Fast On-chip Memory Access
MUL
ADD
FP DIV
MUL

## Slide 85: SW: Reducing Unnecessary Computations
A
T
G
T
Dense DP Calculations
A
D
I
D
C
I
D
T
I
Sparse (Filtered) DP Calculations
A
D
I
D
C
I
D
T
I
A
T
G
T
Filter by sorting
Observation: Calculating the entire DP is not needed
Challenge: Sorting is costly in hardware
RawHash
Rawsamble
ApHMM
Future Research

## Slide 86: SW: Reducing Unnecessary Computations
Histogram Filter
.
.
.
8, 9
10, 14
15, 16, 18
11, 20, 21, …
13, 17, 19, …
State IDs
Range
1.00 – 0.94
0.94 – 0.88
0.88 – 0.82
0.82 – 0.76
0.76 – 0.70
0.06 – 0.00
.
.
.
Software co-design: Replace sorting with a cheaper filtering
RawHash
Rawsamble
ApHMM
Future Research

## Slide 87: Putting the Optimizations Together
RawHash
Rawsamble
ApHMM
Future Research
Effectively implementing the hardware and software optimizations to improve performance and reduce power requirements

## Slide 88: Integrating ApHMM in a Complete System
The specialized task can be offloaded to an accelerator whenever needed
RawHash
Rawsamble
ApHMM
Future Research

## Slide 89: Key Results: Performance
RawHash
Rawsamble
ApHMM
Future Research
Specialized design enables computation up to two orders of magnitude faster:
Better data flow with reduced latency and improved parallelism
Chart: Speedup Over CPU (1 Thread)
| Algorithm Acceleration
CPU (32 Threads) | 23.0925
GPU | 74.9956
ApHMM | 260.0273

## Slide 90: Key Results: Energy Consumption
RawHash
Rawsamble
ApHMM
Future Research
…and a significant reduction in energy consumption by up to three orders of magnitude: simpler hardware with a minimized off-chip memory accesses and data movement
Chart: Energy Reduction Over CPU
| Algorithm Acceleration
CPU | 1
GPU | 1.4528
ApHMM | 2474.0912

## Slide 91
Specialization Provides Significant Performance and Energy Benefits

## Slide 92: Today’s Talk
Significant computation and energy overhead
Limited accuracy and application scope
Algorithm & Hardware Design for AI in Genome Analysis
3
ApHMM (TACO'24 & HiPEAC'24)
  Accelerating ML operations in Genome Graphs
Real-Time and Raw Sequencing Data Analysis
1
RawHash (ISMB/ECCB'23)
  Enabling real-time and accurate read mapping without basecalling
2
Rawsamble (arXiv'24 & HiTSeq'24)
  Enabling new applications by assembling raw sequencing data

## Slide 93: Acknowledgements
Collaborators:
Funding agencies and industry sponsors:
  BioPIM, SNSF, Intel, Google, Huawei, Microsoft, VMware, and SRC

## Slide 94: Fast and Efficient Genome Analysis via New Algorithms and Architectures
Can Firtina
canfirtina@gmail.com
https://canfirtina.com 6 May 2025 Inria – GenScale & Symbiose

## Slide 95: Sequencing Data Analysis
Heuristic Algorithms
Data Structures
Filters
Distributed Computing
Hardware Accelerators
Quick, accurate, and energy-efficient analysis
✓
✕
Imperfections in sequencing data impacts design choices
TATGG
GCCTA
TGCAC
AAGCC
TATAT
TGGTA
AGATA
CCTGG

## Slide 96: Data Movement Overhead
A memory access consumes ~100-1000X
the energy of a complex addition
William Dally,
HiPEAC 2015
RawHash
Rawsamble
ApHMM
Future Research

## Slide 97: Minimizer Sketching
Hash
0xA1
0x02
0xFC
0x45
Find
Minimum
Window of
k-mers ()
Overlapping k-mers ()
GCTATTA
TATTACC
CTATTAC
ATTACCT
0x02
CTATTAC
Sampled
k-mer (Minimizer)
Hash
Hash
Hash
Hash Table
GCTATTACCT

## Slide 98: Spaced Seeding
Pattern
GXTAXTA
GCTATTA
GATACTA
GXTAXTA
GACACTA
GXCAXTA
0xA1
0xA1
0xFC
Spaced Seeds
Hash
Hash
Hash
Pattern
Pattern

## Slide 99: Strobemer Sketches
GCTATTACCTTAATGTGATGGAC
GCTATCCCCTTAATGGGATGGAC
Link
GCTATTAATGGA
GCTATTAATGGA
GCCCTCCCCTTAAAGGGAATGGA
CCTCTAAATGGA
0xA1
0xA1
0xFC
Selected k-mers (e.g., minimizers)
Strobemers
Hash
Hash
Hash
Link
Link

## Slide 100: Hash-Based Sketching and Seed Matching
CAGGCTATAACCCTAATGTTGC
Target Sequence
Hash
Query Sequence
0x01
Hash Table
Store
Query
Match
No Match
GCTATTACCTTAATGTGATGGACGA
0xA4
0x41
0x01
0xFE
0x01
0xA4
0x41
Query
Store
Store
Hash
Hash
Hash
Hash
Sketching
Sketching
GCTA
TAAT
GACG
GCTA
ATGT
<List of Positional Information>

## Slide 101: Chaining (Two Points)
Query Seq.
Target Seq.
Anchor (Seed match)
Chaining
Query Seq.
Target Seq.

## Slide 102: Chaining (Multiple Points)
Exact hash value matches: Needed for finding matching regions between a reference genome and a read
What if there are mutations or errors?
  No hash (seed) match will occur in such positions
The chaining algorithm links exact matches in a proximity even though there are gaps (no seed matches) between them

## Slide 103: Sequence Alignment

## Slide 104: Nanopore Sequencing

## Slide 105: Source of Noise in Nanopore Sequencing
Stochastic thermal fluctuations in the ionic current
  Random ionic movement due to inherent thermal energy (Brownian motion)
Variations in the translocation speed
  Mainly due to the motor protein
Environmental factors
  Temperature: Affecting enzymes including the motor protein
  pH levels: Affecting charge and the shape of molecules
Maybe: Aging & material-related noise between nanopores
  Their effects potentially can be minimized with normalization techniques

## Slide 106: R9 vs. R10 Chemistries
Dual reader head
Motor protein with more consistent translocation speed in R10
Duplex sequencing in R10

## Slide 107: Proteomics with Nanopores
Motone+, “Multi-pass, single-molecule nanopore reading of long protein strands”, Nature 2024.

## Slide 108: Processing Raw Nanopore Signals
K many nucleotides (k-mers) sequenced at a time
Observation: Abrupt change in the signal as DNA moves inside a nanopore (e.g., when sequencing a new k-mer)
Goal: Identify raw signal segments corresponding each sequenced k-mer
  Statistical tests (segmentation) to identify abrupt changes
  Event: A raw signal segment corresponding to a particular k-mer
Event
Segment
pAmpere
Time
…
…
6-mer
…
…
-0.06
TGCGTC
-0.22
ATGCGT

## Slide 109: Scalability Issues with Costly Calculations
CGAAATGCC...AGATTAAATGGGCTTTCT...TGCCCTAA...GAATGGCGT
A Large Genome (Human)
CGAAATGCC...AGATTAAATGGGCTTTCT
A Small Genome (Bacteria)
Computation Cost
(per Region)
Data Generation
Speed
Computation Cost
(per Region)
Data Generation
Speed
Waiting for Data
Waiting for Data
Data
Waiting for Data
Waiting for Data
Data
Increased Latency
No Real-Time Analysis
Real-Time Analysis:
Data is consumed before next one
arrives

## Slide 110: Reference-to-Signal Conversion
Goal: Enable direct comparison to raw signals by converting reference genome into its synthetic signal (one-time task)
K-mer model: Provides expected signal values for every possible k-mer
  A lookup table preconstructed based on nanopore’s characteristics
Use the k-mer model to convert all k-mers of a reference genome to their expected signal values
Reference Genome
Expected Signal
CTGCGTAGCAGCGTAATAG
...
...
GCGTAG
K-mer model
-0.74
CTGCGT
K-mer model
-0.06
TGCGTA
K-mer model
0.24
-0.06,0.24,-0.74,
...
...
Reference Signals
K-mer model
K-mer
Signal
AAAAAA
TTTTTT
…
-0.29
0.04
…

## Slide 111: Challenges in Real-Time Analysis
Rapid analysis to match the nanopore sequencer throughput
Timely decisions to stop sequencing as early as possible
Accurate analysis from noisy raw signal data
Power-efficient computation for scalability and portability

## Slide 112: Applications of Read Until
Depletion: Reads mapping to a particular reference genome is ejected
Enrichment: Reads not mapping to a particular reference genome is ejected
Microbiome studies by removing host DNA
Eliminating known residual DNA or RNA (e.g., mitochondrial DNA)
High abundance genome removal
Removing contaminated organisms
Targeted sequencing (e.g., to a particular region of interest in the genome)
Low abundance genome enrichment

## Slide 113: Applications of Run Until & Sequence Until
Run Until: Stopping the entire sequencing run
Sequence Until: Run Until with accuracy-aware decision making
Stopping when reads reach to a particular depth of coverage
Stopping when the abundance of all genomes reach a particular threshold
Stopping when relative abundance estimations do not change substantially (for high-abundance genomes)
Stopping when finding that the sample is contaminated with a particular set of genomes
…

## Slide 114: In Vitro (e.g., PCR) vs. In Silico
Polymerase Chain Reaction (PCR) as a way of in vitro “analysis”
  Can increase the quantity of DNA in a sample
  Non-dynamic targeted sequencing (e.g., low abundance known targets)
  Requires additional resources: Time and money for preparation and execution of PCR
Adaptive sampling as a way of in silico (i.e., computational) analysis
  Cannot increase the existing quantity of DNA in a sample
  Dynamic targeted sequencing: Decisions can be made based on real-time analysis (e.g., Sequence Until)
  Minimal additional resources
    Almost no additional resources for preparation and execution
    Simultaneous enrichment and depletion is possible
    Better suited for rapid whole genome sequencing
  Beauty of computational analysis (e.g., high flexibility – no need for primers)
PCR and adaptive sampling can be combined depending on the analysis type

## Slide 115: Finding Mapping Positions
Useful for any application that requires exact genomic position
  Variant calling in downstream analysis
  Specifically: Identifying rare variants in cancer genomics
  Methylation profiling
Accurate and flexible depth of coverage estimation
  Alternative: DNA quantification (without computational analysis)
    DNA quantification is challenging for metagenomics analysis
  Computational method: We can map to almost entire set of known reference genomes to accurately estimate the coverage of a metagenomics sample
Transcriptome analysis
  Accurately quantifying expression levels & alternative splicing
Better resolution (i.e., more sensitive analysis) for any other application that does not specifically require mapping positions

## Slide 116
Basecalling
G
G
A
T
Read Mapping
Raw Signal Mapping
Traditional: Translating (basecalling) signals to bases before analysis
Recent Work: Directly analyzing signals without basecalling
Raw Signal
Raw Signal
Basecalled sequences are less noisy than raw signals
Many analysis tools use basecalled sequences
Costly and power-hungry computational requirements
Efficient analysis with better scalability and portability
Raw signals retain more information than just bases
Analyzing Raw Nanopore Signals

## Slide 117: The Problem – Mapping Raw Signals
Raw Signal
Small Reference Genome
Large Reference Genome (Human)
Fewer candidate regions in small genomes
Accurate mapping
High throughput
Substantially larger number of regions to check per read as the genome size increases
Problem: Probabilistic mechanisms
on many regions  inaccurate mapping
Problem: Distance calculation
on many regions  reduced throughput

## Slide 118: RawHash – Key Idea
Raw Signal #1
Hash
0x01
Fast Match
Raw Signal #2
0x01
Hash
Distance Calculation
Challenge #2: Accurately finding as few similar regions as possible
Challenge #1: Generating the same hash value for similar enough signals
Key Observation: Identical nucleotides generate similar raw signals

## Slide 119: Reference-to-Event Conversion
K-mer model: Provides expected event values for each k-mer
  Preconstructed based on nanopore sequencer characteristics
Use the k-mer model to convert all k-mers of a reference genome to their expected event values
K-mer Model
(Lookup Table)
Reference Genome
GCTATTACC
GCTATT
TATTAC
CTATTA
ATTACC
k-mers ()
105.757390
103.170091
81.740642
101.082485
Normalize
2.21
1.15
-0.09
1.11
Expected Event Values
Normalized Event Values

## Slide 120: Enabling Analysis From Electrical Signals
K many nucleotides (k-mers) sequenced at a time
Event: A segment of the raw signal
  Corresponds to a particular k-mer
Observation: Event values generated after sequencing the same k-mer are similar in value (not necessarily the same)
Raw Nanopore Signal
Calculate
Means
Event Value
2.21
Normalize
ACTTGG
Segment
Event
pAmpere
Time
ACTTGG
k-mer

## Slide 121: Quantization -- RawHash

## Slide 122: Packing and Hashing
CTATTA
-0.09
1
1
0
0
1
TATTAC
ATTACC
1.15
1.11
Consecutive k-mers
Consecutive events
0
0
1
1
0
0
0
1
0
1
…
…
…
…
Quantize
Quantize
Pack
1
1
0
0
1
0
0
1
1
0
…
1
0
0
0
1
Hash
0x400D70A4
Hash value of consecutive events
Quantize

## Slide 123: The Sequence Until Mechanism
Problem:
  Unnecessary sequencing waste time, power and money
Key Idea:
  Dynamically decide if further sequencing of the entire sample is necessary to achieve high accuracy
  Stop sequencing early without sacrificing accuracy
Potential Benefits:
  Significant reduction in sequencing time and cost
Example real-time genome analysis use case:
  Relative abundance estimation

## Slide 124: The Sequence Until Mechanism
Key Steps:
  Continuously generate relative abundance estimation after every reads
  Keep the last estimation results
  Detect outliers in the results via cross-correlation of the recent results
  Absence of outliers indicates consistent results
  Further sequencing is likely to generate consistent results  Stop the sequencing
Reads Sequenced
Relative Abundance Estimation
Estimation #1
Relative Abundance Estimation
Reads Sequenced
Relative Abundance Estimation
Estimation #2
Reads Sequenced
Estimation #
…
…
…
Outlier?
Yes
Keep Sequencing
No
Stop Sequencing
Notes: Considering the relative abundance estimation use case, the Sequence Until mechanism works in several steps
[CLICK] We generate ongoing relative abundance estimations after every sequencing of 𝑛 reads.
[CLICK] We always retain the most recent 𝑡 estimation results.
[CLICK] The next step involves detecting any outliers in these results. This is achieved by performing a cross-correlation between the last 𝑡 results.
If we find no outliers, it indicates that we are consistently generating similar results. In other words, the recent sequencing of reads could not change the estimation result significantly.
[CLICK] In such a scenario, it is unlikely that further sequencing of reads will produce an outlier. Therefore, we can make the decision to stop the sequencing process.
This approach allows us to optimize the sequencing process by stopping it when no new significant information is likely to be gained.
[CLICK] If there is an outlier, we simply keep sequencing as new reads keep changing the results.

## Slide 125: Sequence Until – RawHash & UNCALLED

## Slide 126: Sequence Until – RawHash

## Slide 127: Presets

## Slide 128: Versions – RawHash

## Slide 129: Related Works
Basecalled real-time analysis
  ReadFish, ReadBouncer, RUBRIC: Basecalled read mapping
  SPUMONI, SPUMONI 2: Basecalled binary classification using r-index
  Coriolis: Basecalled metagenomics classification
  baseLess: k-mer calling for classification
Raw signal analysis without basecalling
  SquiggleNet, DeepSelectNet, RawMap: Target/non-target classification
  Sigmoni: Target/non-target classification using r-index
  UNCALLED, Sigmap, RawHash: Read mapping

## Slide 130: Adaptive Quantization

## Slide 131: Chaining Scores – RawHash vs RawHash2
RawHash Chaining
RawHash2 Chaining

## Slide 132: Datasets

## Slide 133: Accuracy

## Slide 134: Mapping Accuracy – Radar

## Slide 135: Mapping Accuracy – All Metrics

## Slide 136: Combined Benefits – Radar

## Slide 137: Sequenced Length

## Slide 138: Computational Resources #1

## Slide 139: Computational Resources #2

## Slide 140: Average Time Spent per Read

## Slide 141: FAST5 vs. POD5. vs S/BLOW5

## Slide 142: Flow Cell Types R9 vs R10.4

## Slide 143: Ratio of Filtered Seed Hits

## Slide 144: Presets

## Slide 145: Versions

## Slide 146: Indexing using Raw Signals
Constructing the hash table index from raw nanopore signals
  Reference-to-signal conversion is mainly free from noise (e.g., stay errors)
  Indexed raw nanopore signals are not free from noise
Aggressively filtering consecutive and similar signals to substantially reduce noise at the cost of data loss
Aggressive Filtering
2.21
2.12
2.35
-0.9
-1.05
-0.85
-0.89
-1.01
1.15
1.25
1.20
2.21
2.12
2.35
-0.9
-1.05
-0.85
-0.89
-1.01
1.15
1.25
1.20
Raw Nanopore Signals

## Slide 147: Chaining and Outputting Overlaps
Adjusting the minimum chaining score to avoid false chains
  All-vs-all overlapping tends to find a larger number of seed hits than mapping to a reference genome
  Minimum score for a chain during overlapping is set to be ~5× larger than mapping
  All such chains are reported (instead of a single best mapping)
Avoid cyclic overlaps with deterministic comparisons
Target
Query
Target
Query

## Slide 148: Low-Coverage Human Genome Assembly
Results are shown relative to the best result from each metric
  Metrics: auN, longest unitig, largest connected unitigs (component)
  Coverage: 0.6x
auN
Longest unitig
Largest component
Minimap2
Rawsamble
Flye
Rawsamble leads to better contiguity than using basecalled reads at a low coverage dataset
Can the richer information in raw signals improve assembly quality where basecalled analysis falls short?

## Slide 149: Datasets

## Slide 150: Throughput

## Slide 151: Performance

## Slide 152: Overlapping Statistics

## Slide 153: Assembly Statistics

## Slide 154: Visualizing the E. coli Assembly Graph

## Slide 155: Visualizing the Yeast Assembly Graph

## Slide 156: Visualizing the Green Algae Assembly Graph

## Slide 157: Visualizing the Human Assembly Graph

## Slide 158: HERRO Correction Before and After

## Slide 159: Parameters

## Slide 160: Presets

## Slide 161: Versions

## Slide 162: Utilizing Probabilities in pHMMs
The Baum-Welch algorithm is commonly used with pHMMs
  For both inference and training by effectively utilizing the probabilities
Inference: Identifying the variations between sequences
Training: Maximizing parameters to observe certain variations
Forward Calculations
Backward Calculations
Updating Transition Probabilities
Updating Emission Probabilities
Training Step

## Slide 163: Forward & Backward Calculations
A dynamic programming approach
  Calculate the ‘possibility’ of visiting each state in a pHMM
  Given an observed sequence (from both directions of the sequence)
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T

## Slide 164: Inference using pHMMs
Goal: Identifying the variations between sequences
  Inference by using decoding algorithms (e.g., the Viterbi Algorithm)
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
A
C
T
T
D
G
Inference:

## Slide 165: Training using pHMMs
Goal: Maximizing parameters to observe certain variations
  Training using the parameter updating steps in the Baum-Welch algorithm
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
Training

## Slide 166: SW: Minimizing Redundant Storage
Observation: Filling the entire Backward table is unnecessary
  Pipelining opportunities to directly consume a Backward value
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
Training
✓
Needed
No need

## Slide 167: SW: Minimizing Redundant Storage
Observation: Filling the entire Backward table is unnecessary
  Pipelining opportunities to directly consume a Backward value
  Partial compute approach: Only a single row should be fully stored
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
Training

## Slide 168: SW: Minimizing Redundant Storage
Observation: Filling the entire Backward table is unnecessary
  Pipelining opportunities to directly consume a Backward value
  Partial compute approach: Only a single row should be fully stored
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
Training

## Slide 169: SW: Minimizing Redundant Storage
Observation: Filling the entire Backward table is unnecessary
  Pipelining opportunities to directly consume a Backward value
  Partial compute approach: Only a single row should be fully stored
  Reduces the storage requirements during training
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
Training

## Slide 170: SW: Reducing Unnecessary Computations
Observation: ‘Negligible’ cells can be ignored without significantly reducing overall accuracy
  Filtering: Non-negligible states are identified by sorting
  Sorting to find exactly states with largest Forward or Backward values
Sorting is complex to implement in hardware (and costly)
  Can we filter without sorting?
A
T
G
T
Forward Calculations
A
D
I
D
C
I
D
T
I
Filtered Forward Calculations
A
D
I
D
C
I
D
T
I
A
T
G
T
Filter by sorting

## Slide 171: SW: Reducing Unnecessary Computations
Observation: ‘Negligible’ cells can be ignored without significantly reducing overall accuracy
  Goal: Find at least states with largest Forward and Backward values
  Histogram-based filtering: Placing the states into buckets corresponding to a range of values
  Filter is full as soon we find at least states (e.g., )
Filter is full
Histogram Filter
.
.
.
8, 9
10, 14
15, 16, 18
11, 20, 21, …
13, 17, 19, …
States
Range
1.00 – 0.94
0.94 – 0.88
0.88 – 0.82
0.82 – 0.76
0.76 – 0.70
0.06 – 0.00
.
.
.
The rest is ignored from further calculation
Filter size = 2 < 10
Filter size = 4 < 10
Filter size = 7 < 10
Filter size = 13 > 10

## Slide 172: SW: Avoiding Repeated Operations
Observation: Same multiplications are redundantly performed
  Same default values are used for each possible connection in pHMMs
  Fixed connection patterns generate a fixed set of multiplication results
Goal: Avoid redundant computations
  By enabling efficient reuse of the common multiplications results
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
A
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
T
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
T
…
…
Costly FP Operations
Same output

## Slide 173: SW: Avoiding Repeated Operations
Observation: Same multiplications are redundantly performed
  Same default values are used for each possible connection in pHMMs
  Fixed connection patterns generate a fixed set of multiplication results
Goal: Avoid redundant computations
  By enabling efficient reuse of the common multiplications results
  Lookup tables (LUTs) to efficiently store and use these common results
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
A
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
T
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
T
…
…
Cheap LUTs
Same output

## Slide 174: Overview of ApHMM Design
ApHMM Core
Compute Block
Control Block
LUT
Transition Scratchpad
Histogram
Filter
Data Control
Parameters
Index Control
Calculate Backward (Step-by-Step)
Memory (DRAM/L2/L1)
CPU
Calculate Forward (Full)
Flexible and efficient control logic & hardware design
✓
Update Emission Probabilities
(Step-by-Step)
Update Transition Probabilities
(Step-by-Step)

## Slide 175: Evaluation Methodology
Comparison Points
  CPU: Apollo, HMMER
  GPU: ApHMM-GPU, HMM_cuda
  FPGA: FPGA D&C
Datasets
  Error correction: Real 10,000 DNA sequences from Escherichia coli (E. coli) with average 5,128 read length
  Protein family search: Entire Pfam database (19,632 pHMMs) and real 214,393 protein sequences from Mitochondrial carrier
  Multiple sequence alignment: Aligning over ~1 million protein sequences from Pfam database

## Slide 176: Performance: Workload Acceleration
Up to 60 (CPU-1), 1.75 (GPU), and 1.95 (FPGA) faster execution of the end-to-end applications
Error correction benefits most from the acceleration due to frequent and costly training

## Slide 177: More in the Paper
More results
  Detailed discussion on the results generated per use case
  Justification of the dataset and baseline choices
Details of all mechanisms and configurations
  Details of our design space exploration
  Data distribution and memory layout
  Control and execution flow of ApHMM cores
  Related work discussion (e.g., Pair HMMs vs pHMMs)
  Detailed background on the equations and algorithms

## Slide 178: Filtering – Performance Benefits
Filtering heuristics aim to reduce unnecessary computations
Motivational Study: ~2.5x performance improvements with filtering

## Slide 179: Filtering – Accurate but Costly Sorting
Software-based filtering heuristics aim to reduce unnecessary computations
  High-accuracy can be achieved with filtering with correct setting
Filtering takes up ~8.5% of the overall execution time due to sorting

## Slide 180: Choosing the Right Amount of Cores
We analyze maximum number of cores that ApHMM can utilize
  Before it is bottlenecked by memory bandwidth for genomics applications
ApHMM with 4 cores (ApHMM-4) provides the best overall speedup