## Slide 1
Lost in Translation: Harnessing the Power of Nanopore Electrical Signals in Genomics
Can Firtina | canfirtina@gmail.com | cs.umd.edu/~firtina
Assistant Professor of Computer Science at UMD
IMET Seminar Series, UMBC, MD, USA
February 18, 2026

## Slide 2: Big Data is Everywhere
Large recommender systems
Large Language Models
Graph/Tree Processing
Genomics

## Slide 3: Computing is Bottlenecked by Data
Large recommender systems
Large Language Models
Graph/Tree Processing
Genomics
Data movement → Performance & Energy Bottleneck

## Slide 4: Problems with Data Analysis Today
Special-Purpose Machine
for Data Generation
FAST
General-Purpose Machine
for Data Analysis
SLOW
Processing capabilities oblivious to data analysis requirements
Large amounts of data movement

## Slide 5: A Typical (Biological) Data Analysis
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Costly Operations
Data Movement from Storage
Storage
System
Overall Time/Energy Spent
Data Movement Overhead
Computation Overhead

## Slide 6: A Typical Accelerated (Biological) Data Analysis
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Storage
System
Heuristics
Accelerators
Filters
Computation Overhead
✓
Computation Overhead

## Slide 7: Acceleration Efforts for AI and Genomics
Google’s TPUs:
Cerebras WSE-3 Wafer-scale ML accelerator chip
NVIDIA H100

## Slide 8: Accelerated Computing is Mainstream Now
https://blogs.nvidia.com/blog/accelerated-scientific-systems/?linkId=100000392637737

## Slide 9: Data Movement Dominates Performance
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Storage
System
Heuristics
Accelerators
Filters
Computation Overhead
✓
Data Movement Overhead
Overall Time/Energy Spent

## Slide 10: We need to co-design algorithms and architecture to handle data well

## Slide 11: Pushing Towards New Architectures
GPUs
Heterogeneous
Processors &
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
FPGAs
Modern systems
?
Sequencing Machine

## Slide 12: Recommended: Accelerating Genome Analysis [DAC '23]
Onur Mutlu and Can Firtina, "Invited: Accelerating Genome Analysis via Algorithm-Architecture Co-Design" Proceedings of the 60th Design Automation Conference (DAC 2023), San Francisco, CA, USA, July 2023. Paper [online] [pdf]

## Slide 13: Analyzing Genomes Reveals Key Insights
Detecting pathogens in the environment
Rapid surveillance of disease outbreaks
Genome Editing
Personalized Medicine

## Slide 14: Generating the Entire Genomic Sequence
Whole Genome: 6.4B bps
(Non-human-readable)
CGAAATGCC...AGATTAAACGCT...TGCCCTAA...GAATGGCGT
Whole Human Genome: 6.4B bps (Human-readable)
Raw Genomic Data (Human-readable?)
Sequencing Device
Translator (Basecalling)
AI

## Slide 15: Genomic Data: Giant Jigsaw Puzzle to Solve
CGAAATGCC...AGATTAAACGCT...TGCCCTAA...GAATGGCGT
Human (Reference) Genome: 3.2 Billion bps (haploid)
Unknown origins
?
Non-identical reference genome
Small pieces (reads)
Large volume of data to analyze
AAATGG
Read: ~100 – 100,000 bps
?
Scale: ~
CGAAATGCC...AGATTAAATGGT...TGCCCTAA...GAATGGCGT
Entire Genomic Sequence of an Organism
Dealing with Massive and Noisy Datasets (TBs to PBs)

## Slide 16: Solving the Puzzle: The Practical Way
CGAAATGCC...AGATTAAACGCT...TGCCCTAA...GAATGGCGT
Performing the costly computations only for a few regions
Goal: Quickly and accurately reduce the search space
Read Mapping
Hash
0x01
Indexing
Hash Table
0x00
0x01
0xFF
…
Hash
Positions
2,64,…
13,21
1,101,…
Sketching
Reference Genome
Store
Query
Chaining
Hash Matches
Seeding
Hash
0x00
Sketching
Read
Alignment
DP Calculations
AAATGG
AAATGG
AAATGG
Exact Match
AAA
AAA
CTA
AAT
AAA

## Slide 17: A Common Genome Analysis Pipeline
Assembly
Variant Calling
Metagenomics
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Downstream Analysis
Raw Reads
Read Mapping
Basecalling (Translator)
AAATGTGGTCCATTG
Basecalled (Translated) Reads

## Slide 18: Genome Analysis is Energy Inefficient
Raw Reads
Read Mapping
Basecalling (Translator)
AAATGTGGTCCATTG
Basecalled (Translated) Reads
- Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS 2018
- Kestor et al., “Quantifying the Energy Cost of Data Movement in Scientific Applications,” IISWC 2013
- Pandiyan and Wu, “Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms,” IISWC 2014
Single memory request consumes >160 - 800 more energy compared to performing an addition operation
Costly and large volumes of data movement
Power-Hungry Devices

## Slide 19: Genome Analysis is Computationally Costly
Chart: Runtime (Hour)
| Basecalling + Read Mapping | Assembly
Heterogeneous System (with CPUs and GPUs) | 16 | 1.5
Significant computational overhead

## Slide 20: Genome Analysis Pipeline is Unbalanced
Alser+, “From molecules to genomic variations: Accelerating genome analysis via intelligent algorithms and architectures,” CSBJ 2022

## Slide 21: Limited Application Scope and Accuracy
Energy-efficient analysis for Resource-constrained devices
Urgent analysis within minutes
Large-scale analysis without sacrificing accuracy and performance

## Slide 22: STORM Research Group
Real-Time and Portable Genomic Signal Analysis
Data-centric and AI-Driven Solutions to Analyze Genomic Data
Accurate and Fast Algorithms Scalable to Large Volumes of Genomic Data
Research Directions
Enable fundamentally better integration of biological data analysis in our everyday lives
Goal
Today’s Talk

## Slide 23: New Frontiers: Raw Signal Analysis [ISMB '23]
Can Firtina, Nika Mansouri Ghiasi, Joel Lindegger, Gagandeep Singh, Meryem Banu Cavlak, Haiyu Mao, and Onur Mutlu, "RawHash: enabling fast and accurate real-time analysis of raw nanopore signals for large genomes" Proceedings of the 31st Annual Conference on Intelligent Systems for Molecular Biology (ISMB 2023) and the 22nd European Conference on Computational Biology (ECCB 2023), Lyon, France, July 2023. Paper [online] [pdf] [code] Conference Talk [video] [pptx] [pdf] Preprint (bioRxiv) [online] [pdf] Social Media Thread [Twitter (X)]

## Slide 24: Real-Time Raw Signal Analysis [Bioinformatics '24]
Can Firtina, Melina Soysal, Joël Lindegger, and Onur Mutlu, "RawHash2: Mapping Raw Nanopore Signals Using Hash-Based Seeding and Adaptive Quantization" Bioinformatics, July 2024. Paper [online] [pdf] [code]

## Slide 25: New Directions: Assembling Raw Signals
Can Firtina, Maximilian Mordig, Harun Mustafa, Sayan Goswami, Nika Mansouri Ghiasi, Stefano Mercogliano, Furkan Eris, Joel Lindegger, Andre Kahles, and Onur Mutlu, "Rawsamble: Overlapping and Assembling Raw Nanopore Signals using a Hash-based Seeding Mechanism" [Accepted to Bioinformatics] arXiv, October 2024. Paper [online] [pdf] [code] ISMB 2024 Talk [video] [pptx] [pdf] CSHL 2024 (Biological Data Science) Talk [video] [pptx] [pdf] Social Media Thread [Twitter (X)] [LinkedIn]

## Slide 26: Quickly Aligning Raw Signals [IEEE Access '24]
Joël Lindegger, Can Firtina, Nika Mansouri Ghiasi, Mohammad Sadrosadati, Mohammed Alser, and Onur Mutlu, "RawAlign: Accurate, Fast, and Scalable Raw Nanopore Signal Mapping via Combining Seeding and Alignment" IEEE Access, December 2024. Paper [online] [pdf] [code]

## Slide 27: Benchmarking Raw Signal Analysis [ACM-BCB '25]
Furkan Eris, Ulysse McConnell, Can Firtina, and Onur Mutlu, "RawBench: A Comprehensive Benchmarking Framework for Raw Nanopore Signal Analysis Techniques" Proceedings of the 16th ACM Conference on Bioinformatics, Computational Biology, and Health Informatics (ACM-BCB 2025), Philadelphia, PA, USA, October 2025. Paper [online] [pdf] Conference Talk [pptx] [pdf]

## Slide 28: Basecalling is Accurate yet Costly
Raw Reads
Read Mapping
Basecalling (Translator)
Costly
AI Models
AAATGTGGTCCATTG
Basecalled Reads
Highly accurate reads
Noisy Raw Signals
Significant computation and energy overhead
How to make this pipeline cheaper?

## Slide 29: Can We Survive Without Translation?
Raw Reads
Read Mapping
Reference Genome
CTGCGTAGCAGCGTAATAG
...
...
How to communicate without an accurate translator?
Noisy Raw Signals

## Slide 30: Can We Survive With Noisy Signal Analysis?
Raw Reads
Read Mapping
Reference Genome
CTGCGTAGCAGCGTAATAG
...
...
-0.06,0.24,-0.74,
...
...
Reference-to-Signal Conversion
Raw Signal Analysis
How to identify similarity between noisy signals?
Noisy Raw Signals

## Slide 31: Noise in Raw Electrical Signals
Key Idea: Perform similarity estimation based on vector similarity search
[ , , , , ]
-0.22
0.96
-0.75
-0.06
-0.49
Raw Signals:
-0.21
1.01
-0.76
-0.05
-0.51
Raw Signals:
Problem: Too Costly for Large Genomes
[ , , , , ]
Sequencing CTGCGTAGCA
Sequencing CTGCGTAGCA
Nearest Neighbor Search
Observation: Identical molecules generate similar raw signals

## Slide 32: Scalability Issues Limit Real-Time Analysis
Genome Size Increase: 150
2.4
9.2
28
No Real-Time Analysis for Larger Genomes: Searching mechanism does not scale well

## Slide 33: Benefits of Real-Time Analysis
Sequencing
Analysis
Time
Reducing sequencing time and cost by stopping sequencing early
✓
Reducing latency by overlapping analysis with sequencing
✓
Completely Sequenced Read
Sequenced Bases
Sequencing & Real-Time Analysis
Reduced Latency
Partially Sequenced Read
Sequencing is stopped early with a real-time decision
Reduced Sequencing Time (and Cost)

## Slide 34: RawHash’s Goal
Enable Fast, Accurate, and Scalable Real-Time Analysis for Larger Genomes

## Slide 35: RawHash’s Key Idea
[ , , , , ]
-0.22
0.96
-0.75
-0.06
-0.49
Raw Signals:
-0.21
1.01
-0.76
-0.05
-0.51
Raw Signals:
Key Idea: Perform similarity estimation based on quick exact matches
Challenge: How to generate the same hash value for similar enough signals with various noise types?
Hash
Hash
0x77db
0x77db
Fast Match
CTGCGT
[ , , , , ]

## Slide 36: RawHash’s Key Idea – Quantization
Range of raw signals (normalized)
-3.00
+3.00
0
1
2
3
4
5
6
7
8
9
14
15
10
11
12
13
Bucket #
CTGCGT
-0.06
-0.07
-0.05
-0.05
-0.06
Enables matching raw signals by eliminating slight differences
✓
Quantize
Quantize
Quantize
Quantize
Quantize

## Slide 37: How to Better Quantize Signals
Range of raw signals (normalized)
-3.00
+3.00
0
1
2
3
4
5
6
7
8
9
14
15
10
11
12
13
Bucket #
Equal-width buckets leads to unbalanced bucket loading
✕
Reduced uniqueness and poor resource utilization
✕
-3.00
+3.00
200
400
600
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
K-mer count

## Slide 38: Adaptive Quantization
Key Idea: Quantizing raw signals with non-equal bucket widths by leveraging raw signal distribution
-3.00
3.00
K-mer count
Better bucket utilization
✓
Range of raw signals (normalized)
-3.00
+3.00
0
1
2
3
4
5
6
7
8
9
14
15
10
11
12
13
Bucket #

## Slide 39: RawHash Key Idea – Hash-based Matching
Sequencing CTGCGTAGCA
-0.22
0.96
-0.75
-0.06
-0.49
Hash
0x77db
Fast and Accurate Match
[ , , , , ]
Key Contribution: The first hash-based search (and indexing) mechanism for raw signals
Quantize
0b0111
Quantize
0b0111
Quantize
0b0110
Quantize
0b1011
Quantize
0b0110
Pack
0b01110111011010110110
Hash
0x77db

## Slide 40: Real-Time Analysis Benefits from Fast Search
Genome Size Increase: 150
2.4
9.2
28
Real-time Analysis for Human Genomes: Fast search instead of costly neighbor search

## Slide 41: Fast Search Leads to Accurate Search
Best accuracy for all genomes: Hash values span longer sequences than vectors -> More unique and informative matches
(Almost) Identical accuracy to basecalled analysis:
Is the small difference because RawHash is even better?

## Slide 42: RawHash is Open Source
https://github.com/CMU-SAFARI/RawHash

## Slide 43
So What?

## Slide 44: New Directions: Assembling Raw Signals
Can Firtina, Maximilian Mordig, Harun Mustafa, Sayan Goswami, Nika Mansouri Ghiasi, Stefano Mercogliano, Furkan Eris, Joel Lindegger, Andre Kahles, and Onur Mutlu, "Rawsamble: Overlapping and Assembling Raw Nanopore Signals using a Hash-based Seeding Mechanism" [Accepted to Bioinformatics] arXiv, October 2024. Paper [online] [pdf] [code] ISMB 2024 Talk [video] [pptx] [pdf] CSHL 2024 (Biological Data Science) Talk [video] [pptx] [pdf] Social Media Thread [Twitter (X)] [LinkedIn]

## Slide 45: Beyond Reference Mapping: Overlapping
TGCTGCAATCGTGATCCGAAGTCAGCCGTAGTGGACCACCGGTAAGCT
TGCTGCAA
CTGCAATC
TGATCCGA
CGAAGTCA
TCAGCCGT
CGTAGTGG
AGTGGACC
CCACCGGT
GGTAAGCT
Raw Nanopore Signals
Hash-Based Seeding and Mapping
Raw Nanopore Signals
Reference Signals
Reference Genome (Converted to Signals)
Challenge: Reference genome is not always available
Assembly: Constructing genome from overlapping reads
Existing solutions cannot find overlapping reads without basecalling
✕

## Slide 46
The first mechanism that can perform all-vs-all overlapping from raw signals
Rawsamble

## Slide 47: Eliminating Basecalling from the Pipeline
Basecalling (CPU) + Overlapping
Rawsamble
Basecalling (GPU) + Overlapping
SARS-CoV-2
E. coli
Yeast
Green Algae
Human
Geo. Mean
Elapsed Time (Normalized to Rawsamble)
Average speedup of 60 than CPU-based basecalling: Eliminating basecalling leaves a significant room for performance improvements
Average speedup of 2 than the GPU-based basecalling: GPU vs. GPU comparison is likely to provide even better results
59.70
1.99

## Slide 48: Key Results – First Ever Assemblies
First assemblies ever constructed without basecalling
~400 longer assembled pieces than the average read length: Informative overlaps lead to longer paths
It is time to rethink if we want to translate individual reads separately
E. coli Assembly (From the Rawsamble Overlaps)

## Slide 49: Quickly Aligning Raw Signals [IEEE Access '24]
Joël Lindegger, Can Firtina, Nika Mansouri Ghiasi, Mohammad Sadrosadati, Mohammed Alser, and Onur Mutlu, "RawAlign: Accurate, Fast, and Scalable Raw Nanopore Signal Mapping via Combining Seeding and Alignment" IEEE Access, December 2024. Paper [online] [pdf] [code]

## Slide 50: RawAlign Overview
Coarse-Grained
Fast
Fine-Grained
Accurate

## Slide 51: Benchmarking Raw Signal Analysis [ACM-BCB '25]
Furkan Eris, Ulysse McConnell, Can Firtina, and Onur Mutlu, "RawBench: A Comprehensive Benchmarking Framework for Raw Nanopore Signal Analysis Techniques" Proceedings of the 16th ACM Conference on Bioinformatics, Computational Biology, and Health Informatics (ACM-BCB 2025), Philadelphia, PA, USA, October 2025. Paper [online] [pdf] Conference Talk [pptx] [pdf]

## Slide 52: RawBench Benchmarking Framework
Encoding Reference Genome
  Uses learned pore models by ONT and community
Encoding Raw Signal
  Utilizes statistical and ML-based encoding techniques
Matching Encoded Representations
  Compares representations that are now encoded into the same space
1
2
3
1
Encoding reference genome
ONT pore model
Uncalled4 pore model
Add-on
t-test
Move tables
Add-on
Hash-based
FM-index
Vector distance
R-index
DTW
Add-on
Encoding raw signal
2
Matching encoded representations
3
Input Reference
ACGT
Input Raw Signals

## Slide 53: In-Storage Raw Signal Analysis [ICS '25]
Melina Soysal, Konstantina Koliogeorgi, Can Firtina, Nika Mansouri Ghiasi, Rakesh Nadig, Haiyu Mao, Geraldo Francisco Oliveira Junior, Yu Liang, Klea Zambaku, Mohammad Sadrosadati, and Onur Mutlu, "MARS: Processing-In-Memory Acceleration of Raw Signal Genome Analysis Inside the Storage Subsystem" Proceedings of the 39th International Conference on Supercomputing (ICS 2025), Salt Lake City, Utah, USA, June 2025. Paper [online] [pdf] Conference Talk [video] [pptx] [pdf]

## Slide 54: Read Mapping with Raw Signals
High Level Overview of Read Mapping in Raw Signal Genome Analysis (RSGA)
EVENT DETECTION
SEEDING
hash and query
CHAINING
sorting and DP-based
query
0x00
Mapping (online)
Query Sequence
events
Sketching
Hash
Chaining
matches
x
x
x
Hash Table
0x00
0x01
0xFF
…
Hash
Positions
13,21
1,101,…
2,64,…
I
II
III
chains

## Slide 55: Motivation
Chart: 
| D5 | D4 | D3 | D2 | D1
I/O | 0.44693 | 2.8113 | 14.2983 | 24.4228 | 40.8487
Event detection | 0.32219 | 0.78842 | 6.8819 | 15.2129 | 20.4808
Seeding | 4.3277 | 5.0721 | 8.0838 | 9.3213 | 5.1415
Chaining | 94.8976 | 91.312 | 70.5813 | 50.736 | 33.1082
Chaining & seeding consistently dominate runtime
Event detection & I/O overhead are non-negligible for some datasets

## Slide 56: Impact of I/O data movement
We model I/O data movement overhead when accelerating commonly targeted steps in the pipeline: seeding and chaining
Chart: Latency reduction of seeding and chaining %
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
D1 | 40.8487 | 42.4733 | 44.2325 | 46.1437 | 48.2275 | 50.5084 | 53.0158 | 55.7851 | 58.8597 | 62.2929 | 66.1515
D2 | 24.4228 | 25.9832 | 27.7567 | 29.7901 | 32.1449 | 34.9039 | 38.1811 | 42.1373 | 47.0083 | 53.1525 | 61.1445
D3 | 14.2983 | 15.5191 | 16.9678 | 18.7149 | 20.8631 | 23.5683 | 27.0796 | 31.8203 | 38.5732 | 48.9643 | 67.0182
D4 | 2.8113 | 3.1112 | 3.4827 | 3.9549 | 4.5753 | 5.4265 | 6.6668 | 8.642 | 12.2805 | 21.2107 | 77.7485
D5 | 0.44693 | 0.49616 | 0.55758 | 0.63636 | 0.74106 | 0.88699 | 1.1045 | 1.4633 | 2.1675 | 4.178 | 57.6885
I/O data movement from SSD becomes dominant overhead as compute steps are accelerated in RSGA
As compute latency is reduced, I/O becomes the dominant contributor to total execution time

## Slide 57: MARS Architecture & System - Overview
In-Storage-Processing system for RSGA
Conventional Mode: SSD performs standard SSD storage operations
Accelerator Mode: SSD executes the full RSGA pipeline without host intervention
SSD Controller
SSD-Internal DRAM
Cores
FTL
Flash Controller
…
Bank
Bank
…
Subarrays
.
Merger
Unit
III
…
…
Arithmetic Unit
…
Querying Unit
…
Querying Unit
V
V
.
.
…
MARS
Control
Unit
I
Sorter
Unit
II
Arithmetic Unit
IV
Flash Memory

## Slide 58: MARS Architecture & System (I/IV)
SSD Controller Components
MARS Control Unit
Finite State Machine that orchestrates pipeline execution, control and data flow
I
SSD Controller
Flash Memory
Cores
FTL
Flash Controller
Merger
Unit
III
Sorter
Unit
II
.
.
.
MARS
Control
Unit
I

## Slide 59: MARS Architecture & System (II/IV)
SSD Controller Components
MARS Control Unit
Finite State Machine that orchestrates pipeline execution, control and data flow
I
Merger Unit
Combines sorted subsequences into longer sorted ones
Sorter Unit
Performs parallel sorting of sequences using dedicated logic
II
III
SSD Controller
Flash Memory
Cores
FTL
Flash Controller
.
.
.
MARS
Control
Unit
I
Merger
Unit
III
Sorter
Unit
II
Paradigm: Implements Processing Near DRAM
1 Sorter-Merger pair per flash controller

## Slide 60: MARS Architecture & System (III/IV)
SSD-Internal DRAM Components
SSD-Internal DRAM
…
Bank
Bank
…
Subarrays
…
…
…
…
…
Querying Unit
V
Querying Unit
V
Arithmetic Unit
IV
Arithmetic Unit
Paradigm: Implements Processing Near DRAM
IV
Performs arithmetic and logical operations required for RSGA
Design: Based on the FULCRUM1 architecture for leveraging DRAM subarray proximity for low-latency parallel arithmetic operations
1 per two subarrays
1: [Lenjani, HPCA’20];

## Slide 61: MARS Architecture & System (IV/IV)
SSD-Internal DRAM Components
SSD-Internal DRAM
…
Bank
Bank
…
Subarrays
…
…
…
…
…
Querying Unit
V
Querying Unit
V
Arithmetic Unit
IV
Querying Unit
Paradigm: Implements Processing Using DRAM
V
Performs efficient, in-memory hash table lookups for seeding
Design: Based on the PLUTO2 architecture leveraging DRAM row activation for massively parallel hash-table lookup operations
1 per subarray
1: [Lenjani, HPCA’20]; 2: [Ferreira+, MICRO’22]
Arithmetic Unit
Paradigm: Implements Processing Near DRAM
IV
Performs arithmetic and logical operations required for RSGA
Design: Based on the FULCRUM1 architecture for leveraging DRAM subarray proximity for low-latency parallel arithmetic operations
1 per two subarrays

## Slide 62: Performance Evaluation
Key Observations
Chart: 
| D1 | D2 | D3 | D4 | D5 | GEOMEAN
BC | 0.01 | 0.6 | 0.1 | 0.70385 | 4.7 | 0.2881
GenPIP | 0.02 | 1.5 | 0.2 | 1.9 | 12.7 | 0.7
MARS-CPU2 | 1 | 1 | 1.2 | 10.2 | 1.2 | 1.7
RawGains-FULCRUM | 84.3 | 17.4 | 8 | 44.5 | 32 | 27.8
RawHash2
MARS
1
10
100
D1
D2
D3
D4
D5
GEOMEAN
0.1
BC
MS-CPU
GenPIP
Speedup
MARS outperforms all other baselines across all datasets
MARS outperforms GenPIP adopting PIM outside storage
MARS-CPU provide speedup of 1.7x over RH2
We fundamentally solve the I/O data movement overhead problem
Our SW modifications are effective in reducing the computational load
Basecalling-based pipeline
RSGA-based pipeline

## Slide 63: Energy Evaluation
1
10
102
0.1
Energy Reduction
Chart: 
| D1 | D2 | D3 | D4 | D5 | GEOMEAN
BC | 0.01 | 0.8 | 0.3 | 0.70385 | 0.3 | 0.2
GenPIP | 0.07 | 5.6 | 2.1 | 3.1 | 1.3 | 2.5
MARS-CPU | 1.1 | 2.1 | 4 | 7.2 | 1.2 | 3.12
MARS | 217.1 | 103.9 | 211.8 | 295.9 | 68.5 | 179.4
D1
D2
D3
D4
D5
GEOMEAN
RawHash2
MARS
BC
MS-CPU
GenPIP
Key Observation
MARS reduces energy consumption over all other baselines across all datasets
Improvement stems from
reduced execution time
fundamentally addressing the I/O data movement overhead
Basecalling-based pipeline
RSGA-based pipeline

## Slide 64
Processing Data Where It Makes Sense Provides Significant Performance and Energy Benefits

## Slide 65: Some Interesting Challenges in Signal Analysis
Identifying novel base modifications in various organisms
Better integrating the chemical structure information in genomics
  Distinguishing noise from useful information
Redesigning effective solutions for storage
Enabling end-to-end and energy-efficient analysis with (portable) sequencing devices

## Slide 66: STORM Research Group
Real-Time and Portable Genomic Signal Analysis
Data-centric and AI-Driven Solutions to Analyze Genomic Data
Accurate and Fast Algorithms Scalable to Large Volumes of Genomic Data
Research Directions
Enable fundamentally better integration of biological data analysis in our everyday lives
Goal
Today’s Talk

## Slide 67
Lost in Translation: Harnessing the Power of Nanopore Electrical Signals in Genomics
Can Firtina | canfirtina@gmail.com | cs.umd.edu/~firtina
Assistant Professor of Computer Science at UMD
IMET Seminar Series, UMBC, MD, USA
February 18, 2026

## Slide 68: Backup Slides

## Slide 69: Generating Electrical Signals from DNA
Nanopore Sequencer
Single Nanopore
Raw Signals
(~5000 signals/sec)
https://nanoporetech.com/platform/technology/basecalling
Real-Time Analysis
https://blogs.ed.ac.uk/institute-genetics-cancer/2020/04/08/nanopore-sequencing-controversial-world-records-and-whale-watching/

## Slide 70: Basecalling using PIM [MICRO '23]
Taha Shahroodi, Gagandeep Singh, Mahdi Zahedi, Haiyu Mao, Joel Lindegger, Can Firtina, Stephan Wong, Onur Mutlu, and Said Hamdioui, "Swordfish: A Framework for Evaluating Deep Neural Network-based Basecalling using Computation-In-Memory with Non-Ideal Memristors" Proceedings of the 56th International Symposium on Microarchitecture (MICRO), Toronto, ON, Canada, November 2023. [Slides (pptx) (pdf)] [arXiv version]

## Slide 71: DNN Hardware Acceleration
DNN execution is dominated by:
Memristor-based crossbars support VMM
Vector-Matrix Multiplication (VMM)
Data movement between memory and accelerator
(e.g., GPU or TPU)
Processing in Memory (PIM) minimizes data movement
Memristor-based PIM for DNN Acceleration
  [Ankit+, ASPLOS 2019], [Chi+, ISCA 2016], [Lou+, PACT2020], [Shafiee+, ISCA 2016]

## Slide 72: VMM in Memristor-based Crossbars
Digital to Analog Converters
Analog to Digital Converters

## Slide 73: Non-idealities in Memristor-based Crossbars
Digital to Analog Converters
Analog to Digital Converters
Non-ideal DAC
Variation in
Synaptic Conductance
Wire Resistance
Non-ideal ADC
Subpar utilization of trained models due to non-idealities

## Slide 74: Accuracy: All Non-idealities without Mitigation
Non-idealities
Accuracy (%)
D1
D2
Baseline
Baseline
Combined non-idealities leads to significant accuracy loss (>18%)

## Slide 75: Accuracy: Enhancement Techniques on All Non-idealities
D1
Accuracy (%)
Baseline
Baseline
D3
Accuracy loss drops to 6% from 18% after handling all non-idealities
Enhancement Technique

## Slide 76: ML-based Genome Analysis via PIM [MICRO '22]
Haiyu Mao, Mohammed Alser, Mohammad Sadrosadati, Can Firtina, Akanksha Baranwal, Damla Senol Cali, Aditya Manglik, Nour Almadhoun Alserr, and Onur Mutlu, "GenPIP: In-Memory Acceleration of Genome Analysis via Tight Integration of Basecalling and Read Mapping" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (25 minutes)] [arXiv version]

## Slide 77: Problem 1: Large Data Movement
Raw Signals
Basecalling
Reads
Read quality
control
High-quality
reads
Read
mapping
Mapped
reads
Large data movement between genome analysis steps
3913 GB
546 GB
437 GB
382 GB
[NC'19] Rory Bowden, Robert W Davies, Andreas Heger, Alistair T Pagnamenta, Mariateresa de Cesare, Laura E Oikkonen, Duncan Parkes, Colin Freeman, Fatima Dhalla, Smita Y Patel, et al. Sequencing of human genomes with nanopore technology. Nature Communications, 2019.

## Slide 78: Problem 2: Wasted Computation
Raw Signals
Basecalling
Reads
Read quality
control
High-quality
reads
Read
mapping
Mapped
reads
Low-quality
reads
Unmapped
reads
A considerable amount of computation on useless data due to
Low-quality reads
Unmapped reads
100%
79.5%
69.5%
20.5%
10%

## Slide 79: Goal and Opportunities
Chart: Normalized Speedup
| System A | System B | System C
Normalized Speedup | 2.7 | 6.1 | 9
We perform a study to quantify potential performance benefits
Goal: Efficiently accelerate the entire genome analysis pipeline while minimizing data movement and useless computation
NVM-based PIM accelerators for separate basecalling and read mapping
no data movement
between the accelerators of analysis steps
no data movement
and
no useless reads
(ideal case)

## Slide 80: GenPIP Overview
GenPIP
Read Mapping Module
GenPIP Controller
Basecalling Module
eDRAM
In-memory
Read Mapping
[PARC, ASPDAC’20]
+ Our design
In-memory
Basecaller
[Helix, PACT’20]
PIM-CQS
PIM chunk quality score calculation
Raw signals from the sequencing machine
Signal
chunk
Base quality score
Chunk mapping score
To storage
Read mapping result
Average Calculator
ER
ER
Controller
Quality score
ER
Chunk
Read Mapping Controller
Basecalled
chunk
Chunk quality score
https://arxiv.org/pdf/2209.08600.pdf

## Slide 81: General-Purpose "Things"

## Slide 82: Algorithm Design Demands General-Purpose Computing
Function 2
Function 4
General-Purpose Systems
(e.g., CPUs)
Function 1
Function 3
Your Favorite Output
Your Favorite Algorithm
Paid Costs for Generality:
Supporting unnecessary operations
Inefficient data and control flow
Limited parallelism & bandwidth
High latency &
Substantial energy

## Slide 83: Great Algorithms Demand Specialization
Goal: Avoid wasting computation & energy
Opportunities: Better data flow with minimal latency & power
Everyone’s Favorite Algorithm
Function 2
Function 1
Function 3
Function 1
Function 2
Function 3
Application-Specific Architecture
Paid Costs for Specialization:
Poor programmability
High manufacturing and engineering costs
Efficient processors customized for the task
Better parallelism

## Slide 84: Acceleration Efforts for AI and Genomics
Google’s TPUs:
Cerebras WSE-3 The largest ML accelerator chip
NVIDIA H100

## Slide 85
Important and Commonly Used Applications Demand Specialization

## Slide 86: Probabilistic Graphs in Genomics
Probabilistic graphs are commonly used to identify variations between sequences
To avoid redundant comparisons and storage
To provide rich information
on expected variations
Reference Genome Graph

## Slide 87: Graph-Based Applications in Genomics
Protein
Protein
Family #1
Protein
Family #2
Protein Family Search
with Graph Alignment
GCCCATATGGTTAAGCTT
CCCT
TGCT
GCTA
CCTA
GCTT
ATGC
AAGC
CCCT
GCTT
GCCCTTATGCTTAAGCTA
Error Correction with Probabilistic Graphs
GCCC-TATGGTTAAGCTT
GCCCATATGATTAAGCTT
GCCCATATGGTTAAGCTT
GCCCATATGGTTAAGCTT
GCCCGTATGGTT--GCTT
GCCCATATGCTTAAGCTT
GCCC---TGGTTAAGCT-
GCCCATATCCTTAAGCTT
Multiple Sequence Alignment

## Slide 88: A Common Graph Structure in Genomics
A
C
T
T
D
I
I
I
I
D
D
A: 0.1
T: 0.2
G: 0.6
C: 0.1
A: 0.9
T: 0.1
G: 0.0
C: 0.0
A: 0.1
T: 0.1
G: 0.1
C: 0.7
A: 0.2
T: 0.2
G: 0.2
C: 0.4
0.2
0.4
0.7
0.6
0.3
0.1
Profile Hidden Markov Models (PHMMs): A probabilistic graph structure

## Slide 89: Underlying ML Technique in Genomic Graphs
Forward Calculations
Backward Calculations
Updating Transition Probabilities
Updating Emission Probabilities

## Slide 90: Underlying ML Technique in Genomic Graphs
Forward Calculations
Backward Calculations
Function 1
Function 1
Function 2
Function 2
Function 3
Function 4
Updating Transition Probabilities
Updating Emission Probabilities

## Slide 91: Costly Use of ML in Genomic Graphs
45.76%
51.44%
98.57%
Cost of Using Machine Learning (ML) in pHMMs:

## Slide 92: Goal
Enable rapid and power-efficient use of the underlying ML technique in genome graphs

## Slide 93: Key Approach: HW-SW Co-Design
SW
HW
Reduce redundant data storage by utilizing the fixed data pattern
Reduce unnecessary computations with quick filtering
Avoid repeated operations by utilizing lookup tables
Reduce data movement by processing data where it makes sense
Flexible and efficient hardware design

## Slide 94: HW: Simple Data Pattern in DP Calculations
A
T
G
T
Simple Pattern
A
D
I
D
C
I
D
T
I
Store and access data where it makes sense
Many Different Patterns
Dynamic Programming (DP) Operations:
DP Operations in pHMMs:
Frequent off-chip access
DP Computation in pHMMs
Fast On-chip Memory Access
MUL
ADD
FP DIV
MUL

## Slide 95: SW: Reducing Unnecessary Computations
A
T
G
T
Dense DP Calculations
A
D
I
D
C
I
D
T
I
Sparse (Filtered) DP Calculations
A
D
I
D
C
I
D
T
I
A
T
G
T
Filter by sorting
Observation: Calculating the entire DP is not needed
Challenge: Sorting is costly in hardware

## Slide 96: SW: Reducing Unnecessary Computations
Histogram Filter
.
.
.
8, 9
10, 14
15, 16, 18
11, 20, 21, …
13, 17, 19, …
State IDs
Range
1.00 – 0.94
0.94 – 0.88
0.88 – 0.82
0.82 – 0.76
0.76 – 0.70
0.06 – 0.00
.
.
.
Software co-design: Replace sorting with a cheaper filtering

## Slide 97: Putting the Optimizations Together
Effectively implementing the hardware and software optimizations to improve performance and reduce power requirements

## Slide 98: Integrating ApHMM in a Complete System
The specialized task can be offloaded to an accelerator whenever needed

## Slide 99: Key Results: Performance
Specialized design enables computation up to two orders of magnitude faster:
Better data flow with reduced latency and improved parallelism
Chart: Speedup Over CPU (1 Thread)
| Algorithm Acceleration
CPU (32 Threads) | 23.0925
GPU | 74.9956
ApHMM | 260.0273

## Slide 100: Key Results: Energy Consumption
…and a significant reduction in energy consumption by up to three orders of magnitude: simpler hardware with a minimized off-chip memory accesses and data movement
Chart: Energy Reduction Over CPU
| Algorithm Acceleration
CPU | 1
GPU | 1.4528
ApHMM | 2474.0912